## Slide 1: CSC 112: Computer Operating Systems Lecture 3 Scheduling
Department of Computer Science,
Hofstra University
Acknowledgement: Lecture slides based on UC Berkeley CS 162: Operating Systems and System Programming

## Slide 2: Overview
Metrics to evaluate scheduling algorithms
Goals of Scheduling algorithms
Different scheduling algorithms,
  First in first out (FIFO)
  Shortest job first (SFJ)
  Shortest time-to-complete first (SCTF)
  Round-robin (RR)

## Slide 3: Scheduling
Scheduling is an important problem in many contexts, e.g., logistics, airports, game schedule, etc.
Scheduling: policies that OS employs to determine the execution order of ready processes
Scheduling algorithms/schedulers have diverse objectives and demonstrate different effects on the system performance

## Slide 4: Terminologies
Scheduling metrics and goals:
  CPU utilization: percentage of time CPU is busy executing jobs
  Throughput: the number of processes completed in a given amount of time
  Turnaround time: the time elapses between the arrival and competition of a process
  Waiting time：the time a process spends in the ready queue
  Response Time：the time elapses between the process’ arrival and its first output
Maximize: CPU utilization, throughput
Minimize: Turnaround Time, waiting time, and response time

## Slide 5: Workload Assumptions
Each job runs for the same amount of time
All jobs arrive at the same time
All jobs only use the CPU (no I/O)
Run-time of each job is known
Once started, each job runs to completion (non-preemption)

## Slide 6: First In First Out (FIFO)
A simple and basic scheduling algorithm, also called First Come First Served (FCFS)
Jobs are executed in arrival time order
A first, B slightly later, and then C
Job | Arrival time (ms) | Run time (ms)
A | 0 | 10
B | 0 | 10
C | 0 | 10
A
B
C
Time
0
10
20
30
Gantt Chart

## Slide 7: First In First Out (FIFO)
A: 10-0 = 10
B: 20-0 = 20
C: 30-0 = 30
Average turnaround time = (10 + 20 + 30) / 3 = 20
Job | Arrival time (ms) | Run time (ms) | Finishing time (ms)
A | 0 | 10 | 10
B | 0+ | 10 | 20
C | 0++ | 10 | 30

## Slide 8: First In First Out (FIFO)
Average turnaround time = (70 + 80 + 90) / 3 = 80
Each job runs for the same amount of time
Job | Arrival time (ms) | Run time (ms) | Finishing time (ms)
A | 0 | 10 -> 70 | 70
B | 0+ | 10 | 80
C | 0++ | 10 | 90
A
B
C
Time
0
70
80
90
Gantt Chart

## Slide 9: First In First Out (FIFO)
Convoy effect
  A number of jobs queued up behind one long job to finish execution, causing overall device and CPU utilization to be suboptimal.
Long job
Short job
Short job

## Slide 10: Shortest Job First (SJF)
How to minimize average turnaround time? Run short jobs before long ones.
SJF: jobs with the shortest execution time is scheduled first
  Analogy: at supermarket checkout, Let people with few items jump the queue to cut in front of people with many items. It is not fair for each person, but more efficient from the supermarket (OS) perspective
Average Turnaround time = (10 + 20 + 90) / 3 = 40 (vs. 80 for FIFO)
A
B
C
Time
0
10
20
90
Job | Arrival time (ms) | Run time (ms) | Finishing time (ms)
A | 0 | 70 | 90
B | 0 | 10 | 10
C | 0 | 10 | 20
 | Average Turnaround | Average Turnaround | 40

## Slide 11: Shortest Job First (SJF)
SJF is an optimal scheduling algorithm in terms of average waiting time given these assumptions:
  All jobs arrive at the same time
  All jobs only use the CPU (no I/O)
  Run-time of each job is known
  Once started, each job runs to completion (non-preemption)

## Slide 12: Shortest Job First (SJF)
SJF is no longer optimal if not all jobs arrive at the same time:
All jobs arrive at the same time
A
B
C
Time
0
70
80
90
B and C are ready here, but cannot be scheduled due to non-preemption
Job | Arrival time (ms) | Run time (ms) | Finishing time (ms)
A | 0 | 70 | 70
B | 10 | 10 | 80
C | 20 | 10 | 90
 | Average Turnaround | Average Turnaround | (70+70+70)/3 = 70
Notes: Moving a short process before a long one decreases the waiting time of the short process more than it increases the waiting time of the long process.
All jobs only use the CPU (no I/O)
Run-time of each job is known
Once started, each job runs to completion (non-preemption)

## Slide 13: Shortest Time-to-Complete First (STCF)
This assumption indicates the concept of non-preemption
FIFO and SJF are both non-preemptive schedulers
STCF policy: Always switch to jobs with the shortest completion time
STCF is a preemptive scheduler
STFC is optimal in terms of minimizing the average waiting time, if the assumptions hold.
Once started, each job runs to completion

## Slide 14: Shortest Time-to-Complete First (STCF)
Job | Arrival time (ms) | Run time (ms) | Finishing time (ms)
A | 0 | 70 | 90
B | 10 | 10 | 20
C | 20 | 10 | 30
 | Average Turnaround | Average Turnaround | (90+20+30)/3 = 46.7 (70)
A
B
C
Time
0
10
20
90
A
30
STCF may cause starvation
How about other metric?

## Slide 15: Response Time
Response time refers to the time between a process's arrival in the ready queue and its first execution on the CPU. This metric is crucial for evaluating the responsiveness of the system, especially for interactive applications
FIFO
  R = (0 + 30 + 50) / 3 = 26.7
SJF
  R = (0 + 10 + 30) / 3 = 13.3
A better scheduler for response time? Round-Robin (RR)
Job | Arrival time (ms) | Run time (ms)
A | 0 | 30
B | 0+ | 20
C | 0++ | 10

## Slide 16: Round-Robin (RR)
Concept of time quantum/time slice/scheduling quantum: a fixed and small amount of time units
Each process executes for a time slice
Switches to another one regardless whether it has completed its execution or not
If the job has not yet completed its execution, the incomplete job is added to the tail of the ready queue, FIFO queue.
Notes: Alternate ready processes every fixed-length time-slice, you have a circular queue

## Slide 17: Round-Robin (RR)
Assume that time slice is 5
Job | Arrival time (ms) | Run time (ms)
A | 0 | 30
B | 0+ | 20
C | 0++ | 10
A
B
C
Time
0
60
A
A
B
C
A
B
A
B
A
  R = (0 + 5 + 10) / 3 = 5
Notes: Alternate ready processes every fixed-length time-slice, you have a circular queue

## Slide 18: Round-Robin (RR)
RR
  R = (0 + 1 + 2) / 3 = 1
RR is a good scheduler in terms of short response time
But poor in terms of turnaround time
  FIFO: T = (5 + 10 + 15) / 3 = 10
  SJF: T = (5 + 10 + 15) / 3 = 10 (same as FIFO since each job has the same run-time)
  RR: T = (13 + 14 + 15) / 3 = 14
Job | Arrival time (ms) | Run time (ms) | Time quantum
A | 0 | 5 | 1
B | 0 | 5 | 
C | 0 | 5 | 

## Slide 19: Round-Robin (RR)
If there are n processes in the ready queue and the time quantum is q, no process waits more than (n-1)q time units
The selection of time quantum size should be carefully considered (usually 10-100 milliseconds)
  Switching between processes incurs some overhead, i.e., context-switch time
  Turnaround time depends on the size of time quantum
Notes: Use a timer to implement this

## Slide 20: Round-Robin (RR)
RR is a starvation-free scheduler
  STCF may cause starvation: some processes may never get scheduled, e.g., processes with long execution times
RR is fair, simple, and easy to implement and thus is used in modern OSs, such as Linux, Windows, and MacOS.
Notes: when they shut down the IBM 7094 at MIT in 1973, they found a low-priority process that had been submitted in 1967 and had not yet been run.

## Slide 21: Summary
There are different metrics to evaluate the performance of scheduling algorithms.
FIFO is a simple scheduler, but suffers from the convoy effect
SJF is an optimal scheduling algorithm in terms of minimizing average waiting time, if all jobs start simultaneously and know their execution times in prior
STCF is an optimal scheduling algorithm in terms of minimizing average turnaround time, if all jobs know their execution times in prior
RR is a better algorithm in terms of minimizing average response time

## Slide 22: Incorporating I/O
Every program uses I/O
Process execution consists of
  CPU execution (CPU burst)
  I/O wait (I/O burst)
A
I/O
CPU
A
A
B
A
A
All jobs only use the CPU (no I/O)
Notes: CPU burst
I/O burst
process execution consists of a cycle of CPU execution and I/O wait

## Slide 23: Incorporating I/O
Treating each CPU burst as a sub-job
  Schedule a CPU burst
  Initialize the subsequent I/O burst, when the CPU burst completes
  Switch to another process
A
I/O
CPU
A
A
B
A
A
A
I/O
CPU
A
A
B
A
A
B
B
Overlap
Run-time of each job is known

## Slide 24: Priority-Based Scheduling
A priority level (integer) is assigned to each process
  Larger number indicates higher priority (typically)
  FIFO, SJF, STCF are special priority-based scheduling algorithms
The process with the highest priority is always scheduled
Priority-Based Scheduling:
  Preemptive or non-preemptive
Different priority assignment methods
  Internal or external
Priority-based scheduling may suffer from starvation (solution: aging)
Run-time of each job is known
Notes: Internal: timing constraints, memory requirements, the ratio of average I/O burst to average CPU burst
External: Importance of the process, financial considerations, hierarchy among users

## Slide 25: Multi-Level Feedback Queue (MLFQ)
SJF and STCF are good for turnaround time, but poor for response time
In contrast, RR are good for response time, but terrible for turnaround time
We need a scheduling algorithm that
  Optimizes turnaround time for batch programs
  Minimizes response time for interactive programs
Multi-level Feedback Queue (MLFQ) combines
  Priority-based scheduling
  RR

## Slide 26: Multi-Level Feedback Queue (MLFQ)
MLFQ maintains a number of queues (multi-level queue)
  Each queue has a different priority level
  Jobs which are on the same queue have same priority
Jobs are assigned to a queue
A
B
C
High priority
Low priority
Rule 1: If priority(A) > Priority(B), A runs
  A&B are scheduled before C
Rule 2: If priority(A) == Priority(B), A & B run with RR

## Slide 27: Multi-Level Feedback Queue (MLFQ)
MLFQ varies the priority of a job instead of having a fixed priority
MLFQ varies the priority of a job based on its observed behavior
  Rule 3: When a job enters the system, it is placed at the highest priority
  Rule 4a: If a job uses up an entire time slice while running, its priority is reduced (i.e., it moves down on queue).
  Rule 4b: If a job gives up the CPU before the time slice is up, it stays at the same priority level

## Slide 28: Multi-Level Feedback Queue (MLFQ)
Rule 3 and 4a (starts at the highest, and lower if not finished)
A long running job; Time slice is 10ms
0
50
100
150
200
Q2
Q1
Q0
Time (ms)
High priority
Low priority
Lower priority

## Slide 29: Multi-Level Feedback Queue (MLFQ)
Job A: A long-running CPU-intensive job
Job B: A short-running interactive job (20ms runtime), arrives at 100ms
Time (ms)
High priority
Low priority
Lower priority
A
B
Preemption

## Slide 30: Multi-Level Feedback Queue (MLFQ)
Rule 4b (stays at the same priority);
Job A: A long-running CPU-intensive job
Job B: An interactive job that only needs CPU for 5ms before I/O
Time (ms)
High priority
Low priority
Lower priority
A
B
Q0
Q1
Q2
Remain at the same priority
Notes: Take I/O into account

## Slide 31: Multi-Level Feedback Queue (MLFQ)
What are the problems of the current MLFQ?
  Starvation
  Processes may “game the scheduler” to get more resource share
  Changed behavior over time
High priority
Low priority
Lower priority
A
B
Q0
Q1
Q2
Remain at the same priority

## Slide 32: Multi-Level Feedback Queue (MLFQ)
Starvation
High priority
Low priority
Lower priority
A
C
Q0
Q1
Q2
Interactive jobs always occupy the CPU
B
Long-running job starves

## Slide 33: Multi-Level Feedback Queue (MLFQ)
Rule 5: After some time period S, move all the jobs in the system to the topmost queue.
High priority
Low priority
A
C
Q0
Q1
Q2
B
Priority boost
Helpful for changed behavior
Lower priority

## Slide 34: Multi-Level Feedback Queue (MLFQ)
Rule 4a: If a job uses up an entire time slice while running, its priority is reduced (i.e., it moves down on queue).
Rule 4b: If a job gives up the CPU before the time slice is up, it stays at the same priority level
Rule 4: Once a job uses up its time allotment at a given level (regardless of how many times it has given up the CPU), its priority is reduced(i.e., it moves down one queue).

## Slide 35: Multi-Level Feedback Queue (MLFQ)
High priority
Low priority
Lower priority
A
Q0
Q1
Q2
B
Used up its time allotment

## Slide 36: Multi-Level Feedback Queue (MLFQ)
The refined set of MLFQ rules:
  Rule 1: If Priority(A) > Priority(B), A runs (B doesn’t).
  Rule 2: If Priority(A) = Priority(B), A & B run in RR.
  Rule 3: When a job enters the system, it is placed at the highest priority.
  Rule 4: Once a job uses up its time allotment at a given level (regardless of how many times it has given up the CPU), its priority is reduced(i.e., it moves down on queue).
  Rule 5: After some time period S, move all the jobs in the system to the topmost queue.
Benefit of MLFQ
  It does not require prior knowledge on the CPU usage of a process.

## Slide 37: Multi-Level Feedback Queue (MLFQ)
MLFQ scheduler is defined by the following parameters
  Number of queues
  Time quantum of each queue
  How often should priority be boosted?
  Scheduling algorithms for each queue
  etc.
High priority queue:
  Interactive processes
  Response time
Low priority queue:
  Batch processes (CPU-intensive)
  Turnaround time

## Slide 38: Proportional Share Scheduling
Fair-share scheduler
  Guarantee that each job obtain a certain percentage of CPU time.
  Not optimized for turnaround or response time
Lottery scheduling
  Based on the concept of tickets
    The percentage of tickets denotes the share of a resource for a process
  There are two processes, A and B.
    Process A has 75 tickets  receive 75% of the CPU
    Process B has 25 tickets  receive 25% of the CPU

## Slide 39: Proportional Share Scheduling
A probabilistic way to implement lottery scheduling
  Time slice (like in RR)
  Scheduler knows how many tickets exist
  Scheduler picks a winning tickets from the ticket pool for each time slice
Example
  There are 100 tickets
    Process A has 75 tickets: 0 ~ 74
    Process B has 25 tickets: 75 ~ 99
Scheduler’s winning tickets:
63 85 70 39 76 17 29 41 36 39 10 99 68 83 63
Resulting scheduler:
A
B
A
A
B
B
B
A
A
A
A
A
A
A
A
A ≈ 74%
B ≈ 26%
Notes: The longer these two jobs compete,
The more likely they are to achieve the desired percentages.

## Slide 40: Completely Fair Scheduling (CFS)
Completely Fair Scheduling (CFS)
  Choose the process with lowest execution time: vruntime.
  Run the process for a time slice.
  The current CPU scheduler in Linux (since 2.6.23, 2007)
  Non-fixed time slice.
    CFS assigns process`s time slice a proportion of the processor.
  Priority
    Enables control over priority by using nice value.
  Efficient data structure.
    Use red-black tree for efficient search, insertion and deletion of a process.
Notes: Current linux kernel 6.1.1
17,900 lines of code

## Slide 41: Completely Fair Scheduling (CFS)
Virtual runtime (vruntime)
  Denotes how long the process has been executing.
  Per-process variable
  Increases in proportion with physical (real) time when it runs.
  CFS will pick the process with the lowest vruntime to run next.
sched_latency
  Used to determine how long a process should run before considering a switch.
  A typical value is 48 (milliseconds)
  process`s time slice = sched_latency / (the number of process)
    N = 4, time slice = 12msec
    N = 2, time slice = 24 msec
    What if N = infinite, set the
    minimum time slice value to 6 ms.

## Slide 42: Completely Fair Scheduling (CFS)
CFS deploys a red-black tree
  Balanced binary search tree
  Ordered by vruntime as key
  Complexity:
    insertion, deletion, update -> O(logN)
    find min -> O(1)

## Slide 43: Completely Fair Scheduling (CFS)
How does CFS deal with I/O and sleep
  When a process issues an I/O, it turns into sleep state. Then it will not accumulate vruntime
  As soon as the long-sleep process is waked up, it has a small vruntime, i.e., a high priority. As a result, it is likely to monopolize CPU for a long while.
  Solution: Set the vruntime of a wake-up process to the minimum value found in the RB-tree
How CFS boosts interactivity:
  I/O-bound (Interactive) processes typically have shorter CPU bursts and thus will have a low vruntime – higher priority