## Slide 1: CSC 112: Computer Operating Systems Lecture 6 Real-Time Scheduling II
Department of Computer Science,
Hofstra University
Acknowledgement: Lecture slides based on Buttazzo, Hard Real-Time Computing Systems

## Slide 2: Outline
Part I
  Introduction to RTOS and Real-Time Scheduling
  Fixed-Priority Scheduling
  Earliest Deadline First Scheduling
  Least Laxity First (LLF) Scheduling
  Preemptive vs. Non-Preemptive Scheduling
Part II
  Multiprocessor Scheduling
  Resource Synchronization Protocols (for Fixed-Priority Scheduling)

## Slide 3
Multiprocessor Scheduling

## Slide 4: Multiprocessor models
Identical multiprocessors:
  each processor has the same computing capacity
Uniform multiprocessors:
  different processors have different computing capacities
Heterogeneous multiprocessors:
  each (task, processor) pair may have a different computing capacity
MP scheduling
  Many NP-hard problems, with few optimal results, mainly heuristic approaches
  Only sufficient schedulability tests

## Slide 5: Multiprocessor Models
Identical multiprocessors: each processor has the same speed
P1
P2
P3
Task T1
Task T2

## Slide 6: Multiprocessor Models
Uniform multiprocessors: different processors have different speeds
P1
P2
P3
Task T1
Task T2
x
x/2
x/3
y
y/2
y/3
speed = 1
speed = 2
speed = 3

## Slide 7: Multiprocessor Models
Heterogeneous multiprocessors: each (task, processor) pair may have a different relative speed, due to specialized processor architectures
x/2
x/3
x
CPU
DSP chip
Graphics co-processor
Graphics-intensive task:
Number-crunching task:
x/2
x/3
y
1.5 y
y
Task T1
Task T2

## Slide 8: Global vs partitioned scheduling
Global scheduling
  All ready jobs are kept in a common (global) queue; when selected for execution, a job can be dispatched to an arbitrary processor, even after being preempted
Partitioned scheduling
  Each task may only execute on a specific processor
CPU1
CPU2
CPU3
t1
t2
t3
t2
t1
t3
t4
t5
CPU1
CPU2
CPU3
t1
t2
t3
t1
t4
t5
t2
Global scheduling:
Single system-wide queue
Partitioned scheduling:
per-processor queues
Notes:   A task may execute on any processor
  A preempted job may resume on any processor
All ready tasks are kept in a common (global) queue
When selected for execution, a task can be dispatched to an arbitrary processor, even after being preempted
Single system-wide queue or multiple per-processor queues:

## Slide 9: Global Scheduling vs. Partitioned Scheduling
Global Scheduling
Pros:
  Runtime load-balancing across cores
    More effective utilization of processors and overload management
  Supported by most multiprocessor operating systems
    Windows, Linux, MacOS...
Cons:
  Low schedulable utilization
  Weak theoretical framework
Partitioned Scheduling
Pros:
  Mature scheduling framework
  Uniprocessor scheduling theory scheduling are applicable on each core; uniprocessor resource access protocols (PIP, PCP…) can be used
  Partitioning of tasks can be done by efficient bin-packing algorithms
Cons:
  No runtime load-balancing; surplus CPU time cannot be shared among processors
Notes:   Unused processor time can easily be reclaimed
  Easier re-scheduling (dynamic loads, selective shutdown, etc.)
  Number of preemptions
  Weak theoretical framework
  Migration cost: can be mitigated by proper HW (e.g., MPCore’s Direct Data Intervention)
  • Poor resource utilization for hard timing constraints
    – No more than 50% resource utilization can be guaranteed
  • Suffers from several scheduling anomalies
    – Sensitive to period adjustments
    Lower average response time

## Slide 10: Partitioned Scheduling
Scheduling problem reduces to:
Bin-packing
problem
Uniprocessor
scheduling
problem
+
NP-hard
Various heuristics algorithms
First Fit (FF)
Best Fit (BF)
Worst Fit (WF)
Next Fit (NF)
…
Well-known
EDF
U ≤ 1
t2
t1
t3
t4
t5
RM
(RTA)
...
Notes: FF, NF, BF, FFDU, BFDD, etc.
in the
strong sense
Global (work-conserving) and partitioned approaches are incomparable
Two steps:
  1. Determine a mapping of tasks to processors
  2. Perform run-time scheduling
The Earliest Deadline First (EDF) scheduling algorithm
  - provably optimal (utilization bound = 1.0) on uniprocessors
Partitioned with EDF 
  Assign tasks to the processors, such that no processor’s capacity is exceeded
  Schedule each processor using EDF

## Slide 11: Partitioned Scheduling
Bin-packing algorithms:
  The problem concerns packing objects of varying sizes in boxes (”bins”) with some optimization objective, e.g., minimizing number of used boxes (best-fit), or minimizing the maximum workload for each box (worst-fit)
Application to multiprocessor scheduling:
  Bins are represented by processors and objects by tasks
  The decision whether a processor is ”full” or not is derived from a utilization-based feasibility test.
Since optimal bin-packing is a NP-complete problem, partitioned scheduling is also NP-complete
Example: Rate-Monotonic-First-Fit (RMFF): (Dhall and Liu, 1978)
  Let the processors be indexed as 1, 2, …
  Assign the tasks to processor in the order of increasing periods (that is, RM order)
  For each task , choose the lowest previously-used processor j such that , together with all tasks that have already been assigned to processor j, can be feasibly scheduled according to the utilization-based schedulability test
  Additional processors are added if needed
Notes: Complexity of schedulability analysis for partitioned scheduling: (Leung & Whitehead, 1982)
  The problem of deciding whether a task set is schedulable on m processors with respect to partitioned scheduling is NP-complete
Consequence:
  There cannot be any pseudo-polynomial time algorithm for finding an optimal partition of a set of tasks unless P = NP.
Assumptions:
  Independent, periodic tasks
  Preemptive, uniprocessor scheduling (RM)

## Slide 12: Assumptions for Global Scheduling
Identical multiprocessors
Work-conserving:
  At each instant, the highest-priority jobs that are eligible to execute are selected for execution upon the available processors
  No processor is ever idle when the ready queue is non-empty
Preemption and Migration support
  A preempted task can resume execution on a different processor with 0 overhead, as cost of preemption/migration is integrated into task WCET
No job-level parallelism
  the same job cannot be simultaneously executed on more than one processor, i.e., we do not consider parallel programs that can run on multiple processors in parallel
Notes: The m highest priority ready jobs are always executing on m processors
Work-conserving scheduler
  No processor is ever idle when the ready queue is non-empty
  Independent tasks
  The independence assumtion can be later removed, considering blocking times and shared resource protocols.
  a processor is never left idle while an active job exists
Task execution is assumed to be ”greedy”:
  If higher-priority tasks occupy all processors, a lower-priority task cannot grab a processor until the execution of a higher priority task is complete.
Task execution is assumed to be ”greedy”:
  If higher-priority tasks occupy all processors, a lower-priority task cannot grab a processor until the execution of a higher priority task is complete.

## Slide 13: Source of Difficulty
The “no job-level parallelism” assumption leads to difficult scheduling problems
“The simple fact that a task can use only one processor even when several processors are free at the same time adds a surprising amount of difficulty to the scheduling of multiple processors” [Liu’69]
CPU1
CPU2
CPU3
Notes: The ”root of all evil” in global scheduling: (Liu, 1969)
  Few of the results obtained for a single processor generalize directly to the multiple processor case; bringing in additional processors adds a new dimension to the scheduling problem. The simple fact that a task can use only one processor even when several processors are free at the same time adds a surprising amount of difficulty to the scheduling of multiple processors.

## Slide 14: Global scheduling example
CPU1
CPU2
CPU3
Global ready queue
(ordered according to a given policy, e.g., EM/DM/EDF)
t1
t2
t3
The first m jobs in the queue are scheduled upon the m CPUs
t2
t1
t3
t4
t5
Notes: There is a global queue in which ready tasks ready are placed, according to a certain policy. When there is a free CPU the first task is removed from the queue and is scheduled. When a new task arrives with priority higher than one of the executing tasks, it preempts the executing task with lowest priority. If a task on a different CPU finishes its execution, the preempted task can “migrate” to the free CPU and continue its execution.

## Slide 15: Global scheduling example
t3
CPU1
CPU2
CPU3
t1
t2
When a job finishes its execution, the next job in the queue is scheduled on the available CPU
t2
t1
t3
t4
t5
t2
t1
t3
t4
t5
t4
Global ready queue
(ordered according to a given policy, e.g., EM/DM/EDF)

## Slide 16: Global scheduling example
CPU1
CPU2
CPU3
t1
t2
When a new higher-priority job arrives in its next period T3, it preempts the job with lowestpriority among the executing ones
t2
t1
t3
t4
t5
t4
t3
t2
t1
t3
t4
t5
t3
t3
Global ready queue
(ordered according to a given policy, e.g., EM/DM/EDF)

## Slide 17: Global scheduling example
CPU1
CPU2
CPU3
t1
t2
When another job finishes its execution, the preempted job can resume its execution. Net effect: “migrated” from
CPU3 to CPU1
t2
t1
t3
t4
t5
t4
t3
t3
t4
t3
t4
t2
t5
t3
t4
Global ready queue
(ordered according to a given policy, e.g., EM/DM/EDF)

## Slide 18: Global vs. Partitioned
Global (work-conserving) and partitioned scheduling algorithms are incomparable:
  There are tasksets that are schedulable with a global scheduler, but not with a partitioned scheduler, and vice versa.

## Slide 19: Global vs Partitioned (FP) Scheduling
A taskset schedulable with global scheduling, but not partitioned scheduling. System utilization
Global FP scheduling is schedulable with priority assignment p1>p2>p3 (or p2>p1>p3)
Partitioned scheduling is unschedulable, since assigning any two tasks to the same processor will cause that processor’s utilization to exceed 1, so the bin-packing problem has no feasible solution
A feasible execution trace under global scheduling
Task | T=D | C | Prio
T1 | 2 | 1 | H
T2 | 3 | 2 | M
T3 | 3 | 2 | L
Notes: ½+2/3+2/3=
ot feasible for partitioned scheduling, since any two tasks’ combined utilization will exceed 1.
Three tasks T1(1,2); T2(2,3); T3(2,3) with notation: (WCET, period)

## Slide 20: Global vs Partitioned (FP) Scheduling
A taskset schedulable with partitioned scheduling, but not global scheduling. System utilization , hence the two processors must be fully utilized with no possible idle intervals
Partitioned FP scheduling with RM priority assignment (p1>p2>p3>p4) is schedulable. T1, T3 assigned to Processor 1; T2, T4 assigned to Processor 2. Both processors have utilization 1.0, and harmonic task periods
Global FP scheduling with RM priority assignment p1>p2>p3>p4 is unschedulable. Compared to partitioned scheduling, the difference is at time 7, when T3 (with higher priority than T4) runs on Processor 2. This causes idle intervals on Processor 1 [10,12] and [22,24], since only one task T4 is ready during these time intervals. Since taskset on 2 processors, any idle interval will cause the taskset to be unschedulable
A feasible execution trace
under partitioned scheduling
Task | T=D | C | Prio
T1 | 6 | 4 | 4(H)
T2 | 12 | 7 | 3
T3 | 12 | 4 | 2
T4 | 24 | 10 | 1(L)
Idle
Idle
An infeasible execution trace
under global scheduling
At time 7, T3 runs on Processor 2
At time 7, T4 runs on Processor 2
Notes: 4/6+7/12+4/12+10/24=
Not feasible for partitioned scheduling, since any two tasks’ combined utilization will exceed 1.
Partitioned scheduling is feasible
  Four tasks t1=(4,6); t2=(7,12); t3=(4,12); t4=(10,24)

## Slide 21: Difficulties of Global Scheduling
Dhall’s effect
  With RM, DM and EDF, some low-utilization task sets can be unschedulable regardless of how many processors are used.
Scheduling anomalies
  Decreasing task execution time or increasing task period may cause deadline misses
Hard-to-find worst-case
  The worst-case does not always occur when a task arrives at the same time as all its higher-priority tasks
Dependence on relative priority ordering (omitted)
  Changing the relative priority ordering among higher-priority tasks may affect schedulability for a lower-priority task
Notes: A critical instant does not always occur when a task arrives at the same time as all its higher-priority tasks.

## Slide 22: Dhall’s effect
Global RM/DM/EDF can fail at very low utilization
Example: m processors, n=m+1 tasks. Tasks are light tasks, with small , ; Task is a heavy task, with large , . is some constant value
For global RM/DM/EDF, Task has lowest priority, so must run on m processors starting at time 0, causing to miss its deadline
One solution: assign higher priority to heavy tasks
  If heavy task is assigned the highest priority, then it runs from time 0 to and meets its deadline; The light tasks can run on other processors and meet their deadlines as well
T
Deadline
Miss
m light tasks
1 heavy task
Utot1
Notes: A critical instant does not always occur when a task arrives at the same time as all its higher-priority tasks.

## Slide 23: Hard-to-Find Worst-Case
For uniprocessor scheduling, the worst case occurs when all tasks are initially released at time 0 simultaneously, called the critical instant (recall Slide Response Time Analysis (RTA))
This is no longer true for multiprocessor scheduling, as the worst-case interference for a task does not always occur at time 0, when all tasks are initially released at time 0 simultaneously
  Response time for task is maximized for its 2nd job (8-4=4), which does not arrive at the same time as its higher priority tasks; not for its 1st job (3-0=3), which arrives at the same time as its higher priority tasks
Notes: Recall that knowledge about the critical instant is a fundamental property in
A critical instant does not always occur when a task arrives at the same time as all its higher-priority tasks.
at time 0 when it arrives at the same time as all its higher-priority tasks

## Slide 24: MP Scheduling Anomalies
Decrease in processor demand (decreasing task execution time or increasing task period) may cause deadline misses!
Anomaly 1
  Decrease in processor demand from higher-priority tasks can increase the interference on a lower-priority task because of change in the time when the tasks execute
Anomaly 2
  Decrease in processor demand of a task negatively affects the task itself because change in the task arrival times cause it to suffer more interference
Notes: EDF does not suffer from execution-time anomalies, but does suffer from period anomalies.

## Slide 25: Scheduling Anomaly Example 1
Task | T=D | C | Util | Prio
a | 3 | 2 | 0.67 | H
b | 4 | 2 | 0.5 | M
c | 12 | 8 | 0.67 | L
Task | T=D | C | Util | Prio
a | 4 | 2 | 0.5 | H
b | 4 | 2 | 0.5 | M
c | 12 | 8 | 0.67 | L
Interference of 2
Interference of 1
Interference of 1
Interference of 2
Interference of 2
Interference of 2
12
14
Three tasks on two processors under global scheduling
With Task a’s period , system utilization . WCRT of task c is , where is interference by higher priority tasks a and b. (Task c experiences inference when both processors are busy executing higher priority tasks a and b.) Task c is schedulable but saturated, as any increase in its WCET or interference would make it unschedulable.
With Task a’s period , system utilization is reduced. But WCRT of task c increases: where , since execution segments of tasks a and b on two processors are aligned in time, thus causing more interference to task c
0
0
Task c deadline
at 12
Task c deadline
at 12

## Slide 26: Scheduling Anomaly Example 2
Interference of 2
Interference of 1
Three tasks on two processors under global scheduling
With Task c’s period , system utilization . WCRT of task c is , where is interference by higher priority tasks a and b. Its 1st job meets its deadline at time 10. This schedule repeats in future periods, hence task c is schedulable but saturated, as any increase in its WCET or interference would make it unschedulable.
Task | T=D | C | Util | Prio
a | 4 | 2 | 0.5 | H
b | 5 | 3 | 0.6 | M
c | 10 | 7 | 0.7 | L
Task c’s 1st job’s deadline at 10
Notes: Two processors and total task utilization
Two processors and total task utilization ∑𝑈_𝑖=1.8

## Slide 27: Scheduling Anomaly Example 2
Task c’s 1st job’s deadline at 11
Interference of 2
Interference of 1
With Task c’s period , system utilization is reduced. WCRT of task c is Its 1st job has response time , where , but this is not task c’s WCRT.
Its 2nd job has response time , where . The 2nd job finishes at time 11+12=23, and misses its deadline at time 22.
Another example where the worst-case interference for task c does NOT occur at time 0, when all tasks are initially released at time 0 simultaneously
Task | T=D | C | Util | Prio
a | 4 | 2 | 0.5 | H
b | 5 | 3 | 0.6 | M
c | 11 | 7 | 0.64 | L
0
c
20
b
a
c
23
Interference of 1
Interference of 2
Interference of 2
Task c’s 2nd job’s deadline at 22
Notes: critical instant
it arrives at the same time as all its higher-priority tasks

## Slide 28
Resource Synchronization Protocols
(for Fixed-Priority Scheduling)

## Slide 29: Resource Sharing
When two tasks access shared resources (variables), mutexes (or binary semaphores) are used to protect critical sections. Each Critical Section (CS) must begin with lock(s) and end with unlock(s)
A task waiting for a shared resource is blocked on that resource. Otherwise, it proceeds by entering the critical section and holds the resource
Tasks blocked on the same resource are kept in a queue. When a running task invokes lock(s) when s is already locked, it enters the waiting state, until another task unlocks s
write
read
int x;
int y;
lock(s)
x = 3;
y = 5;
unlock(s)
lock(s)
a = x+1;
b = y+2;
c = x+y;
unlock(s)
Shared resources
(shared variables)
Notes: Some shared resources do not allow simultaneous accesses but require mutual exclusion. A piece of code executed under mutual exclusion constraints is called a critical section.
When a task leaves a critical section, the associated resource becomes free.
Examples of common resources: data structures, variables, main memory area, file, set of registers, I/O unit, … . Examples of common resources: data structures, variables, main memory area, file, set of registers, I/O unit, … .
Each shared resource Ri must be protected by a semaphore Si, and
Many shared resources do not allow simultaneous accesses but require mutual exclusion (exclusive resources). A piece of code executed under mutual exclusion constraints is called a critical section.
A task waiting for an exclusive resource is said to be blocked on that resource. Otherwise, it proceeds by entering the critical section and holds the resource. When a task leaves a critical section, the associated resource becomes free.
Waiting state caused by resource constraints:

## Slide 30: Blocking Delay
0
2
4
6
8
10
12
14
16
18
Lower Priority (LP) tasks can cause blocking delay to Higher Priority (HP) tasks due to resource sharing
  HP tasks may cause preemption delay to LP tasks, but not blocking delay
Example: Two tasks with priority ordering . They both require semaphore s (which protects the red CS)
If HP task tries to lock s that is held by LP task , is blocked until unlocks s, so experiences a blocking delay .
  Since CS is typically very short, it seems this blocking time delay . is bounded by the longest critical section in lower-priority tasks?
No, blocking delay may be unbounded!
preempts
2
blocks
preempts when exits CS
Blocking Delay (short, bounded)
priority

## Slide 31: Priority Inversion I
0
2
4
6
100
102
104
106
108
preempts
blocks
preempts
finishes
preempts when exits CS
Blocking Delay (long, unbounded)
Three tasks with priority ordering . both require semaphore s, and does not require any semaphore
t=1: LP task locks s and enters CS
t=2: HP task is released and preempts
t=3: HP task tries to lock s, but gets blocked by holding s
t=4.2: Medium Priority (MP) task is released and preempts
t=100: MP task finishes execution after running for its WCET ; resumes execution in CS
t=102: LP task unlocks s; HP task preempts and finally locks s, after experiencing a long, unbounded blocking delay , and misses its deadline
This is priority inversion, since MP task causes a long blocking delay to HP task even though they does not share any resources (semaphores)
WCET of
priority
Notes: When tasks share resources, there may be priority inversions. t=3: MP task B is invoked, but cannot start running due to HP task A running
Three tasks with priority ordering . both require semaphore s, and does not require any semaphore
Example
When tasks share resources, there may be priority inversions. t=3: MP task B is invoked, but cannot start running due to HP task A running
Three tasks 𝜏_1, 𝜏_2, 𝜏_3 with priority ordering 𝑃_1>𝑃_2>𝑃_3. 𝜏_1, 𝜏_2 both require semaphore s, and 𝜏_3 does not require any semaphore
Example

## Slide 32: Priority Inversion II
preempts
preempts
finishes
preempts when exits CS
Blocking Delay (long, unbounded)
(This scenario is more realistic and likely than previous one, as MP task may be released anytime during ’s execution after it preempts )
t=1: LP task locks s and enters CS
t=2: HP task is released and preempts
t [2, 3]: MP task is released, but cannot run since HP task is running
t=3: HP task tries to lock s, but gets blocked by holding s; MP task starts running
t=98.5: MP task finishes execution after running for its WCET ; resumes execution in the CS
t=102: LP task unlocks s; HP task preempts and finally locks s, after experiencing a long, unbounded blocking Delay
0
2
4
6
100
102
104
106
108
priority
released
Notes: When tasks share resources, there may be priority inversions. t=3: MP task B is invoked, but cannot start running due to HP task A running
Example

## Slide 33: Deadlocks
Classic deadlock scenario: Two tasks and lock two semaphores s1, s2 in opposite order (s1 protects blue CS A and s2 protects pink CS B)
  HP task enters blue CS A before pink CS B: …lock(s1)…lock(s2)… unlock(s2)…unlock(s1)…
  LP task enters pink CS B before blue CS A: …lock(s2)…lock(s1)… unlock(s1)…unlock(s2)…
  LP task runs first and locks s2
  HP task starts running and locks s1, then tries to lock s2, gets blocked by
  starts running and tries to lock s1, but holds s1. Circular waiting  deadlock
s1
s2
s2
s1
Notes:   <
  HP task enters blue CS A before pink CS B, by calling wait(s1); wait(s2); signal(s2); signal(s1)
  LP task enters pink CS B before blue CS A, by calling wait(s2); wait(s1); signal(s1); signal(s2)
  Tasks must lock semaphores in a “pyramid” fashion
    If we have two semaphores s1 and s2, then using PCP, this is a legal trace:
      lock(s1)…lock(s2)…unlock(s2)…unlock(s1)
    This is an illegal trace:
      lock(s1)…lock(s2)…unlock(s1)…unlock(s2)
  <
  HP task 𝜏_1 enters blue CS A before pink CS B, by calling wait(s1); wait(s2); signal(s2); signal(s1)
  LP task 𝜏_1 enters pink CS B before blue CS A, by calling wait(s2); wait(s1); signal(s1); signal(s2)
  Tasks must lock semaphores in a “pyramid” fashion
    If we have two semaphores s1 and s2, then using PCP, this is a legal trace:
      lock(s1)…lock(s2)…unlock(s2)…unlock(s1)
    This is an illegal trace:
      lock(s1)…lock(s2)…unlock(s1)…unlock(s2)

## Slide 34: Priority Inheritance Protocol (PIP)
0
2
4
6
8
10
12
14
16
18
runs at ’s priority
preempts
blocks
Blocking Delay (short, bounded)
preempts when exits CS
In 1997, this bug caused the Mars pathfinder to freeze up occasionally and then starts working again. Fixed by uploading a software patch enabling Priority-Inheritance Protocol (PIP)
A task in a CS increases its priority, if it is holding a lock s and blocks other higher priority tasks, by inheriting the highest priority of all higher-priority tasks blocked waiting for lock s
t=3: HP task tries to enter CS, gets blocked since LP task is in CS; inherits ’s high priority, and runs without preemption by MP task (regardless of if is released at t [2, 3] or t>3)
priority
Notes: when is blocked on , the lower-priority task currently holding inherits ’s priority
In 1997, this bug caused the Mars pathfinder to freeze up occasionally without explanation, and then starts working again
Fixed by uploading a software patch enabling Priority-Inheritance Protocol (PIP)
PIP: A task in a CS increases its priority if it is holding a lock s, and blocks other higher priority tasks, by inheriting the highest priority of all tasks blocked waiting for lock s
When a task locks a semaphore, it inherits the highest priority of all tasks blocked waiting for the semaphore
We consider two Resource Access Protocols that can prevent priority inversions and/or deadlocks.
Priority Inheritance Protocol
Priority Ceiling Protocol
When a task locks a semaphore, it inherits the highest priority of all tasks blocked waiting for the semaphore
•A task in a CS increases its priority if it blocks other higher priority tasks, by inheriting the highest priority among those tasks it blocks
Scheduling Rule: Ready jobs are scheduled on the processor preemptively in a priority-driven manner according to their current priorities. At its release time t, the current priority of every job is equal to its assigned priority. The job remains at this priority except under the condition stated in rule 3.
Allocation Rule: When a job J requests a resource R at time t,
  if R is free, R is allocated to J until J releases it, and
  if R is not free, the request is denied and J is blocked.
Priority-inheritance Rule: When the requesting job J becomes blocked, the job Jl that blocks J inherits the current priority of J. The job Jl executes at its inherited priority until it releases R (or until it inherits an even higher priority); the priority of Jl returns to its priority l(t) at the time t when it acquired the resource R.
when 𝜏_𝑖 is blocked on 𝑠_𝑘, the lower-priority task currently holding 𝑠_𝑘 inherits 𝜏_𝑖’s priority
Scheduling Rule: Ready jobs are scheduled on the processor preemptively in a priority-driven manner according to their current priorities. At its release time t, the current priority of every job is equal to its assigned priority. The job remains at this priority except under the condition stated in rule 3.
Allocation Rule: When a job J requests a resource R at time t,
  if R is free, R is allocated to J until J releases it, and
  if R is not free, the request is denied and J is blocked.
Priority-inheritance Rule: When the requesting job J becomes blocked, the job Jl that blocks J inherits the current priority of J. The job Jl executes at its inherited priority until it releases R (or until it inherits an even higher priority); the priority of Jl returns to its priority l(t) at the time t when it acquired the resource R.

## Slide 35: Blocking Time under PIP
Under PIP, task may experience two types of blocking delays:
  Direct blocking: tries to lock semaphore s that is already locked
  Push-through blocking: blocked by lower-priority task that has inherited a higher-priority (itself may not need any semaphores)
Example:
  HP task experiences direct blocking by LP task in time interval
  MP task experiences push-through blocking by LP task in time interval
PIP analogy: suppose you have checked out a book from library and planned to read it in your spare time. But you got a message from the library that some VIP, say the university president, just got in the waiting queue for the book. You should then hurry up, give the book-reading task a high priority so it is not preempted by other daily chores, finish reading it, and return it to the library quickly, so the VIP is not delayed for a long time.
Your book-reading task (critical section) initially had a low priority, but it inherits higher priority of the VIP as soon as the VIP gets blocked waiting for the book (shared resource)
LP task ’s priority is increased at time when HP task tries to lock semaphore s but is blocked by ; NOT when lock s at time

## Slide 36: PIP Pros and Cons
Pros:
  It prevents priority inversion
  It is transparent to the programmer
Cons:
  It does not prevent deadlocks and chained blocking
Deadlock still occurs under PIP
Notes: Chained blocking:
  Theorem: task can be blocked at most once by each lower priority task
  If n is the number of lower-priority tasks than , and m is the number of semaphores on which can be blocked, then
  Theorem: can be blocked at most for the duration of min(n, m) critical sections
Priority Ceiling Protocol is a more advanced protocol, which prevents deadlocks and reduces blocking time
Chained blocking:
  Theorem: task 𝜏_𝑖 can be blocked at most once by each lower priority task
  If n is the number of lower-priority tasks than 𝜏_𝑖, and m is the number of semaphores on which 𝜏_𝑖 can be blocked, then
  Theorem: 𝜏_𝑖 can be blocked at most for the duration of min(n, m) critical sections
Priority Ceiling Protocol is a more advanced protocol, which prevents deadlocks and reduces blocking time

## Slide 37: PIP Causes Chained Blocking
Chained blocking: task can be blocked at most once by each lower priority task
Theorem: Task can be blocked at most for the duration of critical sections
  is the number of tasks with priority lower than
  is the number of locks/semaphores on which can be blocked
In this example, Four tasks and three semaphores (s1 protects red CS, s2 protects yellow CS, s3 protects beige CS). Task is blocked for the duration of critical sections
B1 B2 B3
2
3
4
1
priority

## Slide 38: Priority Ceiling Protocol (PCP)
Assumptions: fixed-priority scheduling; resources required by all tasks are known a priori at design time (not required by PIP)
Priority Ceiling Protocol PCP = PIP + ceiling blocking
PIP still holds: When is blocked on , the lower-priority task currently holding inherits ’s priority
Each semaphore is assigned a ceiling, equal to maximum priority of all tasks that require it:
Task can acquire semaphore and enter CS only if
  , that is, its priority is strictly higher than the maximum ceiling of all semaphores () currently held by other tasks; otherwise it is blocked due to ceiling blocking. ( may or may not be the same as )
  Corollary: If itself is currently held by some task, then cannot lock , since , as ceiling of is at least the priority of by definition
Under PCP, a task may experience ceiling blocking, in addition to direct blocking and push-through blocking under PIP:
  tries to lock , but its priority is not strictly higher than the maximum ceiling of all semaphores () currently held by other tasks ( itself may be free)
  Ceiling blocking is “preventive blocking”, since a task may be blocked even though the semaphore it tries to lock is free. This helps to prevent potential deadlocks and chained blocking

## Slide 39: PCP Example I
Three tasks with priority ordering . both require semaphore s, and does not require any semaphore
The execution trace is the same as PIP, since PCP includes PIP as part of the protocol
0
2
4
6
8
10
12
14
16
18
runs at ’s priority
preempts
blocks
Blocking Delay (short, bounded)
preempts when exits CS
priority
Notes: when is blocked on , the lower-priority task currently holding inherits ’s priority
When τ3 is holding s, τ1 cannot lock s, since
Scheduling Rule: Ready jobs are scheduled on the processor preemptively in a priority-driven manner according to their current priorities. At its release time t, the current priority of every job is equal to its assigned priority. The job remains at this priority except under the condition stated in rule 3.
Allocation Rule: When a job J requests a resource R at time t,
  if R is free, R is allocated to J until J releases it, and
  if R is not free, the request is denied and J is blocked.
Priority-inheritance Rule: When the requesting job J becomes blocked, the job Jl that blocks J inherits the current priority of J. The job Jl executes at its inherited priority until it releases R (or until it inherits an even higher priority); the priority of Jl returns to its priority l(t) at the time t when it acquired the resource R.
when 𝜏_𝑖 is blocked on 𝑠_𝑘, the lower-priority task currently holding 𝑠_𝑘 inherits 𝜏_𝑖’s priority
Scheduling Rule: Ready jobs are scheduled on the processor preemptively in a priority-driven manner according to their current priorities. At its release time t, the current priority of every job is equal to its assigned priority. The job remains at this priority except under the condition stated in rule 3.
Allocation Rule: When a job J requests a resource R at time t,
  if R is free, R is allocated to J until J releases it, and
  if R is not free, the request is denied and J is blocked.
Priority-inheritance Rule: When the requesting job J becomes blocked, the job Jl that blocks J inherits the current priority of J. The job Jl executes at its inherited priority until it releases R (or until it inherits an even higher priority); the priority of Jl returns to its priority l(t) at the time t when it acquired the resource R.

## Slide 40: PCP Prevents Deadlocks
Under PCP, . Both semaphores s1 and s2 have ceiling equal to , since they are all required by the higher priority task .
  LP task runs first and locks s2
  HP task runs and preempts . When tries to lock s1, it is blocked since its priority does not exceed ceiling of s2, i.e.,
  will lock both s2 and s1, and exit both CSes before can lock s1 and s2. This prevents circular waiting and deadlock
Analogous to requiring a philosopher to pick up both forks in one atomic operation to prevent deadlocks
Semaphore s1 protects blue CS A and s2 protects pink CS B
Classic deadlock scenario (with or without PIP): Two tasks and lock two semaphores in opposite order:
  LP task runs first and locks s2
  HP task starts running and locks s1, then tries to lock s2, gets blocked by
  starts running and tries to lock s1, but holds s1. Circular waiting  deadlock
Notes: Let each philosopher pick up both left and right forks atomically within a critical section (L3, “Semaphore-based Solution I”)
When τ2 is holding s2 (in pink CS), when LP task is holding (in pink CS), MP task tries to lock and enter yellow CS, but it is blocked since
τ1 cannot lock s1 and enter blue CS, since Deadlock avoidance:
When τ2 is holding s2 (in pink CS), when LP task 𝜏_2 is holding 𝑠_1 (in pink CS), MP task 𝜏_2 tries to lock 𝑠_2 and enter yellow CS, but it is blocked since 𝑃_2≤𝐶(𝑠_2 )=𝑃_1
τ1 cannot lock s1 and enter blue CS, since Deadlock avoidance:

## Slide 41: PCP Prevents Chained Blocking
Three tasks and two semaphores (s1 protects red CS and s2 protects yellow CS)
. Both semaphores s1 and s2 have ceiling equal to , since they are all required by the highest priority task . At time t1, LP task is holding s1 (in red CS). When MP task tries to lock s2 and enter yellow CS, it is blocked since its priority does not exceed ceiling of s1, (ceiling blocking)
Hence must unlock s1 before can lock s2. This prevents possible chained blocking

## Slide 42: PCP Prevents Chained Blocking
Recall the example with chained blocking under PIP
Four tasks and three semaphores (s1 protects red CS, s2 protects yellow CS, s3 protects beige CS)
Under PCP: . All semaphores s1, s2, s3 have ceiling equal to , since they are all required by the highest priority task .
While is holding s1 (in the red CS), cannot lock s2, since ; and cannot lock s3, since (ceiling blocking)
Hence PCP prevents chained blocking, since task is blocked at most once by a lower-priority task (either , or , or )
B
1
2
3
4
B
2
3
4
priority
1
priority
Notes: (which protect the red, yellow and beige CS, respectively)

## Slide 43: PCP Example II
Two tasks τ1, τ2 with priority ordering (higher) and (lower) and two semaphores s1, s2. (In the figure below, a thin blue arrow indicates that a task requires a semaphore during its execution; a solid red arrow indicates that a task is currently holding the required semaphore.)
While τ1 is holding s1, τ2 cannot lock s2, since (ceiling blocking)
  In this case PCP is over-conservative, and there are no bad consequences even if we allow τ1 to hold s1 and τ2 to hold s2 simultaneously
While τ2 is holding s2, τ1 can lock s1, since
s1
C(s1)=2
τ1 (P1=2)
sem | Ceil
s1 | 2
s2 | 1
Task | Prio | sems
τ1 | 2 | s1
τ2 | 1 | s2
s2
τ2 (P2=1)
C(s2)=1

## Slide 44: PCP Example II
s1
C(s1)=2
τ1 (P1=2)
sem | Ceil
s1 | 2
s2 | 1
Task | Prio | sems
τ1 | 2 | s1
τ2 | 1 | s1, s2
s2
τ2 (P2=1)
C(s2)=1
Two tasks τ1, τ2 and two semaphores s1, s2
While τ1 is holding s1, τ2 cannot lock s2, since (ceiling blocking)
  In this case PCP is over-conservative, and there are no bad consequences even if we allow τ1 to hold s1 and τ2 to hold s2 simultaneously
While τ2 is holding s2, τ1 can lock s1, since
Notes: Ceiling blocking is “preventive blocking”, since is blocked by , even though τ2 tries to lock s1 which is free. This prevents any potential deadlocks in the future, when τ2, τ4 each holds one of s1, s2 and tries to lock the other
Ceiling blocking is “preventive blocking”, since 𝜏_2 is blocked by 𝜏_4, even though τ2 tries to lock s1 which is free. This prevents any potential deadlocks in the future, when τ2, τ4 each holds one of s1, s2 and tries to lock the other

## Slide 45: PCP Example II
Two tasks τ1, τ2 and two semaphores s1, s2
While τ1 is holding s1, τ2 cannot lock s2, since (ceiling blocking)
While τ2 is holding s2, τ1 cannot lock s1, since (ceiling blocking)
  In this case PCP is over-conservative, and there are no bad consequences even if we allow τ1 to hold s1 and τ2 to hold s2 simultaneously
s1
C(s1)=2
τ1 (P1=2)
sem | Ceil
s1 | 2
s2 | 2
Task | Prio | sems
τ1 | 2 | s1, s2
τ2 | 1 | s2
s2
τ2 (P2=1)
C(s2)=2
Notes: Ceiling blocking is “preventive blocking”, since is blocked by , even though τ2 tries to lock s1 which is free. This prevents any potential deadlocks in the future, when τ2, τ4 each holds one of s1, s2 and tries to lock the other
Ceiling blocking is “preventive blocking”, since 𝜏_2 is blocked by 𝜏_4, even though τ2 tries to lock s1 which is free. This prevents any potential deadlocks in the future, when τ2, τ4 each holds one of s1, s2 and tries to lock the other

## Slide 46: PCP Example II
Two tasks τ1, τ2 and two semaphores s1, s2
While τ1 is holding s1, τ2 cannot lock s2, since (ceiling blocking)
While τ2 is holding s2, τ1 cannot lock s1, since (ceiling blocking)
  This prevents any potential deadlocks in the future, when τ1, τ2 each holds one of s1, s2 and tries to lock the other
s1
C(s1)=2
τ1 (P1=2)
sem | Ceil
s1 | 2
s2 | 2
Task | Prio | sems
τ1 | 2 | s1, s2
τ2 | 1 | s1, s2
s2
τ2 (P2=1)
C(s2)=2
Notes: Ceiling blocking is “preventive blocking”, since is blocked by , even though τ2 tries to lock s1 which is free. This prevents any potential deadlocks in the future, when τ2, τ4 each holds one of s1, s2 and tries to lock the other
Ceiling blocking is “preventive blocking”, since 𝜏_2 is blocked by 𝜏_4, even though τ2 tries to lock s1 which is free. This prevents any potential deadlocks in the future, when τ2, τ4 each holds one of s1, s2 and tries to lock the other

## Slide 47: PCP Example II
Three tasks τ1, τ2, τ3 and two semaphores s1, s2
While τ2 is holding s2, τ1 cannot lock s1, since (ceiling blocking)
  In this case PCP is over-conservative, and there are no bad consequences even if we allow τ1 to lock s1
While τ2 is holding s2, τ3 can lock s1, since
s1
C(s1)=3
τ1 (P1=2)
sem | Ceil
s1 | 3
s2 | 3
Task | Prio | sems
τ1 | 2 | S1
τ2 | 1 | s1, s2
τ3 | 3 | s2
s2
τ2 (P2=1)
C(s2)=2
τ3 (P3=3)
Notes: Ceiling blocking is “preventive blocking”, since is blocked by , even though τ2 tries to lock s1 which is free. This prevents any potential deadlocks in the future, when τ2, τ4 each holds one of s1, s2 and tries to lock the other
Ceiling blocking is “preventive blocking”, since 𝜏_2 is blocked by 𝜏_4, even though τ2 tries to lock s1 which is free. This prevents any potential deadlocks in the future, when τ2, τ4 each holds one of s1, s2 and tries to lock the other

## Slide 48: PCP Example II
Three tasks τ1, τ2, τ3 and two semaphores s1, s2
While τ3 is holding s1, τ1 cannot lock s2, since (ceiling blocking)
While τ3 is holding s1, τ2 cannot lock s2, since (ceiling blocking)
  In this case PCP is over-conservative, and there are no bad consequences even if we allow τ1 to lock s2 and τ2 to lock s2
s1
C(s1)=3
τ1 (P1=2)
sem | Ceil
s1 | 3
s2 | 3
Task | Prio | sems
τ1 | 2 | S1
τ2 | 1 | s2
τ3 | 3 | s1, s2
s2
τ2 (P2=1)
C(s2)=3
τ3 (P3=3)
Notes: Ceiling blocking is “preventive blocking”, since is blocked by , even though τ2 tries to lock s1 which is free. This prevents any potential deadlocks in the future, when τ2, τ4 each holds one of s1, s2 and tries to lock the other
Ceiling blocking is “preventive blocking”, since 𝜏_2 is blocked by 𝜏_4, even though τ2 tries to lock s1 which is free. This prevents any potential deadlocks in the future, when τ2, τ4 each holds one of s1, s2 and tries to lock the other

## Slide 49: PCP Example II
Three tasks τ1, τ2, τ3 and two semaphores s1, s2
While τ2 is holding s2, τ1 cannot lock s1, since (ceiling blocking)
  This prevents potential chained blocking in the future, when τ1, τ2 each holds one of s1, s2 , and τ3 tries to lock both s1 and s2, and get blocked twice
While τ2 is holding s2, τ3 cannot lock s1, since (ceiling blocking)
  In this case PCP is over-conservative, and there are no bad consequences even if we allow τ3 to lock s1
s1
C(s1)=3
τ1 (P1=2)
sem | Ceil
s1 | 3
s2 | 3
Task | Prio | sems
τ1 | 2 | S1
τ2 | 1 | s2
τ3 | 3 | s1, s2
s2
τ2 (P2=1)
C(s2)=3
τ3 (P3=3)
Notes: Ceiling blocking is “preventive blocking”, since is blocked by , even though τ2 tries to lock s1 which is free. This prevents any potential deadlocks in the future, when τ2, τ4 each holds one of s1, s2 and tries to lock the other
This prevents any potential deadlocks in the future, when τ1, τ2 each holds one of s1, s2 and tries to lock the other
Ceiling blocking is “preventive blocking”, since 𝜏_2 is blocked by 𝜏_4, even though τ2 tries to lock s1 which is free. This prevents any potential deadlocks in the future, when τ2, τ4 each holds one of s1, s2 and tries to lock the other
This prevents any potential deadlocks in the future, when τ1, τ2 each holds one of s1, s2 and tries to lock the other

## Slide 50: PCP Blocking Time
Consider all lower-priority tasks (klp(i)), and the semaphores they can lock (s)
Select from those semaphores (s) with ceiling higher than or equal to
Take max length of all tasks (k)’s critical sections that lock semaphores (s)
(The blocking time is valid even for a task that does not require any semaphores/critical sections, as it may experience push-through blocking.)
Notes: . Blocking delay is MAX length of critical sections of all lower-priority tasks (vs. SUM for PIP)

## Slide 51: PCP Pros and Cons
Pros:
  It prevents priority inversion, deadlocks, and chained blocking
  Any given task is blocked at most once by a lower-priority task
Cons:
  It is not transparent to the programmer, as shared resources required by all tasks must be known a priori at design time, and programmer needs to calculate priority ceilings of all semaphores and pass them to the OS (PIP does not need this step)
 | Deadlock Prevention | Number of blockings | Programmer Transparency
PIP | No |  | Yes
PCP | Yes | 1 | No
 | Deadlock Prevention | Number of blockings | Programmer Transparency
PIP | No |  | Yes
PCP | Yes | 1 | No
  # blockings under PIP: is the number of tasks with priority lower than ; is the number of locks/semaphores on which can be blocked
Notes:   Using PCP, each task can be blocked at most once. For PCP, in addition to normal and push-through blocking:
    Ceiling blocking: τi tried to lock s, but ceilings of currently locked semaphores are higher than Pi (s may be free)
Perform schedulability analysis by including the blocking terms
Transparency:
  PIP is transparent to the programmer; PCP and SRP require the programmer to manually calculate semaphore priority ceiling values and pass them to the OS
  in order to calculate ceilings of all semaphores

## Slide 52: Schedulability Analysis under PIP and PCP
Let denote the maximum blocking time experienced by task due to shared resources
Schedulable utilization bound for RM scheduling with blocking time (sufficient condition):
  A taskset is schedulable under RM scheduling with blocking time if
  priority level i utilization
  Assumptions: task period equal to deadline (); task with smaller period is assigned higher priority (RM priority assignment)
Response Time Analysis (RTA) for RM scheduling with blocking time (necessary and sufficient condition):
  Task ‘s WCRT is computed by solving the following recursive equation to find the minimum fixed-point solution:
  is schedulable iff
Notes: Task index k is in the order of decreasing preemption level πi
1st term denotes utilization of all tasks with higher preemption level; 2nd term contains blocking time due to tasks with lower preemption level

## Slide 53: Example Taskset (without shared resources)
System utilization
  Since utilization exceeds the Utilization Bound of 0.780 of 3 tasks under RM scheduling, we cannot determine schdulability by the Utilization Bound test
RTA shows that the taskset is schedulable by computing WCRT of each task:
Task | T | D | C | Prio | R
1 | 50 | 50 | 5 | H | 5
2 | 500 | 500 | 250 | M | 280
3 | 3000 | 3000 | 1000 | L | 2500
Notes: 1000+250+1250=2500
5/50+250/500+1000/3000=

## Slide 54: Example Taskset (with shared resources under PCP) I
3 semaphores s1, s2, s3
  Task 1 requires semaphore s1, with CS length 1
  Task 2 requires semaphores s2 and s3, with CS lengths 2 and 5, respectively
  Task 3 requires semaphores s2 and s3, with CS lengths 3 and 4, respectively
Ceilings
Blocking times:
  Task 1: (Task 1 does not experience any blocking since its priority is higher than ceilings of s2 and s3: ), so it remains schedulable
  Task 2: (maximum CS length of LP Task 3 since )
    Utilization (utilization bound for 2 tasks under RM)
    Or WCRT:
  Task 3: (Task 3 is the lowest priority task, so it does not experience any blocking), so it remains schedulable
The taskset remains schedulable with shared resources under PCP
sem | Ceiling
s1 | H
s2 | M
s3 | M
Task | T | D | C | Prio | sems | CS Len | B | R
1 | 50 | 50 | 5 | H | s1 | 1 | 0 | 5
2 | 500 | 500 | 250 | M | s2, s3 | 2, 5 | 4 | 284
3 | 3000 | 3000 | 1000 | L | s2, s3 | 3, 4 | 0 | 2500
Notes:   cccc
  A: …lock(s1)…unlock(s1)…
  B: …lock(s2)…lock(s3)… unlock(s3)…unlock(s2)…
  C: …lock(s3)…lock(s2)… unlock(s2)…unlock(s3)…

## Slide 55: Example Taskset (with shared resources under PCP) II
3 semaphores s1, s2, s3
  Task 1 requires semaphores s1, s2 and s3 with CS lengths 1, 1, 1
  Task 2 requires semaphores s2 and s3, with CS lengths 2 and 5, respectively
  Task 3 requires semaphores s2 and s3, with CS lengths 3 and 4, respectively
Ceilings
Blocking times:
  Task 1: (maximum CS length of LP Tasks 2 and 3, since )
    Utilization (Utilization bound for 1 task under RM), so Task 1 remains schedulable
    Or WCRT:
    (Task 1’s CS lengths (1, 1, 1) do not matter since it is the highest priority task and does not block any other task)
  Task 2: (maximum CS length of LP Task 3, since )
  Task 3: (Task 3 is the lowest priority task, so it does not experience blocking), so it remains schedulable
    Same calculation of utilization and WCRT for Tasks 2 and 3 as before
The taskset remains schedulable with shared resources under PCP
sem | Ceiling
s1 | H
s2 | H
s3 | H
Task | T | D | C | Prio | sems | CS Len | B | R
1 | 50 | 50 | 5 | H | s1,s2,s3 | 1, 1, 1 | 5 | 10
2 | 500 | 500 | 250 | M | s2, s3 | 2, 5 | 4 | 284
3 | 3000 | 3000 | 1000 | L | s2, s3 | 3, 4 | 0 | 2500
Notes:   Cccc associated with semaphores s2 and s3
  A: …lock(s1)…unlock(s1)…
  B: …lock(s2)…lock(s3)… unlock(s3)…unlock(s2)…
  C: …lock(s3)…lock(s2)… unlock(s2)…unlock(s3)…

## Slide 56: Scheduling Anomaly w/ Resource Synchronization
Doubling processor speed causes T1 to miss its deadline
  (Yellow part denotes a critical section shared by T1 and T2)