## Slide 1
Real-Time Scheduling
Giorgio Buttazzo
Scuola Superiore Sant’Anna, Pisa E-mail: buttazzo@sssup.it
Goal
Provide some background of RT theory that you can apply for implementing RT control applications (using Shark):
Terminology and models
Basic results on periodic scheduling
Aperiodic task handling
Inter-task communication
Overload and QoS management
2
3
A computing system able to respond to events within precise timing constraints.
Real-Time System
action
Real-Time system
event
Real-Time system
RT system
t
x (t)
Environment
t
y (t+)
It is a system in which the correctness depends not only on the output values, but also on the time at which results are produced.
REAL TIME means that system time must be synchronized with the time in the environment.
4
Typical applications
automotive
multimedia systems
robotics
small embedded devices
 cell phones
 digital TV
 videogames
 intelligent toys
5
6
Implications
Timing constraints are imposed by the dynamics of the environment.
The tight interaction with the environment requires the system to react to events within precise timing constraints.
T | he operating system is responsible f | or
e | forcing such constraints on task execution | .

## Slide 2
7
Environment
S1
A1
S2 A2
A3
F1
F2
Multi-level feedback control
F3
S3
Sensing Control
8
Environment
Software Vision
computer
actuators
sensors
A/D
D/A
Thread (task)
Resource
Traditional Approach
In spite of this large application domain, most of RT applications are designed using empirical techniques:
  assembly programming
  timing through dedicated timers
  control through driver programming
  priority manipulations
The resulting SW can be very efficient, but …
9
Disadvantages
Tedious programming which heavily depends on programmer’s ability
Difficult code understanding
10
Readability 
1
efficiency
Disadvantages
Difficult software maintainability
  Complex appl.s consists of millions lines of code
  Code understanding takes more that re-writing
  But re-writing is VERY expensive and bug prone
Difficult to verify timing constraints without explicit support from the OS and the language
11
Implications
Such a way of programming RT applications is very dangerous.
It may work in most situations, but the risk of a failure is high.
When the system fails is very difficult to understand why.
12
low reliability

## Slide 3
It is not worth studying RT theory, because any timing constraint can be handled by a sufficiently fast computer.
Typical misconception
“RT system = Fast system”
Answers
Given an arbitrary computer speed, we must always guarantee that timing constraints can be met. Testing is NOT sufficient.
Increasing speed may not always work.
13
14
Increasing speed may not always work
1
2
double speed
1
2
deadline miss
15
Never use DELAY
A delay() may cause a delay longer than .
1
2
0 2 4
delay(2)
6 8 10 12 14
blocked
1
2
0 2 4 6 8 10 12 14
16
2
0
5
10
15
0 4 8 12
delay(1)
1
2
deadline miss
0 5 10 15
0
8
12
…
4
Never use DELAY
A delay in a task may also increase the response time of other tasks (example for fixed priorities):
1
17
deadline miss
0 4 8 12 15
1
2
16
16
0 4 8 12 15
2
1

delay(8)
Never use DELAY
A delay in a task may also increase the response time of other tasks (example for deadline scheduling):
18
Speed vs. Predictability
The objective of a real-time system is to guarantee the timing behavior of each individual task.
The objective of a fast system is to minimize the average response time of a task set.
But …
w
Do gu | n’t trust averag arantee individua | e l pe |  | hen you have t rformance | o

## Slide 4
Lessons learned
Tests are not enough for real-time systems
Intuitive solutions do not always work
Delay should not be used in real-time tasks
19
A safe approach:
use predictable kernel mechanisms
analyze the system to predict its behavior
Achieving predictability
The operating system is the part most responsible for a predictable behavior.
Concurrency control must be enforced by:
 appropriate scheduling algorithms
 appropriate syncronization protocols
 efficient communication mechanisms
 predictable interrupt handling
 overload management
20
Let’s review the main scheduling results
21
22
task i
release time start time
finishing time
t
ri si
fi
activation time arrival time
Terminology
Task (or thread)
is a sequence of instructions that in the absence of other activities is continuously executed by the processor until completion.
Ci computation time
23
ri,k
ri,k+1
t
i
Ci
ri,1
Tasks and jobs
A task is an infinite sequence of instances (jobs):
Job 1
i,1
Job 2
i,2
Job 3
i,3
Activation modes
Time driven: periodic tasks
the task is automatically activated by the kernel at regular intervals.
Event driven: aperiodic tasks
the task is activated upon the arrival of an event or through an explicit invocation of the activation primitive.
24

## Slide 5
25
Periodic task model
ri1 = i
ri,k+1 = ri,k + Ti
ri,k
ri,k+1
t
Ti
ri,1 = i
i (Ci , Ti , Di )
Ci
ri,k = i + (k1) Ti di,k = ri,k + Di
often
Di = Ti
26
Aperiodic task model
Aperiodic: ri,k+1 > ri,k
Sporadic: ri,k+1  ri,k + Ti
t
i
Job 1 Job 2 Job 3
Ci
ri,1 ri,k ri,k+1
27
OS support for periodic tasks
task i
while (condition) {
wait_for_next_period();
}
ready
running
idle
active active
idle
idle
28
The IDLE state
Timer
end_cycle
wake_up
IDLE
signal
wait
READY
dispatching terminate
RUNNING
preemption
activate
BLOCKED
29
SLEEP state
signal
dispatching
preemption
wait
end_cycle
wake_up
RUNNING
IDLE
BLOCKED
READY
Timer
terminate
activate
create
sleep
SLEEP
Scheduling
A scheduling algorithm is said to be:
  preemptive: if the running task can be temporarely suspended in the ready queue to execute a more important task.
  non preemptive: if the running task cannot be suspended until completion.
30

## Slide 6
Schedule
A schedule is a particular assignment of tasks to the processor.
Given a task set  = {1, …, n}, a schedule is a mapping  : R+  N such that t  R+, t1, t2 :
t  [t1, t2) e t’  [t1, t2) : (t) = (t’)
k > 0 if k is running
(t) =
0 if the processor is idle
31
(t)
3
2
1
0
t1 t2 t3 t4 t
idle
A sample schedule
idle 1 2 3
At time t1, t2, t3, e t4 a context switch is performed. Each interval [ti, ti+1) is called a time slice.
32
33
A preemptive schedule
t
1
2
3
(t)
3
2
1
0
Definitions
A schedule  is said to be feasible if all the tasks are able to complete within a set of constraints.
A set of tasks  is said to be schedulable if there exists a feasible schedule for it.
34
Types of constraints
Timing constraints
  activation, completion, jitter.
Precedence constraints
  they impose an ordering in the execution.
Resource constraints
  they enforce a synchronization in the access of mutually exclusive resources.
35
36
Precedence graph
acq1
acq2
edge1
edge2
shape
disp
depth
rec

## Slide 7
37
Resource constraints
To preserve data consistency, shared resources must be accessed in mutual exclusion:
x = 3
y = 5
W
R
x = 1
y = 8

W
R
x=1
x = 1
y = 5
y=8
read
38
Mutual exclusion
However, mutual exclusion introduces extra delays:
x = 3
y = 5
x = 1
y = 8
x = 1
y = 8
W
R
W
R

x = 1 y = 8
read
Timing constraints
Can be explicit or implicit.
Explicit constraints
  Are included in the specification of the system activities.
Examples
  open the valve in 10 seconds
  send the position within 40 ms
  read the altimeter every 200 ms
39
40
t

i
Real-Time tasks
Di Ci
ri si fi di
ri release time (arrival time ai )
si start time
Ci worst-case execution time (wcet)
di absolute deadline Di relative deadline fi finishing time
41
Other parameters
di
t

i
ci(t)
fi
Li = fi  di max(0, Li)
ri si
Lateness: Tardiness: Residual wcet:
ci(t) ci(ri) = Ci
Laxity (o slack): di  t  ci(t)
t
slack
42
Jitter
It is the time variation of a periodic event:
Finishing-time Jitter
i
fi,1 fi,2 fi,3
Absolute: max (fi,k – ri,k) – min (fi,k – ri,k)
k k
Relative:
max | (fi,k – ri,k) – (fi,k-1 – ri,k-1) |
k

## Slide 8
Other types of Jitter
Start-time Jitter
i
si,1 si,2 si,3
Completion-time Jitter (I/O jitter)
i
si,1 fi,1 si,2 fi,2 si,3 fi,3
43
44
SOFT tasks
Missing deadlines is not desired but causes only a performace degradation.
Task Criticality
HARD tasks
All jobs must meet their deadlines. Missing a deadline may cause catastrophical effects.
An t | operating system asks is called a hard |  | able to handle hard real-time system. | 
Typical HARD tasks
sensory acquisition
low-level control
sensory-motor planning
Typical SOFT tasks
reading data from the keyboard
user command interpretation
message displaying
graphical activities
45
46
t0
?
Implicit constraints
– do not appear in the system specification, but must be respected to meet the requirements.
Example
What’s the time validity of a sensory data?
47
Example: automatic breaking
obstacle
v
Dashboard Controls
BRAKES
human
Distribution Unit
condition checker
sensors
emergency stop
sensor visibility D
48
acq. task
obstacle in obstacle the field detected
brake pressed
train stopped
Ts  Tb
v
Worst-case reasoning
Ts

## Slide 9
49
D = sensor visibility
v(Ts + ) + Xb < D
a =  g
Xb 
v2
2g
2
b
X  vt  1 at 2
v = a t
v(Ts  )  2g  D
v2
50
 
v
T  D 
s
v 2g
speed
Tmax
vmax
v
Ts
v  (g)2  2Dg  g
max
2Dg
vmax 
Esempio2: contour following
v
F
Goal
Move at velocity v along the surface tangent, exerting a force F < Fmax along its normal direction.
51
Ts
Ts
force not detected
trajectory modified
robot stopped
52
acq. task
v
Worst-case reasoning
v
F(t-1)
F(t)
F(t+1)
d
v = v0 e–(t/d)
53
Lenght covered by the robot after the contact:
L = vTs + xf
f
d
0 0 d 0 d
x  v(t)dt  v e dt  v  (e  e )  v 

t /  0

0
0
L = v(Ts + d)
F = KL = v(Ts + d) < Fmax
Force on the robot tool: (K = elastic coefficient)
54
Condition on the sampling period:
d
s
Kv
T 
0
Fmax 
speed
T
max
vmax
v0
Ts

d 

 | Tmax v |   Fmax   Kv0  Fmax | 
 | max | K | d

## Slide 10
55
The general scheduling problem
Given a set  of n tasks, a set P of m processors, and a set R of r resources, find an assignment of P and R to  which produces a feasible schedule.
Scheduling algorithm
 P R

feasible
Complexity
In 1975, Garey and Johnson showed that the general scheduling problem is NP hard.
However, polynomial time algorithms can be found under particular conditions.
56
Complexity
It’s important to find polynomial time algorithms.
number of tasks n = 30
elementary step = 1s
Alg. 1: O(n) 30 s
Alg. 2: O(n6) 12 min
Alg. 3: O(6n) 7 billions of years
57
Simplifying assumptions
Single processor
Omogeneous task sets
Fully preemptive tasks
Simultanoeus activations
No precedence constraints
No resource constraints
58
Periodic Task Scheduling
60
Problem formulation
i (Ci, Ti) job ik
rik dik
For each periodic task, guarantee that:
each job ik is activated at rik = (k1)Ti
each job ik completes within dik = rik + Di

## Slide 11
Timeline Scheduling (cyclic scheduling)
It has been used for 30 years in military systems, navigation, and monitoring systems.
Examples
Air traffic control
Space Shuttle
Boeing 777
61
Timeline Scheduling
Method
The time axis is divided in intervals of equal length (time slots).
Each task is statically allocated in a slot in order to meet the desired request rate.
The execution in each slot is activated by a timer.
62
63
Example
T
task f
A |  | 40 Hz | 25 ms
 | B | 20 Hz | 50 ms
C |  | 10 Hz | 100 ms
 = GCD (minor cycle)
T = lcm (major cycle)
T
0
25
50
75
100
125
150
175 200

CA + CC  
Guarantee: CA + CB  
64
A B
A C
A B
A
Implementation
timer
timer
timer
timer
minor cycle
major cycle
Timeline scheduling
Advantages
Simple implementation (no real-time operating system is required).
Low run-time overhead.
It allows jitter control.
65
Timeline scheduling
Disadvantages
It is not robust during overloads.
It is difficult to expand the schedule.
It is not easy to handle aperiodic activities.
66

## Slide 12
Problems during overloads
What do we do during task overruns?
Let the task continue
  we can have a domino effect on all the other tasks (timeline break)
Abort the task
  the system can remain in inconsistent states.
67
68
Expandibility
If one or more tasks need to be upgraded, we may have to re-design the whole schedule again.
Example: B is updated but CA + CB > 

A B
0 25
Expandibility
We have to split task B in two subtasks (B1, B2) and re-build the schedule:
A B1 A B2 C A B1 A B2
• • •
0 25 50 75 100
69
CA + CB2 + CC  
Guarantee: CA + CB1  
70
Expandibility
If the frequency of some task is changed, the impact can be even more significant:
task T T
A |  | 25 ms | 25 ms
B |  | 50 ms | 40 ms
 | C | 100 ms | 100 ms
before
 = 25
after
 = 5
T = 200
minor cycle:
major cycle: T = 100
40 sync. per cycle!
71
Example
T
0

0
25 50 75 100 125 150 175 200

25 50 75 100 125 150 175 200
T
Priority Scheduling
Method
Each task is assigned a priority based on its timing constraints.
We verify the feasibility of the schedule using analytical techniques.
Tasks are executed on a priority-based kernel.
72

## Slide 13
73
Priority Assignments
Rate Monotonic (RM): pi  1/Ti (static)
Earliest Deadline First (EDF):
pi  1/di (dynamic)
ri,k+1
t
Ti
i (Ci , Ti , Di )
Ci
ri,1 = 0 ri,k
di,k = ri,k + Di
Di = Ti
74
Rate Monotonic (RM)
Each task is assigned a fixed priority proportional to its rate.
A
0 25 50 75 100
B
0
C
0 40
80
100
75
How can we verify feasibility?
Each task uses the processor for a fraction of time:
C
Ui  i
Ti
Hence the total processor utilization is:
p 
T
n Ci
U 
i1 i
Up is a misure of the processor load
If Up > 1 the processor is overloaded hence the task set cannot be schedulable.
A necessary condition
However, there are cases in which Up < 1
but the task is not schedulable by RM.
76
77
An unfeasible RM schedule
0
6
0
3
3
6
9 12 15 18
9 12 15 18
deadline miss
1
2
6 9
p
U  3  4  0.944
78
Utilization upper bound
6 9
p
U  3  3  0.833
6
0
3
9 12 15 18
1
2
0 3 6 9 12 15 18
NOTE: If C1 or C2 is increased,
2 will miss its deadline!

## Slide 14
79
A different upper bound
4 8
p
U  2  4  1
4
12
0
8
16
1
2
0 4 8 12 16
The upper bound Uub depends on the specific task set.
The least upper bound
Uub
1
Ulub
. . .

80
A sufficient condition
81
If Up  Ulub the task set is certainly schedulable with the RM algorithm.
NOTE
If Ulub < Up  1 we cannot say anything about the feasibility of that task set.
82

n21 n 1
i1 Ti
Ci 
under RM if
under EDF if and only if

i  1
i1 Ti
n C
Basic results
Assumptions:
In 1973, Liu & Layland proved that a set of n
periodic tasks can be feasibly scheduled
n
Independent tasks
Di = Ti
i = 0
lub
 n21/ n 1
U RM
RM bound for large n
for n  Ulub  ln 2
83
1 2 3 4 5 6 7 8 9 10
69%
n
84
CPU%
100
90
80
70
60
50
40
30
20
10
0
Schedulability bound
RM EDF

## Slide 15
85
A special case
4 8
p
U  2  4  1
If tasks have harmonic periods Ulub = 1.
0
4
12
0
8
16
1
2
4
12
8
16
86
U1
1
U2
0.83 1
0.83
n
Ui  n(21/ n 1)
i1
n
Ui  1
i1
Schedulability region
The U-space
RM
EDF
87
Schedule
0
6
0
3
3
6
9 12 15 18
9 12 15 18
1
2
EDF
RM
0
6
0
3
3
6
9 12 15 18
9 12 15 18
deadline miss
1
2
RM Optimality
RM is optimal among all fixed priority algorithms:
88
If there exists a fixed priority assignment which leads to a feasible schedule for , then the RM assignment is feasible for .
If  is not schedulable by RM, then it cannot be scheduled by any fixed priority assignment.
EDF Optimality
EDF is optimal among all algorithms:
89
If there exists a feasible schedule for , then EDF will generate a feasible schedule.
If  is not schedulable by EDF, then it cannot be scheduled by any algorithm.
90
Critical Instant
For any task i, the longest response time occurs when it arrives together with all higher priority tasks.
1
2
R2
1
2
R2

## Slide 16
The Hyperbolic Bound
In 2000, Bini et al. proved that a set of n
periodic tasks is schedulable with RM if:
91
n
(Ui 1)  2
i1
92
U1
1
U2
0.83 1
0.83
n
Ui  1
i1
Schedulability region
The U-space
n
Ui  n(21/ n 1)
i1
n

i1
(Ui 1)  2
RM
EDF
93
Ci
t
i
Extension to tasks with D < T
Ti
Di
di,k ri,k+1
pi  1/Di pi  1/di
(static)
(dynamic)
ri,k
Scheduling algorithms
Deadline Monotonic:
Earliest Deadline First:
94
Deadline Monotonic
1
2
0 4 8 12 16 20 24 28
Problem with the Utilization Bound
2 3
   1.16  1
3 6
i
p 
i1 Di
n C
U 
but the task set is schedulable.
Ci
t
i
How to guarantee feasibility?
Ti
Di
ri,k di,k ri,k+1
Fixed priority: Response Time Analysis (RTA)
EDF: Processor Demand Criterion (PDC)
95
Response Time Analysis
[Audsley ‘90]
For each task i compute the interference due to higher priority tasks:
Ii  Ck
Dk  Di
compute its response time as
Ri = Ci + Ii
verify if Ri  Di
96

## Slide 17
97
Computing the interference
k
i
0 Ri
Interference of k on i
in the interval [0, Ri]:
k
k
ik
C
Ri T
I 
Interference of high priority tasks on i:
k
k
i
Ri C T
I 
i1

k 1
98
Computing the response time
k
k
i
C
Ri
T
i 
R  C 
i1
k 1
Iterative solution:
k
i
C
i
Tk
R( s1)
i1
k 1
i 
Rs  C 
R0  C
i i
iterate until
i i
Rs  R( s1)
In any interval of time, the computation demanded by the task set must be no greater than the available time.
Processor Demand Criterion
[Baruah, Howell, Rosier 1990]
t1 , t2  0, g(t1 , t2 )  (t2  t1 )
99
100
Processor Demand
di t2
g(t1 , t2 )  Ci
ri t1
t1 t2
The demand in [t1, t2] is the computation time of those jobs started at or after t1 with deadline less than or equal to t2:
101
Processor Demand
For synchronous task sets we can only analyze intervals [0,L]
L
Di
Ti + Di
2Ti + Di
3Ti + Di
0
L
i
g(0, L)
n
i
L  Di  Ti C
T i
g(0, L)  
i1
Processor Demand Test
Question
How can we bound the number of intervals in which the test has to be performed?
102
i
 L
L  Di  Ti C
Ti
n
L 0 
i 1

## Slide 18
Example
1
2
0 2 4 6 8 10 12 14 16
4
2
0
g(0, L)
8
6
L
103
L
Bounding complexity
Since g(0,L) is a step function, we can check feasibility only at deadline points.
If tasks are synchronous and Up < 1, we can check feasiblity up to the hyperperiod H:
H = lcm(T1, … , Tn)
104
105
Bounding complexity
Moreover we note that: g(0, L)  G(0, L)

i
 i 
i i
 C
T
 L  T  D 
i1
n
G(0, L)  
i
n
n
Ti
C
Ti
C
i1 i 1
  L i  (Ti  Di )
n
 LU  (Ti  Di )Ui
i 1
106
g(0, L)
L
G(0, L)
Limiting L
n
G(0, L)  LU  (Ti  Di )Ui
i1
L
L*
for L > L*
g(0,L)  G(0,L) < L
1U
n
(Ti  Di )Ui
L*  i1
107
Processor Demand Test
1U
D = {dk | dk  min (H, L* )}
H = lcm(T1, … , Tn)
n
(Ti  Di )Ui
L*  i1
n
L  D  T
 i i Ci  L
i1 Ti
U < 1 AND L 0
A set of n periodic tasks with D ≤ T is schedulable by EDF if and only if
108
Summarizing: RM vs. EDF
 | Di = Ti | Di  Ti
RM | Suff.: polynomial O(n) LL: Ui  n(21/n –1) HB: Ui+1)  2 Exact pseudo-polynomial RTA | pseudo-polynomial Response Time Analysis i Ri  Di R  C  i1 Ri C i i  T k k 1 k
EDF | polynomial: O(n) Ui  1 | pseudo-polynomial Processor Demand Analysis L  0, g(0, L)  L

## Slide 19
Questions
If EDF is more efficient than RM, why commercial RT systems are still based on RM?
Main reason
RM is simpler to implement on top of commercial (fixed priority) kernels.
EDF requires explicit kernel support for deadline scheduling, but gives other advantages.
109
Advantages of EDF
However, EDF offers the following advantages with respect to RM:
Less overhaed due to preemptions;
More flexible behavior in overload situations;
More uniform jitter control;
Better aperiodic responsiveness.
110
Runtime overhead
Two different types of overhead are considered:
Overhead for job release
 EDF has more than RM, because the absolute deadline must be updated at each job activation
Overhead for context switch
 RM has more than EDF because of the higher number of preemptions
111
2
0
7
28
35
35
RM
1
5
21
7
14
10 15 20 25 30
28
35112
35
EDF
1
0
2
0
14 21
deadline miss
Preemptions
U  2  4  0.97
5 7
0 5 10 15 20 25 30
113
Preemptions
4
6
8 10
12 14
16
18
20
30
20
10
0
60
50
40
80
70
Number of tasks
Avg. no. of preemptions
(1000 sims of 1000 units)
RM
EDF
T  [10, 100]
 = 0.9
114
Preemptions
0.55
0.6
0.65
0.8
0.85 0.9
0.95
40
30
20
10
0
50
80
70
60
0.7 0.75
Load
Avg. no. of preemptions
(1000 sims of 1000 units)
RM
EDF
T  [10, 100]
N = 10

## Slide 20
115
Example with RM
0
2
4
6
8
10 12
14 16 18 20
10
20
6
12
18
1
2
3
Under RM, preemptions increase as computation times increase
116
Example with RM
0
2
4
6
8
10 12
14 16 18 20
10
20
6
12
18
1
2
3
Under RM, preemptions increase as computation times increase
117
Example with EDF
0
2
4
6
8
10 12
14 16 18 20
10
20
6
12
18
1
2
3
Under EDF, preemptions may decrease as computation times increase
118
Example with EDF
0
2
4
6
8
10 12
14 16 18 20
10
20
6
12
18
1
2
3
Under EDF, preemptions may decrease as computation times increase
Robustness under overloads
Two situations are considered:
Permanent overload
 This occurs when U > 1
Transient overload
 This occurs when some job executes more than expected
119
2
3
0
0 20 40 60 80
12 24
36
48
60
72
84
High priority tasks execute at the proper rate
Low priority tasks are completely blocked
120
RM under permanent overload
U  4  6  5  1.25
8 12 20
1
0 8 16 24 32 40 48 56 64 72 80

## Slide 21
121
2
3
80
0
12 24
36
48
60
72
84
0 20 40 60
All tasks execute at a slower rate
No task is blocked
EDF under permanent overload
U  4  6  5  1.25
8 12 20
1
0 8 16 24 32 40 48 56 64 72 80
122
EDF is predictable in overloads
Theorem (Cervin ‘03)
If U > 1, EDF executes tasks with an average period T’i = Ti U.

1
2

3
8 10
12 15
20
25
Ti T’i
1
2



3
8 | 10
12 | 15
20 | 25
U = 1.25
We now show that this is not true
Big misconceptions
EDF is not predictable during overloads because we don’t know which tasks are going to miss their deadlines.
RM is predictable during overloads because the tasks that miss their deadlines are low priority tasks.
123
RM during transient overruns
5
15
10
20
9
25 30
0
27
20
0 2 4 6
8 10 12 14 16 18 20 22 24 26 28 30
deadline 18
miss
1 (2/5)
0
2 (3/9)
3(1/20)
0
4(1/30)
Uavg = 0.817
C1avg = 2, C1max = 4
i
Who is missing its deadline |  |  | s not t | he lowest priority task 124
Another misconception
125
RM reduces jitter during task execution more than EDF
126
Jitter under RM
0
6
18
12
24
8
18
0
0
1 (2/6)
2 (3/8)
3(2/12)
12
24
RTJ1 = 0
RTJ2 = 2
RTJ3 = 8
3 experiences a very high jitter

## Slide 22
127
Jitter under EDF
0
6
18
12
24
8
18
0
0
1 (2/6)
2 (3/8)
3(2/12)
12
24
RTJ1 = 1
RTJ2 = 2
RTJ3 = 3
For a little increase of RTJ1, RTJ3 decreases a lot
Jitter experiments
1
2
3
7
8
9
0.2
0.1
0
0.5
0.4
0.3
0.6
4 5 6
Task number
RM
EDF
10
128
Normalized Avg. RTJ
U = 0.8 N = 10
Jitter experiments
1
2
3
7
8
9
0.4
0.3
0.2
0.1
0
0.5
4 5 6
Task number
Normalized Avg. RTJ
EDF
U = 0.9 N = 10
10
129
1.0
0.9
RM
0.8
0.7
0.6
130
Another result on Jitter
Input-Output Jitter
i
si,1 fi,1 si,2
fi,2 si,3 fi,3
IOJi = max (fi,k – si,k) – min (fi,k – si,k)
Theorem (Cervin 03)
IOJiEDF  IOJiRM
131
I/O Jitter under RM
0
6
18
12
24
8
18
0
0
1 (2/6)
2 (3/8)
3(2/12)
12
24
IOJ1 = 0
IOJ2 = 2
IOJ3 = 5
All tasks except 1 experience I/O jitter
132
I/O Jitter under EDF
0
6
18
12
24
8
18
0
0
1 (2/6)
2 (3/8)
3(2/12)
12
24
RTJ1 = 0
RTJ2 = 0
RTJ3 = 0
All tasks experience no I/O Jitter

## Slide 23
Handling Aperiodic Tasks
Handling Criticality
Aperiodic tasks with HARD deadlines must be guaranteed under worst-case conditions.
Off-line guarantee is only possible if we can bound interarrival times (sporadic tasks).
Hence sporadic tasks can be guaranteed as periodic tasks with Ci = WCETi and Ti = MITi
WCET = Worst-Case Execution Time MIT = Minimum Interarrival Time
134
SOFT aperiodic tasks
Aperiodic tasks with SOFT deadlines should be executed as soon as possible, but without jeopardizing HARD tasks.
We may be interested in
 minimizing the average response time
 performing an on-line guarantee
135
136

1

2
ape
3
4
0
8
12
6
0
4
8
12
6
2
10
1
Periodic Scheduling
(EDF)
C = 1
2
C = 3
137
Immediate service
1

2
ape
3
4
0
8
12
6
0
12
2
4 6 8 10
C1 = 1
2
C = 3
deadline miss
Response Time = 3
138
Background service
1

2
ape
3
4
0
8
12
6
0
12
4 6 8
2
10
C1 = 1
2
C = 3
Response Time = 10

## Slide 24
Aperiodic Servers
A server is a kernel activity aimed at controlling the execution of aperiodic tasks.
Normally, a server is a periodic task having two parameters:
Cs capacity (or budget) Ts server period
139
To preserve periodic tasks, no more than Cs units must be executed every period Ts
Aperiodic service queue
Service queue
Server
periodic/sporadic HARD tasks
aperiodic SOFT tasks
CPU
READY queue
The server is scheduled as any periodic task.
Priority ties are broken in favor of the server.
Aperiodic tasks can be selected using an arbitrary queueing discipline.
140
Fixed-priority Servers
Polling Server
Deferrable Server
Sporadic Server
Slack Stealer
141
Dynamic-priority Servers
Dynamic Polling Server
Dynamic Sporadic Server
Total Bandwidth Server
Tunable Bandwidth Server
Constant Bandwidth Server
142
Polling Server (PS)
At the beginning of each period, the budget is recharged at its maximum value.
Budget is consumed during job execution.
When the server becomes active and there are no pending jobs, Cs is discharged to zero.
When the server becomes active and there are pending jobs, they are served until Cs > 0.
143
144
1

2
ape
2
4
0
8
12
6
0
4
8
12
6
2
10
RM + Polling Server
C1 = 2
2
C = 1
0
5
10
PS Cs = 1
Ts = 5
Response Time = 8

## Slide 25
PS properties
In the worst-case, the PS behaves as a periodic task with utilization Us = Cs/Ts .
Aperiodic tasks execute at the highest priority if Ts = min(T1, … , Tn).
Liu & Layland analysis gives that:
145


 
 1
2
1
 n
 s 
lub s
 U 1 
 U  n 
U RM  PS (n)
146
RM + PS schedulability
U
s
0
1
1
ln2
RM  PS
(n  )  U  ln 2 
s  U 1
Ulub
 s  | 
U RM  PS (n)  U  n (K1/ n  1) lub s K  2 Us 1 | 
147
Deferrable Server (DS)
Is similar to the PS, but the budget is not discharged if there are no pending requests.
Keeping the budget improves responsiveness, but decreases the utilization bound.
ape
0
4
8
12
6
2
10
0
4
8
DS Cs = 1
Ts = 4
148
1

2
ape
2
4
0
8
12
6
0
4
8
12
6
2
10
RM + Deferrable Server
C1 = 2
C2 = 1
0
5
10
DS Cs = 1
Ts = 5
Response Time = 4
1
149
Analysis of RM + DS





  1
1
lub
n 
s
s
s
 2U 1 
U  2
 U  n 
U RM  DS (n)
DS
1
Cs
C1
Ts +Cs
2Ts+Cs


2
C2
T1
Cs Cs
T2
150
RM + DS schedulability
Us
0
1
1
ln2
lub
U RM  DS (n  )
PS
DS
lub
 U  n (K 1/ n  1)
s
U RM  PS (n)
PS
2
Us 1
K 
DS
2Us 1
 Us  2
K

## Slide 26
151



Designing server parameters




 1
1
n 
 s 
s
2U 1
 U  2 
U p  n 
s
Determine U max from
s
Define Us  U max
Define Ts = min (T1, …, Tn)
Compute Cs = UsTs
Total Bandwidth Server (TBS)
It is a dynamic priority server, used along with EDF.
Each aperiodic request is assigned a deadline so that the server demand does not exceed a given bandwidth Us .
Aperiodic jobs are inserted in the ready queue and scheduled together with the HARD tasks.
152
153
The TBS mechanism
periodic/sporadic tasks
aperiodic tasks
CPU
Deadline assignment
Up + Us  1
READY queue
Deadlines ties are broken in favor of the server.
Periodic tasks are guaranteed if and only if
Deadline assignment rule
Deadline has to be assigned not to jeopardize periodic tasks.
A safe relative deadline is equal to the minimum period that can be assigned to a new periodic task with utilization Us:
Us = Ck / Tk Tk = dk  rk = Ck / Us
Hence, the absolute deadline can be set as:
154
dk = rk + Ck / Us
155
 | dk = max (rk , dk-1 | ) + Ck / Us | 
Deadline assignment rule
C1/Us C2/Us
C1 C2
r1 r2 d1 d2
To keep track of the bandwidth assigned to previous jobs, dk must be computed as:
156
Us = 1  Up = 1/4
1
2
ape
2
4
0
8
12
6
0
12
4 6
2
EDF + TBS schedule
C1 = 1
C2 = 3
1
8 d1 10
d2
r1
r2
d1 = r1 + C1 / Us = 1 + 2·4 = 9
d2 = max(r2 , d1) + C2 / Us = 9 + 1·4 = 13

## Slide 27
157
Improving TBS
What’s the minimum deadline that can be assigned to an aperiodic job?
1
2
ape
2
4
0
8
12
6
0
4
12
6
2
C1 = 1
C2 = 3
8 d1 10
r1
158
Improving TBS
If we freeze the schedule and advance d1 to 7, no task misses its deadline, but the schedule is not EDF:
1
2
ape
2
4
0
8
12
6
0
12
4 6
2
C1 = 1
C2 = 3
8 d1 10
r1
Feasible schedule  EDF
159
Improving TBS
Clearly, advancing the deadline now does not produce any enhancement:
1

2
ape
2
4
0
8
12
6
0
4
12
6
2
C1 = 1
2
C = 3
8 d1 10
r1
160
Computing the deadline
In general, the new deadline has to be set to the finishing time of the current job:
ape
d 0  max(r , d 0 )
k k k 1
k k k k
d s1  f s  f (d s )
k
d s
k
f s
161
Computing the deadline
The actual finishing time can be estimated based on the periodic interference:
ape
k k p k k
f s  C  I (r , d s )
k
d s
k
f s
I
p
Ck
162
Periodic Interference
p k a k f k
I (t, d s )  I (t, d s )  I (t, d s )
Up = 1/2  1/3 = 5/6 Us = 1  Up = 1/6
Ck = 2
dk = 3 + 2/ Us = 15
1
2
ape
2
4
0
8
6
dk
12
16
20
12
18
0
3

## Slide 28
163
Computing interference
a k  i
i
 active
I (t, d s )  c (t)



n
i
s
f k 
k i
Ti
i1 
1 C

d  next (t)
I (t, d s ) 
i
next (t) = next release time
of task i after t
dk
1
2
ape
2
4
0
8
6
12
16
20
12
18
0
3
164
The Optimal Server
k k p k k
f s  C  I (r , d s )
ape
k
d s
k
f s
Ip
Ck
d 0  max(r , d 0 )
k k
d s1  f s
k k
d s1  d s
k
s = 0
s = s+1
EXIT
compute the initial
k k 1 deadline with TBS
advance deadline
165
k k p k k
f s  C  I (r , d s )
d 0  max(r , d 0 )
k k
d s1  f s
k k
k
s = 0
s = s+1
EXIT
k k 1 O(1)
O(n)
( d s1  d s ) OR (s = K)
O(Kn)
polynomial
Tunable Bandwidth Server TB(K)
K = max number of steps
TB(0) = TBS TB() = TB*
Tuning performance vs. overhead
performance
overhead
166
K = 0
TBS
TB*
optimal server
K = 
167
Aperiodic responsiveness
0.1
0.2
0.8
0.9
0
1
5
4
3
2
7
6
0.3 0.4 0.5 0.6 0.7
Relative Aperiodic Load: a/(1-Up)
Avg. Response Time
TB(0)
Up = 0.85
9
8
10
TB(1)
TB(3)
TB(5)
TB*
168

1
4
8
Us = 1/4
0
8
12
4 6
2
10
1
C = 1
1 overrun
Problems with the TBS
Without a budget management, there is no protection against execution overruns.
If a job executes more than expected, hard tasks could miss their deadlines.
deadline miss

## Slide 29
Solution: task isolation
In the presence of overruns, only the faulty task should be delayed.
Each task i should not demand more than its declared utilization (Ui = Ci/Ti).
If a task executes more than expected, its priority should be decreased (i.e., its deadline postponed).
169
170
Bandwidth partitioning
Ideally, each task should be assigned a given bandwidth and never demand more.
10 %
45 %
25 %
20 %
1
2
3
4
Questions
What do we do if a task overruns?
  Only that task should be delayed.
Consequences
  if the task is hard => exception
  if the task is soft => QoS degradation
171
Achieving isolation
Isolation among tasks can be achieved through a bandwidth reservation.
Each task is managed by a dedicated server having bandwidth Us .
The server assigns priorities (or deadlines) to tasks so that they do not exceed the reserved bandwidth.
172
173
Implementation
CPU
server
Ready queue
EDF
1

Us1
Us2
Us3
Us1 + Us2 + Us3  1
2 server
3 server
Constant Bandwidth Server (CBS)
It assigns deadlines to tasks as the TBS, but keeps track of job executions through a budget mechanism.
When the budget is exhausted it is immediately replenished, but the deadline is postponed to keep the demand constant.
174

## Slide 30
CBS parameters
Given by the user
Maximum budget: Qs
Server period: Ts
Us = Qs / Ts (server bandwidth)
Maintained by the server
Current budget: cs (initialized to 0)
Server deadline: ds (initialized to 0)
175
Basic CBS rules
Arrival of job Jk  assign ds
if (rk + cs /Us  ds) then recycle (cs, ds )
else ds = rk + Ts cs = Qs
Budget exhausted  postpone ds
ds = ds + Ts cs = Qs
176
177
Deadline assignment
0
5
12
0
5
12
3
2
6
3
1
cs
Qs = 6
Ts = 12
178
Budget exhausted
12
12
3
cs
Qs = 3
Ts = 6
1
5
0 3 6
0 3
179
EDF + CBS schedule
CBS: Qs = 2, Ts = 6
1
2
6
0
12
18
24
9
27
0
8
14
d0
ape
3
d1
r1
3
r2
d2
1
18
d3
d4
0
2
4
6
8 10
cs
12
14 16 18
20 22 24 26
r3
24 27
18
CBS properties
Bandwidth Isolation
If a task i is served by a CBS with bandwidth Us then, in any interval t, i will never demand more than Us t.
Hard schedulability
A hard task i (Ci, Ti) is schedulable by a CBS with Qs = Ci and Ts = Ti, iff i is schedulable by EDF.
180

## Slide 31
181
It depends on the price (overhead) we want to pay to reduce task response times
Selecting the most suitable service mechanism
performance
overhead
optimal server (TB*)
TBS
Slack Stealer
DS PS
Background
TB(k)
CBS
SS
Inter-task communication mechanisms
Shared memory
Message passing ports
Asynchonous buffers
Handling shared resources
Problems caused by mutual exclusion
184
Critical sections
2
1
globlal memory buffer
write
read
int x;
int y;
wait(s) x = 3; y = 5; signal(s)
wait(s) a = x+1; b = y+2; c = x+y; signal(s)
185
Blocking on a semaphore
CS

1

2
CS
p1 > p2
1
2

It seems that the maximum blocking time for 1 is equal to the length of the critical section of 2, but …
186
Conflict on a critical section
priority
BCT
SCT
MT
B

## Slide 32
187
Priority Inversion
A pr tim | high priority task is blocked by a lower iority task a for an unbounded interval of e. | -
Solution
Introduce a concurrency control protocol for accessing critical sections.
Resource Access Protocols
Under fixed priorities
Non Preemptive Protocol (NPP)
Highest Locker Priority (HLP)
Priority Inheritance Protocol (PIP)
Priority Ceiling Protocol (PCP)
Under EDF
Stack Resource Policy (SRP)
188
Non Preemptive Protocol
189
Preemption is forbidden in critical sections.
Implementation: when a task enters a CS, its priority is increased at the maximum value.
PROBLEMS:
high priority tasks that do not use CS may also block
ADVANTAGES: simplicity
190
Conflict on critical section
B
priority
1
2
3
Schedule with NPP
priority
1
2
3
191
PCS = max{P1, … Pn}
192
Problem with NPP
priority
1
2
3
1 cannot preemt, although it could
useless blocking

## Slide 33
Highest Locker Priority
193
A task in a CS gets the highest priority among the tasks that use it.
FEATURES:
Simple implementation.
A task is blocked when attempting to preempt, not when entering the CS.
Schedule with HLP
priority
1
2
3
2 is blocked, but 1 can preempt within a CS
194
PCS = max {Pk | k uses CS}
195
Problem with HLP
CS
1
test
CS
2
1

2
p1 p2
1 blocks just in case ...
Priority Inheritance Protocol
[Sha, Rajkumar, Lehoczky, 90]
196
A task in a CS increases its priority only if it blocks other tasks.
A task in a CS inherits the highest priority among those tasks it blocks.
PCS = max {Pk | k blocked on CS}
197
priority
1
2
3
p1 p3
Schedule with PIP
direct blocking
push-through blocking
Types of blocking
Direct blocking
A task blocks on a locked semaphore
Push-through blocking
A task blocks because a lower priority task inherited a higher priority.
198
BLOCKING:
a delay caused bya lower priority task

## Slide 34
199
Identifying blocking resources
A task i can be blocked by those semaphores used by lower priority tasks and
  directly shared with i (direct blocking) or
  shared with tasks having priority higher than i
(push-through blocking).
Theo | rem: i can by eac | be block h of such | ed at most semaphores | once
Theo | rem: i can by eac | be block h lower pr | ed at most iority task | once
200
Bounding blocking times
If n is the number of tasks with priority less than i
and m is the number of semaphores on which i can be blocked, then
Theo | rem: i can the du sectio | be blo ration o ns | cked at most f min(n,m) cri | for tical
201
Example
priority
1
2

3
 | B |  | D | 
 | A |  | C | 
 | A |  | B |  | C |  | D
1 can be blocked once by 2 (on A2 or C2) and
once by 3 (on B3 or D3)
2 can be blocked once by 3 (on B3 or D3)
3
 cannot be blocked
202
Schedule with PIP
priority
1
2
3
4
P2
P1
Remarks on PIP
203
ADVANTAGES
It is transparent to the programmer.
It bounds priority inversion.
PROBLEMS
It does not avoid deadlocks and chained blocking.
204
Chained blocking with PIP
Theo | rem: i can by eac | be block h lower pr | ed at most iority task | once
priority
1

2
B1 B2 B3
3
4

## Slide 35
Priority Ceiling Protocol
205
Can be viewed as PIP + access test.
A task can enter a CS only if it is free and there is no risk of chained blocking.
To prevent chained blocking, a task may stop at the entrance of a free CS (ceiling blocking).
C(sk) = max {Pj : j uses sk}
Pi > max {C(sk) : sk locked by tasks  i}
Resource Ceilings
Each semaphore sk is assigned a ceiling:
A task i can enter a CS only if
206
Schedule with PCP
s1 C(s1) = P1
priority s2 C(s2) = P1
1
2
3
t1
207
t1: 2 is blocked by the PCP, since P2 < C(s1)
Remarks on PCP
208
ADVANTAGES
Blocking is reduced to only one CS
It prevents deadlocks
PROBLEMS
It is not transparent to the programmer: semaphores need ceilings
209
Typical Deadlock
1
2
1
2
blocked
blocked
P1 > P2
A B
B
A
210
Deadlock avoidance with PCP
1 2
1
2
P1 > P2
A B
B A
CA = P1 CB = P1
ceiling blocking

## Slide 36
Guarantee with resource constraints
We select a scheduling algorithm and a resource access protocol.
We compute the maximum blocking times (Bi) for each task.
We perform the guarantee test including the blocking terms.
211
212
Guarantee with RM (D = T)
preemption by HP tasks
i
blocking by LP tasks

i1
 i21/i 1
Ti
k 1 Tk
Ck  Ci  Bi
i
By LL test:
k
i i i
C
T
Ri
R  C  B  
i1
k 1 k
Guarantee with RM (D ≤ T)
preemption by HP tasks
i
blocking by LP tasks
By RTA test: i Ri  Di
213
Stack Resource Policy [Baker 1990]
It works both with fixed and dynamic priority
It limits blocking to 1 critical section
It prevents deadlock
It supports multi-unit resources
It allows stack sharing
It is easy to implement
214
215
Stack Resource Policy [Baker 90]
 Available units: n
k
For each resource Rk: Nk
 Maximum units: Nk
nk
Rk
 a static preemption level:
pi  1 Ti
pi  1 di
i i
  1 D
 a priority pi: RM
EDF
For each task i the system keeps:
 its resource requirements: i(Rk)
j
Ck (nk )  max  j : nk   j (Rk )
Stack Resource Policy [Baker 90]
Resource ceiling
System ceiling  s  maxCk (nk )
k
SRP Rule
216
A job cannot preempt until pi is the highest and i > s

## Slide 37
217
Example
t
i
3 1
2 2
1 3
s
3
2
1
0
SRP: Notes
Blocking always occurs at preemption time
A task never blocks on a wait primitive (semaphore queues are not needed)
Semaphores are still needed to update the system ceiling
Early blocking allows stack sharing
218
219
SRP: Stack sharing
stack
Classical blocking
1
2
t1 t2
stack
Early blocking
1
2
t1 t2
SRP: Stack sharing
If tasks can be grouped in M subsets with the same preemption level, then tasks within a group cannot preempt each other.
Then the stack size is the sum of the stack memory needed by M tasks.
If we have 100 tasks with 10 preemption levels, and each task requires 10 Kb of stack, then
1 Mb without SRP
Stack size =
100 Kb under SRP (90% less)
220
 1

i1
Ti
k 1 Tk
Ck  Ci  Bi
i
EDF Guarantee (Di = Ti)
preemption by HP tasks
i
blocking by LP tasks
221
222
EDF Guarantee: PD test (Di  Ti )
1
.
.
.
i
k
n
Tasks are ordered by decreasing preemption level

## Slide 38
223
EDF Guarantee: PD test (Di  Ti )
i
k
L  Dk  Tk C T k
k 1
gi (0, L)  Bi  
i
i L: D  L  max(D , L* )
i
i
i
L*  k 1
1 Uk k 1
Bi  (Tk  Dk )Uk
n i
U  1 AND gi (0, L)  L
224
Message passing paradigm
Every task operates on a private memory space, exchanging messages through channels:
Channel: logical link by which two tasks can communicate.
Message: set of data having a predefined format.
Communication Ports
The operating system provides the channel abstraction through the port construct.
A task can use a port to exchange messages by means of two primitives:
send sends a message to a port
receive receives a message from a port
225
226
Port types
STREAM
writer reader
MAILBOX
clients
server (owner)
STICK
producer (owner)
consumers
227
send(p, mes);
Using a port
Task A Task B
p = port_create(); p = port_connect();
receive(p, mes);
port_delete(p); port_disconnect(p);
NOTE: Task A is the owner and must start first.
Port primitives
port_create(name, size, num, type, access);
name: identification string
size: message size (in bytes)
num: maximum number of messages
type: STREAM, MAILBOX, STICK
access: READ, WRITE
It returns a port identifier.
port_delete(port_id);
Deletes the specified port.
228

## Slide 39
Port primitives
port_connect(name, size, type, access);
name: stringa di identificazione size: message size (in bytes) type: STREAM, MAILBOX, STICK
access: READ, WRITE
It returns a port identifier.
port_disconnect(port_id);
Deletes the specified port.
229
Port primitives
port_send (port_id, msg_ptr, sync) sends the message pointed by msg_ptr to the port identified by port_id.
sync = BLOCK blocks on a full buffer
sync = NON_BLOCK returns 0
port_receive(port_id, msg_ptr, sync)
receives a message from port_id and copies it into the buffer pointed by msg_ptr.
sync = BLOCK blocks on an empty buffer
sync = NON_BLOCK returns 0
230
writer(void)
TASK
{ PORT
char
p; mes[6];
p = port_create(“door”, 6, 8, STREAM, WRITE); while (condition) {
build_message(mes); port_send(p, mes, BLOCK); task_endcycle();
}
port_delete(p);
}
A task creates a port to send messages of 6 bytes. The port can keep up to 8 messages.
231
232
reader(void)
TASK
{ PORT
char
q; data[2];
q = port_connect(“door”, 2, STREAM, READ); while (condition) {
if (port_receive(q, data, NON_BLOCK)) action1();
else action2();
task_endcycle();
}
port_disconnect(q);
}
A task connects to an already opened port to receive messages of 2 bytes.
Periodic task communication
N
1 2
T1 T2
If T1 < T2, 1 puts more messages than 2 can read.
When the buffer is full, 1 must proceed with the same rate of 2.
233
234
f1
f2
t
Exchanged messages
# of exchanged messages = t · fi

## Slide 40
235
Buffer Saturation
If T1 < T2, the buffer saturates when:
T  T 
 t    t   N
 1   2 
Hence, the tasks proceed at their proprer rate while:
 t   t  t t
T  T   T  T 1  N
 1   2  1 2
T2  T1
t  (N 1) T1T2
That is, while:
236
STICK Ports
If T1 < T2, 1 overwrites previous messages.
Example:
STICK PORT
T2 = 2T1
2
aceg
T1
1
abcdefg
237
STICK Ports
If T1 > T2, 2 reads the same message more than once (messages are not consumed).
Example:
STICK PORT
T2
2
aabbccddee
T1 = 2T2
1
abcde
Blocking on STICK ports
STICK ports use a semaphore to avoid simultaneous accesses to the internal buffer.
Long messages may cause long blocking delays on the semaphore.
A more efficient solution avoids blocking through a buffer replication mechanism.
238
Cyclic Asynchronous Buffer
It is a mechanism for exchanging messages among periodic tasks with different rates.
It avoids memory conflicts by replicating the internal buffers.
State message semantics: messages are overridden by senders and are not consumed by receivers.
239
240
R
msg1
Simultaneous accesses
If a writer task W arrives while a task R is reading, the new message is written in a new buffer:
CAB
W
msg2

## Slide 41
241
Reading from a CAB
Once written, a message becomes available to the next reader:
R1
R2
writer write M1
write
read M1
read M1
M2
read M2
Accessing a CAB
CABs are accessed through a memory pointer.
Hence, a reader is not forced to copy the message in its memory space.
More tasks can simultaneously read the same message.
At each instant, a pointer (mrd) points to the most recent message stored in the CAB.
242
243
W
R1
R2
M2
R1
M1
M1 M2

R2
CAB
mrd
M3
M4
M4
If a CAB is used by N tasks, to avoid blocking, it must have at least N +1 buffers.
Dimensioning a CAB
The (N+1)-th buffer is needed for keeping the most recent message in the case all the other buffers are used.
244
Inconsistency with N buffers
mrd
M1 M2 M3 M4
M5
1 2 3 W
Assume all buffers are used and W overwrites the most recent message (M4) with M5.
If (while W is writing) 1 finishes and requests a new message, it finds the CAB inconsistent.
245
Writing in a CAB
246
. . .
p = cab_reserve(cab_id);
<copy message in *p>
cab_putmes(cab_id, p);
. . .

## Slide 42
Reading from a CAB
247
. . .
p = cab_getmes(cab_id);
<process message with *p>
cab_unget(cab_id, p);
. . .
CAB Primitives
cab_create(cab_name, buf_size, max_buf);
creates a CAB with max_buf buffers with size buf_size bytes.
It returns a global CAB identifier.
cab_delete(cab_id);
deletes the specified CAB.
248
CAB Primitives
cab_reserve(cab_id)
returns a pointer to write in a free buffer
cab_putmes(cab_id, pointer)
releases the pointer after a write operation
cab_getmes(cab_id)
returns a pointer to the most recent message
cab_unget(cab_id, pointer)
releases the pointer after a read operation
249
250
Position control
x
0
xd
M
Motor driver
xd
v
d
v
x
y


K
p
K
v
+
+
+
PD regulator
251
TASK pos_control()
{
int float
xd, vd, x, v;
y, Kp, Kv;
while (1) { get_gains(&Kp, &Kv);
get_setpoint(&xd, &vd); read_sensors(&x, &v);
y = Kp*(xd - x) - Kv*(vd - v); output(y);
task_endcycle();
}
}
252
Two-level control loop
force
sensor
Kf
F
Fd

+
vd
Motor driver
v
y

K
v
+

## Slide 43
253
Using CABs
Force sensor
motor
vd
CAB
f

v
y
v
F
Fd
vd
Using visual feedback
camera us
An ultrasound sensor is used for speed control
The camera is used for stear control
254
255
Three-level control
camera
US
car model H(z)
v
d

d
d
I
v 
vd
d
CAB1
CAB2

v
d
m
visual control
Tv = 100 ms
distance control
Td = 20 ms
motor control
Td = 5 ms
Overload management
257
0.75
0.5
0.25
0
0.75
0.5
0.25
0
time time
Examples of load
System designed under worst-case assumptions
load
1
System designed under average-case assumptions
load
1
Transient vs. permanent overload conditions
Transient overload: avg < 1, max > 1
Possible causes
 Arrival of aperiodic activities
 Exceptions raised by the kernel
 Malfunctioning of input devices
 Task with variable execution
 Sporadic overruns
258

## Slide 44
259
Types of overruns
A task is said to be in overrun if the time demanded for execution exceeds the expected value according to which the task has been guaranteed.
There are two types of overrun:
Execution overrun
A job executes more than expected
Activation overrun
A job arrives before the time it is expected
Transient vs. permanent overload conditions
Permanent overload: avg > 1
Possible causes
 Activation of a new periodic task
 Increase in the task frequencies
 Increase in the task quality (execution times)
 Changes in the environment
 Bad system design
260
Overload management methods
Activation overruns of aperiodic tasks
 Value-based scheduling
  tasks are assigned values and executed accordingly
 Admission control
  least importance tasks are rejected
  important tasks receive full service
Activation/Execution overruns
 Resource Reservation
  Tasks cannot use more than reserved
Permanent overload of periodic tasks
 Performance degradation
  all tasks are executed
  but with reduced requirements
261
Value-based scheduling
If  > 1, no all tasks can finish within their deadline.
To avoid domino effects, the load is reduced by rejecting the least important tasks.
To do that, the system must be able to handle tasks with both timing constraints and importance values.
262
263
How to assign values
A task i can be assigned a value vi according to different criteria. Those most common are:
vi = Vi | arbitrary constant
vi = Ci | computation time
vi = Vi/Ci | value density
264
Value as a function of time
In a real-time system, the value of a task depends on its completion time and criticality:
fi
vi (fi)
non real-time
fi
vi (fi)
soft
fi
vi (fi)
firm
d
i
di
ri
r
i
r
i
fi
vi (fi)
hard
ri
di 

## Slide 45
Performance evaluation
The performance of a scheduling algorithm A on a task set  can be evalutated through its Cumulative Value:
n
A (T )  vi ( fi )
i1
n
Note that: A (T )  max (T )  Vi
i1
265
266
Optimality under overloads
 | * (T )  | ma A | x A (T )
The performance of an algorithm can be evalutated with respect to *.
In overload conditions, there are no optimal on-line algorithms able to guarantee a cumulative value equal to *.
267
Proof (assume: Vi = Ci)
To maximize A we should know the future.
0
2
6
8
4
10 12 14 16
10
6
6

1

2

3
A = 10
w
t
If at | time t = 0 r3 is n that maximizes th | ot know, e cumula |  | e cannot select th ive value. | e
task |  |  |  |  | 
268
0 2 4 6 8 10 12 14 16
10
6
6
1
2

3
A = 12
0 2 4 6 8 10 12 14 16
10
6
6

1

2

3
A = 16
Best-effort scheduling
CPU
READY queue
tasks
Tasks are always accepted in the system.
Performance is controlled through a suitable (value-based) priority assignment.
Problem: domino effect.
269
Admission control
CPU
task
READY queue
test
Y
rejected N
Every task is subject to an acceptance test which keeps the load  1.
It prevents domino effects, but does not take values into account.
Low efficiency due to the worst-case guarantee (tasks may be unnecessarily rejected).
270

## Slide 46
Task scheduling and task rejection are controlled by two separate policies.
Tasks are scheduled by deadline, rejected by value.
In case of early completions, rejected tasks can be recovered by a reclaiming mechanism.
271
READY queue CPU
rejection policy
reject queue
Robust scheduling
scheduling
planning policy
task
recovery policy
EDF
Robust EDF
Scheduling Policy 
Rejection policy
when an overload is detected, reject the least value task which can bring the load below 1.
Recovery policy
  keep rejected tasks by decreasing values;
  when there is enough spare time, re-accept the highest value task which is still feasible.
272
Example: task rejection
Vi
7 1
10 2
5 3
2 4
3 5
0 2 4 6 8 10 12 14 16 18 20
at time t = 4  3 rejected
273
Example: task rejection
Vi
7 1
10 2
5 3
2 4
3 5
0 2 4 6 8 10 12 14 16 18 20
at time t = 4  3 rejected
274
275
1
2
0 2 4 6 8 10 12 14 16 18 20
at time t = 8  3 can be recovered
Example: task recovery
1
2
Vi
7 
10 
5 3
2 4
3 5
Resource Reservation
Handling sporadic overruns

## Slide 47
277
1
4
8
Us = 1/4
0
8
12
4 6
2
10
C1 = 1
1 overrun
Problems with overruns
Without a budget management, there is no protection against execution overruns.
If a job executes more than expected, hard tasks could miss their deadlines.
deadline miss
Solution: Temporal Isolation
The execution of a task should not affect the guarantee performed on the other tasks.
Each task i receives a fraction Ui of the processor (its bandwidth) and behaves as it were executing alone on a slower processor of speed Ui.
bandwidth reservation
Temporal isolation
bandwidth enforcement
278
Bandwidth reservation
Ideally, each task should be assigned a given bandwidth and never demand more.
25 %
20 %
1
2
3
10 %
4
45 %
However, tasks are subject to overruns or the reserved bandwidth can be insufficient for the task.
279
Bandwidth enforcement
It is a mechanism needed for degrading the QoS when a task demands more than the reserved bandwidth.
If a task executes more than expected, its priority should be decreased (i.e., its deadline postponed).
When a task experiences an overrun, only that task is delayed, so that the guarantee performed on the other tasks is preserved.
280
281
Implementation
CPU
server
Ready queue
EDF
1
2
3
Us1
Us2
Us3
Us1 + Us2 + Us3  1
server
server
Handling permanent overload

## Slide 48
Performance Degradation
The load can be decreased not only by rejecting tasks, but also by reducing their performance requirements.
This can be done by:
reducing precision of results
skipping some jobs;
relaxing timing constraints.
283
Reducing precision
In many applications, computation can be performed at different level of precision: the higher the precision, the longer the computation. Examples are:
binary search algorithms
image processing and computer graphics
neural learning
284
285
Imprecise computation
In this model, each task i (Ci, Di, wi) is divided in two portions:
a mandatory part: m (M , D )
i i i
an optional part: oi (Oi, Di)
Mi Oi
wi is an importance weight
286
Mi Oi
Imprecise computation
In this model, a schedule is said to be:
feasible, if all mandatory parts complete in Di
precise, if also the optional parts are completed.
n
error: i = Oi  i average error: a   wi i
i1
i
GOAL: minimize the average error
Job skipping
Periodic load can also be reduced by skipping some jobs, once in a while.
Many systems tolerate skips, if they do not occur too often:
multimedia systems (video reproduction)
inertial systems (robots)
monitoring systems (sporadic data loss)
287
288
2 6
p
U  1  4  1.17  1
Example
The system is overloaded, but tasks can be schedulable if t1 skips one instance every 3:

1
 |  |  |  |  | sk | ip |  |  |  |  | sk | ip |  |  |  |  | sk | ip |  |  | 
2

## Slide 49
FIRM task model
Every job can either be executed within its deadline, or completely rejected (skipped).
A percentage of task instances must be guaranteed off line to finish in time.
Each task i is described by (Ci, Ti, Di, Si):
Si is the minimum number of jobs that must be executed between two consecutive skips.
289
Every instance can be red or blue:
  red instances must finish within their deadline
  blue instances can be aborted
If a blue instance is aborted, the next Si-1 instances must be red.
If a blue instance is completed within its deadline, the next instance is still blue.
The first Si-1 instances of every task must be
red.
290
291
i
Example
Ci = 1 Ti = 2 Di = 2 Si = 3
skip skip
skip
skip
i
skip
skip
skip
Equivalent utilizazion factor
292
n
p
L0
 gi (0, L)
i1
L
U *  max
Ti Si
Ci

 Ti
 L L 
gi (0, L)   
Theorem: A set of firm periodic tasks is schedulable if
 1
p
U *
Schedulability Analysis
A sufficient condition
293
1
i1
Ti Si
Theorem: A set of firm periodic tasks is not schedulable if
n Ci (Si 1) 
A necessary condition
NOTE: the sum represents the utilization of the computation that must take place.
294

## Slide 50
295
Bandwidth saving
In general, skipping jobs of periodic tasks causes a bandwidth saving:
Such a bandwidth can be used for
  improving aperiodic responsiveness (by increasing their reserved bandwidth);
  accepting a larger number of periodic tasks.
p p
U  U  U *
296
Hence:
gi (0, L)  Ti  1
L Ti
Not always skips save bandwidth:
Ci = Ti
0 Ti
In this case: Up* = 1
In fact, for L = Ti we have gi (0,L) = Ci = Ti
i
skip skip
297
C1 = T1
0 T1

1
*
In this case we still have: Up = 1
In fact: g(0, T1) = T1 e g(0, T2) = T2
However, notice that:
Hence:
T1 T2
g(0,T1 )  g(0,T2 )  1
C2 = T1
0 T2
2
Relaxing timing constraints
The idea is to reduce the load by increasing deadlines and/or periods.
Each task must specify a range of values in which its period must be included.
Periods are increased during overloads, and reduced when the overload is over.
298
299
time
# of jobs
4
3
2
1
4 arrives at time t*
t*
Overload handling due to a new arrival
300
time
Overload handling due to an increased rate
1
# of jobs
3
2
1 increases its rate at t*
t*

## Slide 51
301
Example
20 40 70
p
U  10  10  15  0.96
task | Ci | Ti0 | Tmin | Tmax
1 | 10 | 20 | 20 | 25
2 | 10 | 40 | 40 | 50
3 | 15 | 70 | 35 | 80
 1.13
 10  10  15  5
20 40 70 30
p
U
 0.99
 10  10  15  5
23 50 80 30
p
U
Load adaptation
If 4 arrives with: C4 = 5, T4 = 30 the system is not schedulable any more:
However, there exists a feasible schedule within the specified ranges:
302
Elastic task model
Tasks’ utilizations are treated as elastic springs and can be changed by period variations.
The resistance of a task to a period variation is controlled by an elastic coefficient Ei:
 the greater Ei the greater the elasticity
303
304
t
Elastic task model
A periodic task i is characterized by:
(Ci, Ti0, Ti-min, Ti-max, Ei)
The actual period Ti  [Ti-min, Ti-max]
Ei
i
ri Ti-min Ti0 Ti-max
Special cases
A task with Tmin = Tmax, is equivalent to a hard task.
A task with Ei = 0 can intentionally change its period but does not allows the system to do that.
305
306
1
2 3
4
1
Up
1
Up
1
2 3 4
Compression algorithm
During overloads, utilizations must be compressed to bring the load below one.

## Slide 52
307
L0 x
The linear spring analogy
x1o x2o x3o
0
x1 x2
x3
F
0
F = k1(x1o - x1) F = k2(x2o - x2) F = k3(x3o - x3)
Ld x
x1 + x2 + x3 = Ld x1o + x2o + x3o = L0
308
1 2 3
k k k
F ( 1  1  1 )  (x  x  x )  (x  x  x )
Solution without constraints
Summing the equations, we have:
1o 2o 3o 1 2 3
 (L0  Ld )
That is:
(L0  Ld )
1  1  1
k1 k2 k3
F 
309
That is:
0 d
1 1o 1
1  1  1
k1 k2 k3
(L  L )
F  k (x  x ) 
1
1
k
1 1o 0 d
1  1  1
k1 k2 k3
x  x  (L  L )
Solution without constraints
Substituting F in the equations, we have:
310
K 
i1 ki
//
n 1
i
K 1
k
//
i io 0 d
x  x  (L  L )
And defining: Ei = 1/ki
n
Es   Ei
i1
s
i
E
E
i io 0 d
x  x  (L  L )
Solution without constraints
311
Period computation
s
i
E
E
Ui  Uio  (U0 Ud )
i
i
U
Ci
T 
And then:
312
0
L0 x
F
0 Ld x
F
0
Ld x
Solution with constraints
Iterative solution:

## Slide 53
Other use of elastic tasks
Quickly find new period configurations during negotiation.
Dynamically adjust the rates to fully utilize the processor.
313
Problem Understanding
Real-Time applications are usually guaranteed based on worst-case execution times (WCETs).
However, a precise WCET estimation is very difficult to achieve (due to interrupts, prefetch, cache, and DMA mechanisms).
A wrong WCET estimate may cause the following problems:
314
315
Over-estimation of WCETs
high predictability
low efficiency
Under-estimation of WCETs
high efficiency
low predictability
1
0.75
0.5
0.25
0
time
Predictability vs. efficiency
load
0.75
0.5
0.25
0
time
load
1
Adaptive solution
The user does not specify any WCET.
The system:
  monitors tasks’ execution times to estimate the actual load (Ue);
  adapts the task rates to keep the processor utilization close to a desired value (Ud).
316
Task importance must be taken into account while performing rate adaptation.
Qi = ci + k (Ci  ci)
Execution Time Estimator
Monitored parameters (for each task ti): ci current average execution time Ci current worst-case execution time
Building a prediction:
k = balancing factor
317
318
Load as a feedback
Rate Adaptation Algorithm
Load estimator
Execution time Estimator
Ud
U
e
Ti
Real-Time System |  | 
ci |  | Ci
Q
i