## Slide 1: Zonghua Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 1
Introduction to ARM Processor and ARM Assembly
Zonghua Gu
Fall 2025
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Why ARM processor
ADC
DAC
USART,SPI, I2C
LCD Driver
USB 2.0
Touch sensing
Advanced timers
Motor control
ARM: Acron RISC Machine, founded in 1990
Public company, Headquarter at Cambridge, England, UK, 2023 Revenue: US$2.68 billion
Arm processors are used as the main CPU for most mobile phones and handhelds.
The world's second fastest supercomputer (previously fastest) in 2022, the Japanese Fugaku is based on Arm AArch64 architecture

## Slide 3: Embedded Systems

## Slide 4: Memory
Memory is arranged as a series of “locations”
  Each location has a unique “address”
  Each location holds a byte (byte-addressable)
  e.g. the memory location at address 0x080001B0 contains the byte value 0x70, i.e., 112
The number of locations in memory is limited
  e.g. 4 GB of RAM
  1 Gigabyte (GB) = 230 bytes
  232 locations  4,294,967,296 locations!
Values stored at each location can represent either program data or program instructions
  e.g. the value 0x70 might be the code used to tell the processor to add two values together
70
BC
18
01
A0
0x00000000
0xFFFFFFFF
0x080001B0
0x080001AF
0x080001AE
0x080001AD
0x080001AC
Memory
Address
Data
8 bits
32 bits

## Slide 5: Computer Architecture
Instructions and data are stored in the same memory.
Von-Neumann
Harvard
Data and instructions are stored into separate memories.

## Slide 6: Computer Architecture
Instructions and data are stored in the same memory.
Von-Neumann
Harvard
Data and instructions are stored into separate memories.

## Slide 7: ARM Cortex-M Series Family
Instructions and data are stored in the same memory.
Von-Neumann
Harvard
Data and instructions are stored into separate memories.
ARM
Cortex-M0
ARM
Cortex-M1
ARM
Cortex-M0+
ARM
Cortex-M23
ARM
Cortex-M3
ARM
Cortex-M7
ARM
Cortex-M4
ARM
Cortex-M33
ARMv6-M
ARMv6-M
ARMv6-M
ARMv8-M
ARMv7-M
ARMv7E-M
ARMv7E-M
ARMv8-M

## Slide 8: Levels of Program Code
High-level language
  Level of abstraction closer to problem domain
  Provides for productivity and portability
C Program
Compile
Assemble
Assembly Program
Assembly language
  Textual representation of instructions
  Human-readable format instructions
Machine Program
Hardware representation
  Binary digits (bits)
  Encoded instructions and data
  Computer-readable format instructions
0010000100000000
0010000000000000
1110000000000001
0100010000000001
0001110001000000
0010100000001010
1101110011111011
1011111100000000
1110011111111110
int main(void){
int i;
int total = 0;
for (i = 0; i < 10; i++) {
total += i;
}
while(1); // Dead loop
}

## Slide 9: See a Program Runs
int main(void){
int a = 0;
int b = 1;
int c;
c = a + b;
return 0;
}
C Code
compiler
MOVS r1, #0x00 ; int a = 0
MOVS r2, #0x01 ; int b = 1
ADDS r3, r1, r2 ; c = a + b
MOVS r0, 0x00 ; set return value
BX lr ; return
Assembly Code
assembler
0010000100000000
0010001000000001
0001100010001011
0010000000000000
0100011101110000
Machine Code
In Binary
; MOVS r1, #0x00
; MOVS r2, #0x01
; ADDS r3, r1, r2
; MOVS r0, #0x00
; BX lr
2100
2201
188B
2000
4770
In Hex

## Slide 10: Processor Registers
Fastest way to read and write
Registers are within the processor chip
A register stores 32-bit value
ARM Cortex-M has
  R0-R12: 13 general-purpose registers
  R13: Stack pointer (Shadow of MSP or PSP)
  R14: Link register (LR)
  R15: Program counter (PC)
  Special registers (xPSR, BASEPRI, PRIMASK, etc)

## Slide 11: Program Execution
Program Counter (PC) is a register that holds the memory address of the next instruction to be fetched from the memory.
1. Fetch instruction at PC address
2. Decode the instruction
3. Execute the instruction
4770 2000
188B
2201
2100
0x080001B4
0x080001B2
0x080001B0
0x080001AE
0x080001AC
PC
Memory Address
PC = 0x080001B0
Instruction = 188B or
2000188B or 8B180020

## Slide 12: Three-state pipeline: Fetch, Decode, Execution
Pipelining allows hardware resources to be fully utilized
One 32-bit instruction or two 16-bit instructions can be fetched.
Pipeline of 32-bit instructions

## Slide 13: Three-state pipeline: Fetch, Decode, Execution
Pipelining allows hardware resources to be fully utilized
One 32-bit instruction or two 16-bit instructions can be fetched.
Pipeline of 16-bit instructions

## Slide 14: Machine codes are stored in memory
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
ALU
4770 2000
188B
2201
2100
pc
lr
sp
0x00000000
0xFFFFFFFF
0x080001B4
0x080001B2
0x080001B0
0x080001AE
0x080001AC
Registers
Memory
Address
Data
CPU

## Slide 15: Fetch Instruction: pc = 0x08001AC Decode Instruction: 2100 = MOVS r1, #0x00
0x080001AC
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
ALU
4770 2000
188B
2201
2100
pc
lr
sp
0x00000000
0xFFFFFFFF
Registers
Memory
Address
Data
CPU
0x080001B4
0x080001B2
0x080001B0
0x080001AE
0x080001AC

## Slide 16: Execute Instruction: MOVS r1, #0x00
0x080001AC
0x00000000
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
ALU
4770 2000
188B
2201
2100
pc
lr
sp
0x00000000
0xFFFFFFFF
Registers
Memory
Address
Data
CPU
0x080001B4
0x080001B2
0x080001B0
0x080001AE
0x080001AC

## Slide 17: Fetch Next Instruction: pc = pc + 2
0x080001AE
0x00000000
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
ALU
4770 2000
188B
2201
2100
pc
lr
sp
0x00000000
0xFFFFFFFF
Registers
Memory
Address
Data
CPU
0x080001B4
0x080001B2
0x080001B0
0x080001AE
0x080001AC
Thumb-2 consists of a mix of 16- & 32-bit instructions
In reality, we always fetch 4 bytes from the instruction memory (either one 32-bit instruction or two 16-bit instructions)
To simplify the demo, we assume we only fetch 2 bytes from the instruction memory in this example.

## Slide 18: Fetch Next Instruction: pc = pc + 2 Decode & Execute: 2201 = MOVS r2, #0x01
0x080001AE
0x00000001
0x00000000
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
ALU
4770 2000
188B
2201
2100
pc
lr
sp
0x00000000
0xFFFFFFFF
Registers
Memory
Address
Data
CPU
0x080001B4
0x080001B2
0x080001B0
0x080001AE
0x080001AC

## Slide 19: Fetch Next Instruction: pc = pc + 2 Decode & Execute: 188B = ADDS r3, r1, r2
0x080001B0
0x00000001
0x00000001
0x00000000
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
ALU
4770 2000
188B
2201
2100
pc
lr
sp
0x00000000
0xFFFFFFFF
Registers
Memory
Address
Data
CPU
0x080001B4
0x080001B2
0x080001B0
0x080001AE
0x080001AC

## Slide 20: Fetch Next Instruction: pc = pc + 2 Decode & Execute: 2000 = MOVS r0, #0x00
0x080001B2
0x00000001
0x00000000
0x00000000
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
ALU
4770 2000
188B
2201
2100
pc
lr
sp
0x00000000
0xFFFFFFFF
Registers
Memory
Address
Data
CPU
0x080001B4
0x080001B2
0x080001B0
0x080001AE
0x080001AC

## Slide 21: Fetch Next Instruction: pc = pc + 2 Decode & Decode: 4770 = BX lr
0x080001B4
0x00000001
0x00000000
0x00000000
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
ALU
4770 2000
188B
2201
2100
pc
lr
sp
0x00000000
0xFFFFFFFF
Registers
Memory
Address
Data
CPU
0x080001B4
0x080001B2
0x080001B0
0x080001AE
0x080001AC

## Slide 22: Realities
In the previous example,
  PC is incremented by 2
  Well, I lied!

## Slide 23: Realities
PC is always incremented by 4.
  Each time, 4 bytes are fetched from the instruction memory
  It is either two 16-bit instructions or one 32-bit instruction
    If bit [15-11] = 11101, 11110, or 11111, then, it is the first half-word of a 32-bit instruction.
    Otherwise, it is a 16-bit instruction.

## Slide 24: Example: Calculate the Sum of an Array
int a[10] = {1, 2, 3, 4, 5, 6, 7, 8, 9, 10};
int total;
int main(void){
int i;
total = 0;
for (i = 0; i < 10; i++) {
total += a[i];
}
while(1);
}

## Slide 25: Example: Calculate the Sum of an Array
CPU
I/O Devices
Data
Memory (RAM)
Instruction Memory (Flash)
int main(void){
int i;
total = 0;
for (i = 0; i < 10; i++) {
total += a[i];
}
while(1);
}
int a[10] = {1, 2, 3, 4, 5, 6, 7, 8, 9, 10};
int total;
Starting memory address
0x08000000
Starting memory address
0x20000000
Notes: #define __I volatile const /*!< defines 'read only' permissions */
#define __O volatile /*!< defines 'write only' permissions */
#define __IO volatile /*!< defines 'read / write' permissions */

## Slide 26: Example: Calculate the Sum of an Array
Instruction Memory (Flash)
int main(void){
int i;
total = 0;
for (i = 0; i < 10; i++) {
total += a[i];
}
while(1);
}
Starting memory address
0x08000000
0010 0001 0000 0000
0100 1010 0000 1000
0110 0000 0001 0001
0010 0000 0000 0000
1110 0000 0000 1000
0100 1001 0000 0111
1111 1000 0101 0001 0001 0000 0010 0000
0100 1010 0000 0100
0110 1000 0001 0010
0100 0100 0001 0001
0100 1010 0000 0011
0110 0000 0001 0001
0001 1100 0100 0000
0010 1000 0000 1010
1101 1011 1111 0100
1011 1111 0000 0000
1110 0111 1111 1110
MOVS r1, #0x00
LDR r2, = total_addr
STR r1, [r2, #0x00]
MOVS r0, #0x00
B Check
Loop: LDR r1, = a_addr
LDR r1, [r1, r0, LSL #2]
LDR r2, = total_addr
LDR r2, [r2, #0x00]
ADD r1, r1, r2
LDR r2, = total_addr
STR r1, [r2,#0x00]
ADDS r0, r0, #1
Check: CMP r0, #0x0A
BLT Loop
NOP
Self: B Self
Notes: #define __I volatile const /*!< defines 'read only' permissions */
#define __O volatile /*!< defines 'write only' permissions */
#define __IO volatile /*!< defines 'read / write' permissions */

## Slide 27: Example: Calculate the Sum of an Array
0x00000000
0x00000000
0x00000000
0x00000000
0x00000000
0x00000000
0x00000000 0x00000000
0x00000000
0x00000000
0x00000000
0x00000000
0x0000000A
0x00000009
0x00000008
0x00000007
0x00000006
0x00000005
0x00000004
0x00000003
0x00000002
0x00000001
Data
Memory (RAM)
int a[10] = {1, 2, 3, 4, 5, 6, 7, 8, 9, 10};
int total;
Assume the starting memory address of the data memory is 0x20000000
0x20000054
0x20000050
0x2000004C
0x20000048
0x20000044
0x20000040
0x2000003C 0x20000038
0x20000034
0x20000030
0x2000002C
0x20000028
0x20000024
0x20000020
0x2000001C
0x20000018
0x20000014
0x20000010
0x2000000C
0x20000008
0x20000004
0x20000000
Memory
address
in bytes
Memory
content
total= 0x00000000
a[9] = 0x0000000A
a[8] = 0x00000009
a[7] = 0x00000008
a[6] = 0x00000007
a[5] = 0x00000006
a[4] = 0x00000005
a[3] = 0x00000004
a[2] = 0x00000003
a[1] = 0x00000002
a[0] = 0x00000001
Notes: #define __I volatile const /*!< defines 'read only' permissions */
#define __O volatile /*!< defines 'write only' permissions */
#define __IO volatile /*!< defines 'read / write' permissions */

## Slide 28: Loading Code and Data into Memory

## Slide 29: Loading Code and Data into Memory

## Slide 30: Loading Code and Data into Memory
Stack is mandatory
Heap is used only if dynamic allocation (e.g. malloc, calloc) is used.

## Slide 31: View of a Binary Program

## Slide 32: STM32L4
from st.com

## Slide 33: Memory Map