## Slide 1: CSC 112: Computer Operating Systems Lecture 6 Real-Time Scheduling I
Department of Computer Science,
Hofstra University
Acknowledgement: Lecture slides based on Buttazzo, Hard Real-Time Computing Systems

## Slide 2: Outline
Part I
  Introduction to RTOS and Real-Time Scheduling
  Fixed-Priority Scheduling
  Earliest Deadline First Scheduling
  Least Laxity First (LLF) Scheduling
  Preemptive vs. Non-Preemptive Scheduling
Part II
  Multiprocessor Scheduling
  Resource Synchronization Protocols (for Fixed-Priority Scheduling)

## Slide 3
Introduction to RTOS and Real-Time Scheduling

## Slide 4: Embedded Control Systems
An embedded control system co´nsists of:
  The system-under-control (SUT)
    may include sensors and actuators
  The controller/computer
    sends signals to the system according to a predetermined control objective
In the old days, each control task runs on a dedicated CPU
  No RTOS, bare metal
  No need for scheduling
  Just make sure that task execution time < deadline
Now, multiple control tasks share one CPU
  Multitasking RTOS
  Need scheduling to make sure all tasks meet deadlines
Controller/computer
actuators
D/A
SUT
sensors
A/D
Thread or process (task)
Resource

## Slide 5: Requirements
The tight interaction with the environment requires the system to react to events within precise timing constraints
Timing constraints are imposed by the dynamics of the environment
The real-time operating system (RTOS) must be able to execute tasks within timing constraints

## Slide 6: A Robot Control Example
Consider a robot equipped with:
  two actuated wheels
  two proximity (US) sensors
  a mobile (pan/tilt) camera
  a wireless transceiver
Goal:
  follow a path based on visual feedback
  avoid obstacles
visual−based navigation
visual tracking
obstacle avoidance
10 ms
100 ms
object recognition
mot_dx
mot_sx
pan
tilt
camera
US1 US2
1 ms
vehicle control
5 ms
20 ms
feature extraction
motor control
motor control
motor control
motor control
1 ms
Notes: send complete robot status every 20 ms

## Slide 7: Real-Time Systems
A computer system that is able to respond to events within precise timing constraints
A system where the correctness depends not only on the output values, but also on the time at which results are produced
A real-time system is not a necessarily a real fast system
  Speed is always relative to a specific environment
  Running faster is good, but does not guarantee hard real-time constraints
The objective of a real-time system is to guarantee the worst-case timing behaviour of each individual task
The objective of a fast system is to optimize the average-case performance
  A system with fast average-case performance may not meet worst-case timing requirements
  Analogy: there was a person who drowned in a river with average depth of 15 cm
x (t)
RT system Environment
t
y (t+)
Notes: response time of a task set.

## Slide 8: RTOS Requirements
Timeliness: results must be correct not only in their value but also in the time domain
  provide kernel mechanism for time management and for handling tasks with explicit timing constraints and different criticality
Predictability: system must be analyzable to predict the consequences of any scheduling decision
  if some task cannot be guaranteed within time constraints, system must notify this in advance, to handle the exception (plan alternative actions)
Efficiency: operating system should optimize the use of available resources (computation time, memory, energy)
Robustness: must be resilient to peak-load conditions
Fault tolerance: single software/hardware failures should not cause the system to crash
Maintainability: modular architecture to ensure that modifications are easy to perform

## Slide 9: Sources of Nondeterminism
Architecture
  cache, pipelining, interrupts, DMA
Operating System (our focus in this lecture)
  scheduling, synchronization, communication
Language
  lack of explicit support for time
Design Methodologies
  lack of analysis and verification techniques

## Slide 10: Task
The concept of concurrent tasks reflects the intuition about the functionality of embedded systems.
  Task here can refer to either process or thread, depending on the underlying RTOS support
Tasks help us manage timing complexity:
  multiple execution rates
    multimedia
    automotive
  asynchronous input
    user interfaces
    communication systems
“activation” = “arrival” = “release” time
Task i
activation time ai
start time si
finish time fi
Execution time Ci
CPU
activation
dispatching termination
Ready queue
3 2 1

## Slide 11: Schedule
A specific assignment of tasks to the processor that determines the task execution sequence. Formally:
Given a task set , a schedule is a function that associates an integer to each time slice with the meaning:
  : in the processor is idle
  : in the processor executes
At times t1, t2,…: context switch to a different task
1 2 3
idle
idle
(t)
3
2
1
0
t
t3
t4
t1 t2
Notes: Deciding the order of a set of tasks with certain known characteristics (periodicity, execution time) on a limited set of processing units, subject to a set of constraints on the completion time of each task.

## Slide 12: Preemptive vs. Nonpreemptive Scheduling
priority
1
2
3
(t)
3
2
1
0
0
2
4
6
8 10 12 14 16 18 20
0
2
4
6
8 10 12 14 16 18 20
A scheduling algorithm is:
  preemptive: if the active job can be temporarily suspended to execute a more important job
  non-preemptive: if the active job cannot be suspended, i.e., always runs to completion
Preemptive scheduling example
Notes:  + Exception handling: timely response to issues
Different levels of importance or criticality: preemption executes most critical tasks
Running tasks may be suspended and placed in the ready queue

## Slide 13: Definitions
Feasible schedule
  A schedule is said to be feasible if all the tasks can complete according to a set of specified constraints.
Schedulable set of tasks
  A set of tasks is said to be schedulable if there exists at least one algorithm that can produce a feasible schedule for it.
Hard real-time task: missing deadline may have catastrophic consequences, so deadline violations are not permitted. A system able to handle hard real-time tasks is a hard real-time system
  sensory acquisition
  low-level control
  sensory-motor planning
Soft real-time task: missing deadlines causes Quality-of-Service(QoS)/performance degradation, so deadline violations are expected and permitted
  reading data from the keyboard—user command interpretation
  message displaying
  graphical activities
Notes: Deciding the order of a set of tasks with certain known characteristics (periodicity, execution time) on a limited set of processing units, subject to a set of constraints on the completion time of each task.
Hard Real-Time System if it can handle hard tasks
HARD tasks
  All jobs must meet their deadlines. Missing deadlines may cause catastrophic consequences.
  e.g., sensor reading, motor control.
SOFT tasks
  Missing deadlines is not desirable but causes only Quality-of-Service(QoS) degradation.
  e.g., reading data from keyboard, user command interpretation, message display
A system able to handle HARD tasks is a hard real-time system

## Slide 14: Real-Time Task
t
fi
d
i
relative deadline Di
i
ai si
response time Ri
absolute deadline (di = ai + Di)
A task characterized by a timing constraint on its response time, called deadline:
  relative deadline : part of task attribute definition, measured from task arrival time ai
  Absolute deadline : measured from some absolute reference time point 0
  Gantt chart convention: upwards arrows denote job arrival/release times; downwards arrows denote deadlines
Definition: feasible task
  A real-time task is said to be feasible if it completes within its absolute deadline, that is, if , or, equivalently, if
Notes: “Completion time” = fi - si = Ri – (si- ai)

## Slide 15: Tasks and Jobs
A task running several times on different input data generates a sequence of instances (jobs)
  Upwards arrow: task arrival or release times; downwards arrow: task deadlines
Activation mode:
  Periodic tasks: the task is activated by the operating system at predefined time intervals
  Aperiodic tasks: the task is activated at an event arrival
Job 1
i,1
Job 2
i,2
Job 3
i,3
ai,k
ai,k+1
t
i
Ci
ai,1
Notes: Time-driven

## Slide 16: Estimating WCET is Not Easy
Each job operates on different data and can take different paths.
Even for the same data, computation time depends on processor state (cache state, number of preemptions).
We use to denote Worst-Case Execution Time (WCET) in this lecture, and assume it is given as part of task parameters.
?
Distribution
(probability density function)
loop
?
?
execution time
Ci
min
Ci
max
timer

## Slide 17: Predictability/Safety vs. Efficiency
execution time
Ci
min
Ci
max
Ci
avg
Ci estimate
safe
efficient
unsafe
Tradeoff between safety and efficiency in estimating the WCET
  Setting a large achieves high predictability and safety, since it is unlikely to be exceeded at runtime; but it hurts efficiency, since the system needs to reserve more CPU time for the task. Suitable for hard real-time tasks.
  Setting a small achieves high efficiency, but hurts safety, since the task may execute for more than its estimate. Suitable for soft real-time tasks.
Distribution
(probability density function)
Notes: where deadline violations may cause severe consequencesIt is a parameter related to the consequences of missing the deadline
  Hard: missing deadline may have catastrophic consequences
  Hard Real-Time System if it can handle hard tasks
    sensory acquisition
    low-level control
    sensory-motor planning
  Soft: missing a deadline causes performance degradation
    reading data from the keyboard—user command interpretation
    message displaying
    graphical activities
Value, vi = the relative importance of a task wrt other tasks

## Slide 18: Jitter
It is a measure of the time variation of a periodic event:
fi,1
Finish-time Jitter
i
fi,2
fi,3
si,1
Start-time Jitter
i
si,1 si,2 si,3
Completion-time Jitter (I/O Jitter)
i
si,2
si,3
fi,2
fi,1
fi,3
Notes: max (tk – ak) – min (tk – ak)
k k
max | (tk – ak) – (fk-1 – ak-1) |

## Slide 19: Periodic Task
A periodic task has a tuple of 3 attributes ():
  Worst-Case Execution Time (WCET) ; Period ; Relative Deadline
  Implicit deadline if ; Constrained deadline if
It generates an infinite sequence of jobs in every period:
Ti
job ik
ai,k
ai,k+1
i (Ci , Ti , Di )
Ci
t
ai,1 = i
task phase or
Release offset
ai,k di,k
= i + (k1) Ti
= ai,k + Di
often
Di = Ti
input
C
i
wait()
timer (period Ti )
output
A job of task
Multiple jobs released by task
Notes: Consider a periodic task τ1(C1,T1,D1) with phase Φ1, where:
  C1 = 10 ms, T1 = 50 ms, D1 = 25 ms, and Φ1 = 100 ms
What is τ1’s utilization factor?
Is τ1 feasible?
What is τ1,1’s absolute deadline?
What is τ1,1’s laxity?
What is τ1,2’s release time?
Can τ1,1 and τ1,2 have different laxity?
Can τ1,1 and τ1,2 have different slack?
If τ1,2’s slack is 10ms, what is τ1,s’s finishing time?
What is τ1,2’s response time?
With a 2-CPU machine, can τ1,2 and τ1,3 have the same release time?
Can τ1,2 and τ1,3 have the same finishing time?

## Slide 20: Aperiodic & Sporadic Task
Aperiodic task: jobs may arrive at arbitrary time instants
Sporadic task: arrival times with a minimum interarrival time constraint
Aperiodic:
ai,k+1 > ai,k
minimum interarrival time
Sporadic:
ai,k+1
 ai,k + Ti
Ci
job ik
Ci
Ci
ai,k
ai,k+1
t
i
ai,1

## Slide 21: Types of Constraints
Timing constraints
  Deadline, jitter
Precedence constraints
  Relative ordering among task executions
Resource constraints
  Synchronization when accessing mutually-exclusive resources (shared data)

## Slide 22: Precedence Constraints
Tasks must be executed with specific precedence relations, specified by a Directed Acyclic Graph (Precedence Graph)
Example application of parts inspection in a factory. Tasks:
  Image acquisition (acq1, acq2)
  Edge detection (edge1, edge2)
  Shape detection (shape), pixel disparities (disp)
  Height determination (height), recognition (rec)
stereo vision
processing
recognition
acq1
acq2
edge1
edge2
shape
disp
depth
rec
Notes: Precedence graph?

## Slide 23: Resource Constraints
To ensure data consistency, shared data must be accessed in mutual exclusion
Example: the writer task writes to variables and ; the reader task reads and . The pair of variables should be updated atomically, i.e., should read either or .
Left upper: an erroneous scenario when τR reads a set of inconsistent values .
Left lower: protecting the critical section (yellow parts) with a mutex lock ensures atomicity.
x = 3
y = 5
W
R
x = 1
y = 8
x = 1
y = 5
W
R
x=1
y=5
read
x = 3
y = 5
x = 1
y = 8
x = 1
y = 8
W
R
x = 1
y = 8
W
R

read
Erroneous scenario with no lock protection
Correct scenario with lock protection

## Slide 24: Scheduling Metrics
Lateness represents the delay of a task completion with respect to its deadline; if a task completes before the deadline, its lateness is negative.
Tardiness or exceeding time is the time a task stays active after its deadline; if a task completes before the deadline, its tardiness is 0.
Notes: Using the above definitions, we have dᵢ ≥ rᵢ + Cᵢ

## Slide 25: Example: Lateness
Which schedule is better depends on application requirements:
In (a), the maximum lateness is minimized with , but all jobs to miss their deadlines.
In (b), the maximal lateness is larger with , but only one job misses its deadline.

## Slide 26: Scheduling Algorithms
Static cyclic scheduling (offline)
  All task invocation times are computed offline and stored in a table; Runtime dispatch is a simple table lookup
Online scheduling;
  Fixed priority scheduling (also called static-priority scheduling)
    Each task is assigned a fixed priority; Runtime dispatch is priority-based, e.g., Rate Monotonic (RM), Deadline Monotonic (DM)
  Dynamic priority scheduling
    Task priorities are assigned dynamically at runtime, e.g., Earliest Deadline First (EDF), Least-Laxity First (LLF)
  Non-real-time scheduling, e.g., round-robin, multi-level queue…
RT scheduling algorithms
Static cyclic scheduling
(offline)
Online scheduling
Fixed-priority
(e.g., RM, DM)
Dynamic-priority
(e.g., EDF, LLF)

## Slide 27: Static Cyclic Scheduling
The same schedule is executed once during each hyper-period (least common multiple of all task periods in a taskset).
  The hyper-period is partitioned into frames of length f.
    If a task’s WCET exceeds f, then programmer needs to cut it to fit within a frame, and save/restore program state manually
  The schedule is computed offline and stored in a table. Runtime task dispatch is a simple table lookup.
Pros:
  Deals with precedence, exclusion, and distance constraints
  Efficient, low-overhead for runtime task dispatch
  Lock-free at runtime
Cons:
  Task table can get very large if task periods are relatively prime
  Maintenance nightmare: complete redesign when new tasks are added, or old tasks are deleted
Not widely used
  Except in certain safety-critical systems such as avionic systems
Notes: Execution timeline is an infinite sequence of hyper periods
Online monitoring and exception handling (babbling idiot prevention)
Advantages:
  Deals with precedence, exclusion, and distance constraints
  Efficient, low-overhead for runtime task dispatch
  Lock-free at runtime
  Online monitoring and exception handling (babbling idiot prevention)
Disadvantages:
  Not efficient for event-driven workload
  Maintenance nightmare
    Complete redesign when new tasks are added, or old tasks are deleted

## Slide 28
Fixed-Priority Scheduling

## Slide 29: Fixed Priority Scheduling
Each task is assigned a fixed priority for all its invocations
Pros:
  Predictability
  Low runtime overhead
  Temporal isolation during overload
Cons:
  Cannot achieve 100% utilization in general, except when task periods are harmonic
Widely used in most commercial RTOSes and CAN bus

## Slide 30: Rate Monotonic & Deadline Monotonic Scheduling
Rate Monotonic (RM)
  Assign higher priority to task with smaller period
  For implicit deadline tasksets (deadline D = period T), RM is the optimal priority assignment, i.e., if a taskset is not schedulable with RMS priority assignment, then it is not schedulable with any other fixed priority assignment
Deadline Monotonic (DM)
  Assign higher priority to task with smaller relative deadline
  For constrained deadline tasksets (D T), DM is the optimal priority assignment
Why do we want D < T?
  Some events happen infrequently, but need to be handled urgently
Example taskset:
0
50
0
100
25
75
2
0
40
80
100
3
1
0
50
0
100
25
75
2
0
40
80
100
3
1
RM Scheduling w/
DM Scheduling w/
(D2=15 indicated by red downward arrow for )
Notes: RTA also applies to DMS

## Slide 31: Two Schedulability Analysis Approaches
Utilization bound test
  Calculate total CPU utilization and compare it to a known bound
  Polynomial time complexity
  Pessimistic: sufficient but not necessary condition for schedulability
Response Time Analysis (RTA)
  Calculate Worst-Case Response Time Ri for each task Taui and compare it to its deadline Di
  Pseudo-polynomial time complexity
    An algorithm runs in pseudo-polynomial time if its running time is polynomial in the numeric value of the input (which is exponential in the length of the input – its number of digits).
  Accurate: necessary and sufficient condition for schedulability
IMPORTANT
Notes:     refers to a class of algorithms whose running time is polynomial in the numeric value of the input but not necessarily in the input size (the number of bits required to represent the input). This distinction arises because the numeric value of an input can be exponentially larger than its representation in bits.

## Slide 32: Utilization Bound Test
CPU%
100
90
80
70
60
50
40
30
20
10
0
1 2 3 4 5 6 7 8 9 10
69%
# tasks
RM UB Test
# Tasks | RM Util Bound
1 | 1.00
2 | 0.828
3 | 0.780
4 | 0.757
5 | 0.743
10 | 0.718
inf | 0.693
A taskset is schedulable under RM scheduling if system utilization
  as
  Assumptions: task period equal to deadline (); task with smaller period is assigned higher priority (RM priority assignment); tasks are independent (no resource sharing)
Sufficient but not necessary condition
  Guaranteed to be schedulable if test succeeds
  May still be schedulable even if test fails
Special case: if periods are harmonic (larger periods divisible by smaller periods), then utilization bound is 1 (necessary and sufficient condition)
IMPORTANT
Notes: (not deadline-monotonic!) Applies to rate-monotonic priority assignmentA taskset is schedulable under RM scheduling if its system utilization
  as
  Assumptions: task period equal to deadline (); task with smaller period is assigned higher priority (RM priority assignment); tasks are independent (no resource sharing)
(not deadline-monotonic!) Applies to rate-monotonic priority assignmentA taskset is schedulable under RM scheduling if its system utilization 𝑈=∑_(𝑖=1)^𝑁▒𝐶_𝑖/𝑇_𝑖 ≤𝑁(2^(1/𝑁)−1)
  𝑈→0.69 as 𝑁→∞
  Assumptions: task period equal to deadline (𝑃_𝑖=𝐷_𝑖); task with smaller period 𝑃_𝑖 is assigned higher priority (RM priority assignment); tasks are independent (no resource sharing)

## Slide 33: Utilization Bound Test Examples
0
9
18
6
12
0
18
3
3
6
9
15
deadline miss
12
15
6
12
0
18
3
9
15
Taskset 1 (3, 6, 6), 2 (4, 9, 9)
unschedulable
Taskset 1 (3, 6, 6), 2 (3, 9, 9)
schedulable (UB test is sufficient but not necessary condition)
Taskset 1 (2, 4, 4), 2 (4, 8, 8)
schedulable (periods are harmonic)
4
12
0
8
16
1
2
1
2
1
2
6
12
0
18
3
9
15
4
12
0
8
16
We use the notation i (Ci, Ti, Di) to denote task i with WCET Ci Period Ti, Deadline Di

## Slide 34: Response Time Analysis (RTA)
Assumptions:
  Consider the synchronous taskset: all tasks are initially released at time 0 simultaneously, called the critical instant. This is the worst-case when each task experiences maximum amount of interference from higher priority tasks: if the taskset is schedulable with this assumption, then it will be schedulable for any other release offset.
  No resource sharing (no critical sections)
  Figure shows task has the worst-case response time if it is initially released at time 0, simultaneously with higher priority task (lower figure)
initially released at time 0 simultaneously, the critical instant. experiences 3 preemptions by and has longer response time
initially released with a non-zero offset, not all at time 0. experiences 2 preemptions by and has shorter response time
Notes: Synchronous taskset: all tasks are released at time 0 simultaneously.
  This is the worst-case: if taskset is schedulable with this assumption, then it will be schedulable for any other release offset
  Let’s explain this equation with the example taskset

## Slide 35: Response Time Analysis (RTA)
For each task , compute its Worst-Case Response Time (WCRT) and compare to its deadline . is schedulable iff . The taskset is schedulable if all tasks are schedulable (necessary and sufficient condition. “iff” stands for “if and only if”).
Task ‘s WCRT is computed by solving the following recursive equation to find the minimum fixed-point solution:
  where is the set of tasks with higher priority than task .
  is the ceiling operator, e.g.,
  denotes the number of times HP task pre-empts during its one job execution; denotes the total preemption delay caused by HP task to during its one job execution
IMPORTANT
Notes: Synchronous taskset: all tasks are released at time 0 simultaneously.
  This is the worst-case: if taskset is schedulable with this assumption, then it will be schedulable for any other release offset
  Let’s explain this equation with the example taskset

## Slide 36: An Example Taskset
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
Consider a taskset of 3 task with () of . Under RM, task priorities are assigned to be High for T1, Medium for T2, and Low for T3
System Utilization =
  Utilization Bound
Utilization bound test fails, but taskset is actually schedulable

## Slide 37: Task T1
T1 is the highest priority task, with no interference from other tasks
, so T1 is schedulable
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
0
10
20
30
40
50
Time
Task
T1
T1

## Slide 38: Task T2
T2 is the medium priority task, with interference
from higher priority Task 1
Solve for iteratively, starting with initial value :
  Iteration 1:
  Iteration 2:
Hence , so T2 is schedulable
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
0
10
20
30
40
50
Time
Task
T1
T1
T2
T2

## Slide 39: Task T3
T3 is the lowest priority task, with interference
from higher priority tasks
Solve for iteratively, starting with initial value :
  Iteration 1:
  Iteration 2:
  Iteration 3:
  Iteration 4:
Hence , so T3 is schedulable
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
0
0
10
20
30
40
50
Time
T3
T3
Task
T1
T1
T2
T2

## Slide 40: RTA for T3: Initial Condition
Initially
We have not taken into account any preemption delays from higher priority tasks T1 and T2 yet
T2
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
0
10
20
30
40
50
Time
Task
T1
T1
T2
T2
T3
12

## Slide 41: RTA for Task 3: Iteration 1
T1 preempts T3 once, and T2 preempts T3 once
  since all 3 tasks are released at time 0 (synchronous release time assumption), and T1 and T2 have higher priority than T3
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
32
0
10
20
30
40
50
Time
Task
T1
T1
T2
T2
T3

## Slide 42: RTA for Task 3: Iteration 2
T1 preempts T3 twice, and T2 preempts T3 once
  Since T3 has not finished execution at time 30, and another job of higher priority task T1 is released at time 30 and preempts T3
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
0
10
20
30
40
50
Time
Task
T1
T1
T2
T2
T3
T3
42
Notes: R3 = 12 + ceil(32/30)*10 + ceil(32/40)*10 = 42

## Slide 43: RTA for Task 3: Iteration 3
T1 preempts T3 twice, and T2 preempts T3 twice
  Since T3 has not finished execution at time 40, and another job of higher priority task T2 is released at time 40 and preempts T3
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
0
10
20
30
40
50
Time
T3
T3
Task
T1
T1
T2
T2
52

## Slide 44: RTA for Task 3: Iteration 4
T1 preempts T3 twice, and T2 preempts T3 twice
  Since T3 has finished execution at time 52, and the next arrivals of T1 and T2 are at time 60 and 80, respectively, so T3 will not experience additional preemptions from T1 and T2
Now the recursive equation has converged, and we have obtained the WCRT of T3
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
0
10
20
30
40
50
Time
T3
T3
Task
T1
T1
T2
T2
52
Notes: 𝑅_3 = 52 ≤𝐷_3 = 52

## Slide 45: When T3 is Unschedulable
The recursive equation may not converge, i.e., a task’s WCRT may be infinity, e.g., suppose we change T2’s WCET to be 20, then:
Solve for iteratively, starting with initial value :
  Iteration 1:
  Iteration 1:
  Iteration 3:
  Iteration 4:
  …
Hence . This means that T3’s first job never finishes execution due to interferences by higher priority tasks, hence T3 is unschedulable
It is also possible for T3 to be unschedulable if converges but it exceeds its deadline , e.g., if we set , then (another job of T3 is released at time 50, but RTA for the current job is not affected by the newly-released job.)
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 20 | M
T3 | 52 | 12 | L
0
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 50 | 12 | L

## Slide 46: DM for Constrained Deadline Tasksets (D T)
Deadline monotonic (Fixed Priority):
  A task with smaller relative deadline gets higher priority
  For constrained deadline tasksets (D T), DM is the optimal priority assignment
  No Utilization Bound test for RM or DM, for tasksets with D T; must use Response Time Analysis (RTA)
  Consider a taskset with two tasks both with . Using RTA, assuming has higher priority (since task periods are equal, we can assign either task higher priority), we can determine , hence it is unschedulable
Notes: Schedulability analysis need to be changed (discussions omitted) but we can not use it to determine schedulability
Overhead: EDF typically exhibits less frequent preemptions ⇒ lower overhead
Overrun behavior (U > 1): EDF – automatic “period rescaling”, RM – complete blocking of lower priority tasks Transient: Task overrun can cause deadline miss of EDF: arbitrary task RM: only lower priority task If we don’t know which task will overrun, the result is the same. Jitter and latency: RM has no jitter only for the highest-priority task. In overall comparison, EDF provides better results (smaller release-time jitter a smaller input-output latency) Resource reservation: Simpler in case of EDF (see future lecture)

## Slide 47: RM vs. DM Example
Three tasks:
Under RM (or DM), priority ordering
Three tasks with assigned a smaller deadline of :
Under DM, priority ordering
0
3
6
9
12
0
3
6
9
12

## Slide 48
Earliest Deadline First (EDF) Scheduling

## Slide 49: Earliest Deadline First (EDF)
As each jon enters the system, it is assigned a deadline, and its priority is determined by its absolute deadline
  The job with the earlier deadline is assigned the higher priority
  This priority assignment is dynamic because a periodic task’s priority changes for each job released by the task (vs. fixed-priority scheduling, where a periodic task is assigned a fixed priority for all its jobs)
Pros:
  Optimal: can achieve 100% CPU utilization
Cons:
  Poor temporal isolation during overload
  c.f. RM vs. EDF: Robustness under Overload
Notes: EDF minimizes lateness of the “most tardy task” [Dertouzos, 1974] High runtime overhead for managing ready
Earliest Deadline First (EDF)
  Each job is assigned a deadline upon its arrival
  Task with earlier deadline is assigned higher priority
    Pros: can achieve 100% utilization
    Cons: high runtime overhead, lack of temporal protection for HP tasks

## Slide 50: EDF Scheduling Example
Say you have two tasks, both released at time 0
  T1 has WCET 5 ms, with deadline of 20 ms
  T2 has WCET 10 ms, with deadline of 12 ms
Non-EDF scheduling: T1 before T2, T2 misses its deadline at 12
EDF scheduling: T2 before T1, both tasks meet their deadlines
T1
T2
0
5
15
T2 Deadline
T2
T1
0
5
15
T1 Deadline
20
20
T1 before T2
T2 before T1
  Convention: Upwards arrows indicate arrival time; Downwards arrows indicate deadline
Notes: This is a simple example of EDF. Since it’s not widely used in the auto industry, we will not consider it further.

## Slide 51: Schedulable Utilization Bound: EDF vs. RM
CPU%
100
90
80
70
60
50
40
30
20
10
0
69%
RM
EDF
100%
1 2 3 4 5 6 7 8 9 10
# tasks
The schedulable utilization bound for EDF Scheduling is 1 (necessary and sufficient condition):
  A taskset is schedulable under EDF scheduling iff system utilization does not exceed 1
    “iff” stands for “if and only if”
  Assumptions: task period equal to deadline (); tasks are independent (no resource sharing)
Recall: schedulable utilization bound for Fixed-Priority scheduling (sufficient but not necessary condition):
  A taskset is schedulable under RM scheduling if system utilization
  as
IMPORTANT

## Slide 52: RM vs. EDF Example
0
9
18
6
12
0
18
3
3
6
9
15
deadline miss
12
15
Under RM (Fixed-Priority scheduling), all jobs of (with smaller period T=6) have higher priority than all jobs of (with larger period T=9). Taskset unschedulable with RM
1
2
0
9
18
6
12
0
18
3
3
6
12
9
15
15
1
2
Under EDF (Dynamic Priority scheduling), different jobs of and may have different priorities, depending on their absolute deadlines , which is different for each newly-released job every period. Taskset schedulable with EDF
Task | T=D | C
 | 6 | 3
 | 9 | 4
Task | T=D | C
 | 6 | 3
 | 9 | 4
>
>
>
priority
>
>
priority
>
=
When two jobs have equal priority, the newly arrived job does not preempt the running job
Notes: L6-Exercises ANS.pptx p7 illustrates that, EDF uses absolute deadline di, which is different for each job, where DM/RM uses relative deadline Di, which is a static param that never changes, for setting priority of each job

## Slide 53: RM vs. EDF: Robustness under Overload
Under permanent overload, with CPU utilization U > 1
  Under EDF, all tasks execute at a slower rate with “period rescaling”, i. e., all tasks are delayed evenly
  Under RM, higher priority tasks are protected while lower priority tasks are delayed or complete blocked
  Recall Slide 25 Example Lateless
Under transient overload, when some job overruns (executes longer than expected temporarily)
  Under EDF, task overruns can cause deadline miss of arbitrary task
  Under RM: task overruns only affect lower priority tasks
Conclusion: RM offers better temporal isolation for higher priority tasks, at the expense of lower priority tasks
Notes: Not transient overload
  This occurs

## Slide 54: EDF Period Rescaling
Theorem on Period Rescaling [Cervin et al. 2003]:
  If system utilization , tasks are executed with an average period under EDF scheduling

## Slide 55: EDF for Constrained Deadline Tasksets (D T)
Earliest Deadline First (Dynamic-Priority):
  A task with smaller absolute deadline gets higher priority
  EDF is still optimal, but instead of Utilization Bound, we use Density Bound to determine schedulability
  Density of task is defined as . Taskset is schedulable if system density does not exceed 1: (sufficient but not necessary condition)
    (Demand Bound Function can be used as necessary and sufficient condition (not covered))
  Consider a taskset with two tasks both with . It is obviously unschedulable under any scheduling algo. System utilization is ; System density . But we cannot determine schedulabiity based on .
  Consider a taskset with two tasks . . Yet the taskset is schedulable under EDF:
IMPORTANT

## Slide 56: Summary of Schedulability Analysis Algorithms
 | Fixed-Priority Scheduling |  | Dynamic Priority Scheduling | 
Optimal Scheduling Algorithm | Rate Monotonic (RM) Scheduling for implicit deadline taskset (D=T) | Deadline Monotonic (DM) Scheduling for constrained deadline taskset (DT) | Earliest Deadline First (EDF) Scheduling for implicit deadline taskset (D=T) | Earliest Deadline First (EDF) Scheduling for constrained deadline taskset (DT)
Schedulability Analysis Algorithm | Utilization Bound (UB) test (sufficient condition) or Response Time Analysis (RTA) (necessary and sufficient) | RTA Response Time Analysis (RTA) (necessary and sufficient) | Utilization Bound (UB) test (necessary and sufficient) | Density Bound test (sufficient condition) or Demand Bound Function (not covered)
 | Fixed-Priority Scheduling |  | Dynamic Priority Scheduling | 
Optimal Scheduling Algorithm | Rate Monotonic (RM) Scheduling for implicit deadline taskset (D=T) |  | Earliest Deadline First (EDF) Scheduling for implicit deadline taskset (D=T) | 
Schedulability Analysis Algorithm |  |  |  | 
IMPORTANT

## Slide 57
Least Laxity First (LLF) Scheduling

## Slide 58: Least Laxity First (LLF) Scheduling
LLF assigns priority to jobs dynamically based on their current laxity (slack)
  With absolute deadline and remaining execution time , laxity of ’s job at time is . Job with the smallest laxity has the highest priority
  While an active job waits and does not run, its laxity decreases and its priority increases until it becomes the highest priority job and starts to run
  If an active job runs in the previous time slot, then its laxity remains the same, as is incremented by 1, and is decremented by 1
  If an active job does not run in the previous time slot, then its laxity is decremented by 1, as is incremented by 1, and remains the same
Analogy: suppose you have an assignment that is due in 5 hours at 12:00, and it takes =3 hours to complete. Current time is =7:00, so the current laxity is =12−7−3=2.
  If you work for an hour until =8:00, then the laxity remains the same: =12−8−2=2, since the remaining execution time is decremented by 1: =3-1=2
  If you sleep for an hour until =8:00, then the laxity is decremented by 1: =12−8−3=1, since the remaining execution time does not change: =3
  If you sleep for 2 hours until =9:00, then the laxity is now 0: =12−9−3=0. Your must give the assignment the highest priority and start working on it right away, otherwise you will miss the deadline
EDF and LLF are both optimal scheduling algorithms, i.e., they both have schedulable utilization bound of 1
  LLF incurs frequent context switches, hence is less practical than EDF
t

## Slide 59: RM, EDF, LLF Example
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Time
Task
T1
T2
Task | T=D | C
T1 | 5 | 2
T2 | 6 | 3
T1
T2
T1
Time | τ₁ Laxity | τ₂ Laxity | Running Task
t=0 | 5-0-2=3 | 6-0-3=3 | (tie)
t=1 | 5-1-1=3 | 6-1-3=2 | 
t=2 | 5-2-1=2 | 6-2-2=2 | (tie)
t=3 | 5-3-1=1 | 6-3-1=2 | 
t=4 | done | 6-4-1=1 | 
t=5 | 10-5-2=3 | done | 
t=6 | 10-6-1=3 | 12-6-3=3 | (tie)
t=7 | done | 12-7-3=2 | 
Time | τ₁ Laxity | τ₂ Laxity | Running Task
t=0 | 5-0-2=3 | 6-0-3=3 | 
t=1 | 5-1-1=3 | 6-1-3=2 | 
t=2 | 5-2-1=2 | 6-2-2=2 | 
t=3 | 5-3-1=1 | 6-3-1=2 | 
t=4 |  | 6-4-1=1 | 
t=5 | 10-5-2=3 |  | 
t=6 | 10-6-1=3 | 12-6-3=3 | 
t=7 |  | 12-7-3=2 | 
T2
T1
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Time
Task
T1
T2
T1
T1
T2
EDF and RM have the same schedule
LLF has more frequent context switches

## Slide 60
Preemptive vs. Non-Preemptive Scheduling

## Slide 61: Preemptive vs. Non-Preemptive Scheduling
Non-preemptive scheduling pros:
  It reduces runtime overhead
    Less context switches
    No mutex locks needed for critical sections
  It preserves program locality, improving the effectiveness of CPU cache
    As a result, task WCET becomes smaller and execution time distribution becomes more predictable (shown on right)
  Sometimes NP scheduling can improve schedulability
Cons:
  Reduced schedulability
  Scheduling anomalies
Preemptive scheduling pros:
  Better schedulability (higher CPU utilization)
Cons:
  Runtime overhead due to frequent context-switches
  Destroys program locality so task WCET becomes larger
Notes:   Pipeline mechanisms, Prefetch queues
  It reduces stack size, since no more than one task can be active, and tasks can share the same stack space

## Slide 62: Sometimes NP Scheduling Improves Schedulability
An example where NP scheduling improves schedulability (for fixed-priority scheduling)

## Slide 63: Disadvantage of NP Scheduling: Reduced Schedulability
In general, NP scheduling reduces schedulability. The utilization bound under NP scheduling drops to zero due to blocking time
An example with with two tasks T1 and T2, CPU utilization of nearly 0, yet unschedulable.
  If (WCET of T2) (period of T1), then the taskset is unschedulable with arbitrarily small system CPU utilization (when goes to 0 and goes to infinity)
  This example is valid whether or has higher priority: even if has higher priority, it may be released very shortly after is released at time 0, and it has to wait for to finish due to NP scheduling
T1
T2
Notes: Non preemption reduces schedulability (analysis must take blocking times into account); Non preemption reduces schedulability (analysis must take blocking times into account);
Schedulable utilization bound drops to zero.
  Here is an example with CPU utilization of nearly 0, yet unschedulable.

## Slide 64: Disadvantage of NP Scheduling: Scheduling Anomalies
Scheduling anomaly: three tasks under NP fixed-priority scheduling witjh priority ordering and NP
Doubling the processor speed (reducing task execution times by half) makes task miss its deadline, since starts earlier before is released, causing a long delay to it due to NP scheduling (this anomaly does not occur for preemptive scheduling)
Notes: I have given an overview of the basic concepts of real-time scheduling
Focus on static priority scheduling
Commercial tools from TimeSys and Tripac Software make it easier to do schedulability analysis
  However, it is good to know the internals of these tools

## Slide 65: Online Resources
Priority-Driven Scheduling, Marilyn Wolf
  https://www.youtube.com/watch?v=zSgr_oFmjqI&list=PLzwefUCNStZsmz5fWPVwVvTo1iPeGmG9M&index=4
RMS and EDF, Marilyn Wolf
  https://www.youtube.com/watch?v=oHMC2aO8GII&list=PLzwefUCNStZsmz5fWPVwVvTo1iPeGmG9M&index=5
Real-Time Scheduling Models, Marilyn Wolf (long)
  https://www.youtube.com/watch?v=WloSQ7ZEKXk