## Slide 1: CSC 112: Computer Operating Systems Lecture 6 Real-Time Scheduling
Department of Computer Science,
Hofstra University
Acknowledgement: Lecture slides based on UC Berkeley CS 162: Operating Systems and System Programming

## Slide 2: Outline
Introduction to RTOS and Real-Time Scheduling
Fixed-Priority Scheduling
Earliest Deadline First Scheduling
Resource Synchronization Protocols (for Fixed-Priority Scheduling)
Preemptive vs. Non-Preemptive Scheduling
Multiprocessor Scheduling

## Slide 3
Introduction to RTOS and Real-Time Scheduling

## Slide 4: Embedded Control Systems
An embedded control system co´nsists of:
  The system-under-control (SUT)
    may include sensors and actuators
  The controller/computer
    sends signals to the system according to a predetermined control objective
In the old days, each control task runs on a dedicated CPU
  No RTOS, bare metal
  No need for scheduling
  Just make sure that task execution time < deadline
Now, multiple control tasks share one CPU
  Multitasking RTOS
  Need scheduling to make sure all tasks meet deadlines
Controller/computer
actuators
D/A
SUT
sensors
A/D
Thread (task)
Resource

## Slide 5: Requirements
The tight interaction with the environment requires the system to react to events within precise timing constraints
Timing constraints are imposed by the dynamics of the environment
The real-time operating system (RTOS) must be able to execute tasks within timing constraints

## Slide 6: A Robot Control Example
Consider a robot equipped with:
  two actuated wheels
  two proximity (US) sensors
  a mobile (pan/tilt) camera
  a wireless transceiver
Goal:
  follow a path based on visual feedback
  avoid obstacles
visual−based navigation
visual tracking
obstacle avoidance
10 ms
100 ms
object recognition
mot_dx
mot_sx
pan
tilt
camera
US1 US2
1 ms
vehicle control
5 ms
20 ms
feature extraction
motor control
motor control
motor control
motor control
1 ms
Notes: send complete robot status every 20 ms

## Slide 7: Real-Time Systems
A computer system that is able to respond to events within precise timing constraints
A system where the correctness depends not only on the output values, but also on the time at which results are produced
A real-time system is not a necessarily a real fast system
  Speed is always relative to a specific environment
  Running faster is good, but does not guarantee hard real-time constraints
The objective of a real-time system is to guarantee the worst-case timing behaviour of each individual task
The objective of a fast system is to optimize the average-case performance
  A system with fast average-case performance may not meet worst-case requirements, e..g.,
  There was a person who drowned in a river with average depth of 6 inches
x (t)
RT system Environment
t
y (t+)
Notes: response time of a task set.

## Slide 8: RTOS Requirements
Timeliness: results must be correct not only in their value but also in the time domain
  provide kernel mechanism for time management and for handling tasks with explicit timing constraints and different criticality
Predictability: system must be analyzable to predict the consequences of any scheduling decision
  if some task cannot be guaranteed within time constraints, system must notify this in advance, to handle the exception (plan alternative actions)
Efficiency: operating system should optimize the use of available resources (computation time, memory, energy)
Robustness: must be resilient to peak-load conditions
Fault tolerance: single software/hardware failures should not cause the system to crash
Maintainability: modular architecture to ensure that modifications are easy to perform

## Slide 9: Sources of Nondeterminism
Architecture
  cache, pipelining, interrupts, DMA
Operating System (our focus in this lecture)
  scheduling, synchronization, communication
Language
  lack of explicit support for time
Design Methodologies
  lack of analysis and verification techniques

## Slide 10: Task
The concept of concurrent tasks reflects the intuition about the functionality of embedded systems.
  Task here can refer to either process or thread, depending on the underlying RTOS support
Tasks help us manage timing complexity:
  multiple execution rates
    multimedia
    automotive
  asynchronous input
    user interfaces
    communication systems
“activation” = “arrival” = “request” = “release” time
Task i
activation time ai
start time si
finish time fi
Execution time Ci
CPU
activation
dispatching termination
Ready queue
3 2 1

## Slide 11: Schedule
A specific assignment of tasks to the processor that determines the task execution sequence. Formally:
Given a task set , a schedule is a function that associates an integer to each time slice with the meaning:
  : in the processor is idle
  : in the processor executes
At times t1, t2,…: context switch to a different task
1 2 3
idle
idle
(t)
3
2
1
0
t
t3
t4
t1 t2
Notes: Deciding the order of a set of tasks with certain known characteristics (periodicity, execution time) on a limited set of processing units, subject to a set of constraints on the completion time of each task.

## Slide 12: Preemptive vs. Nonpreemptive Scheduling
priority
1
2
3
(t)
3
2
1
0
0
2
4
6
8 10 12 14 16 18 20
0
2
4
6
8 10 12 14 16 18 20
A scheduling algorithm is:
  preemptive: if the active job can be temporarily suspended to execute a more important job
  non-preemptive: if the active job cannot be suspended, i.e., always runs to completion
Preemptive scheduling example
Notes:  + Exception handling: timely response to issues
Different levels of importance or criticality: preemption executes most critical tasks
Running tasks may be suspended and placed in the ready queue

## Slide 13: Definitions
Feasible schedule
  A schedule is said to be feasible if all the tasks can complete according to a set of specified constraints.
Schedulable set of tasks
  A set of tasks is said to be schedulable if there exists at least one algorithm that can produce a feasible schedule for it.
Hard real-time task: missing deadline may have catastrophic consequences, so deadline violations are not permitted. A system able to handle hard real-time tasks is a hard real-time system
  sensory acquisition
  low-level control
  sensory-motor planning
Soft real-time task: missing deadlines causes Quality-of-Service(QoS)/performance degradation, so deadline violations are expected and permitted
  reading data from the keyboard—user command interpretation
  message displaying
  graphical activities
Notes: Deciding the order of a set of tasks with certain known characteristics (periodicity, execution time) on a limited set of processing units, subject to a set of constraints on the completion time of each task.
Hard Real-Time System if it can handle hard tasks
HARD tasks
  All jobs must meet their deadlines. Missing deadlines may cause catastrophic consequences.
  e.g., sensor reading, motor control.
SOFT tasks
  Missing deadlines is not desirable but causes only Quality-of-Service(QoS) degradation.
  e.g., reading data from keyboard, user command interpretation, message display
A system able to handle HARD tasks is a hard real-time system

## Slide 14: Real-Time Task
t
fi
d
i
relative deadline Di
i
ai si
response time Ri
absolute deadline (di = ai + Di)
A task characterized by a timing constraint on its response time, called deadline:
  relative deadline : part of task attribute definition, measured from task arrival time ai
  Absolute deadline : measured from some absolute reference time point 0
Definition: feasible task
  A real-time task is said to be feasible if it completes within its absolute deadline, that is, if , or, equivalently, if
Notes: “Completion time” = fi - si = Ri – (si- ai)

## Slide 15: Tasks and Jobs
A task running several times on different input data generates a sequence of instances (jobs)
  Upwards arrow: task arrival or release times; downwards arrow: task deadlines
Activation mode:
  Periodic tasks: the task is activated by the operating system at predefined time intervals
  Aperiodic tasks: the task is activated at an event arrival
Job 1
i,1
Job 2
i,2
Job 3
i,3
ai,k
ai,k+1
t
i
Ci
ai,1
Notes: Time-driven

## Slide 16: Estimating WCET is Not Easy
Each job operates on different data and can take different paths.
Even for the same data, computation time depends on the processor state (cache, prefetch queue, number of preemptions).
We use to denote Worst-Case Execution Time (WCET) in this lecture, and assume it is given as part of task parameters.
?
Distribution
(probability density function)
loop
?
?
execution time
Ci
min
Ci
max
timer

## Slide 17: Predictability/Safety vs. Efficiency
execution time
Ci
min
Ci
max
Ci
avg
Ci estimate
safe
efficient
unsafe
Tradeoff between safety and efficiency in estimating the WCET
  Setting a large achieves high predictability and safety, since it is unlikely to be exceeded at runtime; but it hurts efficiency, since the system needs to reserve more CPU time for the task. Suitable for hard real-time tasks.
  Setting a small achieves high efficiency, but hurts safety, since the task may execute for more than its estimate. Suitable for soft real-time tasks.
Distribution
(probability density function)
Notes: where deadline violations may cause severe consequencesIt is a parameter related to the consequences of missing the deadline
  Hard: missing deadline may have catastrophic consequences
  Hard Real-Time System if it can handle hard tasks
    sensory acquisition
    low-level control
    sensory-motor planning
  Soft: missing a deadline causes performance degradation
    reading data from the keyboard—user command interpretation
    message displaying
    graphical activities
Value, vi = the relative importance of a task wrt other tasks

## Slide 18: Jitter
It is a measure of the time variation of a periodic event:
fi,1
Finish-time Jitter
i
fi,2
fi,3
si,1
Start-time Jitter
i
si,1 si,2 si,3
Completion-time Jitter (I/O Jitter)
i
si,2
si,3
fi,2
fi,1
fi,3
Notes: max (tk – ak) – min (tk – ak)
k k
max | (tk – ak) – (fk-1 – ak-1) |

## Slide 19: Periodic Task
A periodic task has a tuple of 3 attributes ():
  Worst-Case Execution Time (WCET): ; Period ; Relative Deadline
It generates an infinite sequence of jobs in every period:
Ti
job ik
ai,k
ai,k+1
i (Ci , Ti , Di )
Ci
t
ai,1 = i
task phase or
Release offset
ai,k di,k
= i + (k1) Ti
= ai,k + Di
often
Di = Ti
input
C
i
wait()
timer (period Ti )
output
A job of task
Multiple jobs released by task
Notes: Consider a periodic task τ1(C1,T1,D1) with phase Φ1, where:
  C1 = 10 ms, T1 = 50 ms, D1 = 25 ms, and Φ1 = 100 ms
What is τ1’s utilization factor?
Is τ1 feasible?
What is τ1,1’s absolute deadline?
What is τ1,1’s laxity?
What is τ1,2’s release time?
Can τ1,1 and τ1,2 have different laxity?
Can τ1,1 and τ1,2 have different slack?
If τ1,2’s slack is 10ms, what is τ1,s’s finishing time?
What is τ1,2’s response time?
With a 2-CPU machine, can τ1,2 and τ1,3 have the same release time?
Can τ1,2 and τ1,3 have the same finishing time?

## Slide 20: Aperiodic & Sporadic Task
Aperiodic task: jobs may arrive at arbitrary time instants
Sporadic task: arrival times with a minimum interarrival time constraint
Aperiodic:
ai,k+1 > ai,k
minimum interarrival time
Sporadic:
ai,k+1
 ai,k + Ti
Ci
job ik
Ci
Ci
ai,k
ai,k+1
t
i
ai,1

## Slide 21: Types of Constraints
Timing constraints
  Deadline, jitter.
Precedence constraints
  Relative ordering among task executions.
Resource constraints
  Synchronization when accessing mutually-exclusive resources (shared data).

## Slide 22: Precedence Constraints
Tasks must be executed with specific precedence relations, specified by a Directed Acyclic Graph (Precedence Graph)
Example application of parts inspection in a factory. Tasks:
  Image acquisition (acq1, acq2)
  Edge detection (edge1, edge2)
  Shape detection (shape), pixel disparities (disp)
  Height determination (height), recognition (rec)
stereo vision
processing
recognition
acq1
acq2
edge1
edge2
shape
disp
depth
rec
Notes: Precedence graph?

## Slide 23: Resource Constraints
To ensure data consistency, shared data must be accessed in mutual exclusion
Example: the writer task writes to variables and ; the reader task reads and . The pair of variables should be updated atomically, i.e., should read either or .
Left upper: an erroneous scenario when τR reads a set of inconsistent values .
Left lower: protecting the critical section (yellow parts) with a mutex lock ensures atomicity.
x = 3
y = 5
W
R
x = 1
y = 8
x = 1
y = 5
W
R
x=1
y=8
read
x = 3
y = 5
x = 1
y = 8
x = 1
y = 8
W
R
x = 1
y = 8
W
R

read
Erroneous scenario with no lock protection
Correct scenario with lock protection

## Slide 24: Scheduling Metrics
Lateness Lᵢ = fᵢ − dᵢ represents the delay of a task completion with respect to its deadline; note that if a task completes before the deadline, its lateness is negative.
Tardiness or exceeding time Eᵢ = max(0, Lᵢ) is the time a task stays active after its deadline.
Laxity or slack time Xᵢ = dᵢ − aᵢ − Cᵢ is the maximum time a task can be delayed on its activation to complete within its deadline.
Notes: Using the above definitions, we have dᵢ ≥ rᵢ + Cᵢ

## Slide 25: Scheduling Metrics
Lateness represents the delay of a task completion with respect to its deadline; note that if a task completes before the deadline, its lateness is negative.
Tardiness or exceeding time is the time a task stays active after its deadline.
Laxity or slack time is the maximum time a task can be delayed in order to complete within its deadline.
Notes: Using the above definitions, we have dᵢ ≥ rᵢ + Cᵢ

## Slide 26: Example: Lateness
Which schedule is better depends on application requirements:
In (a), the maximum lateness is minimized, but all jobs to miss their deadlines.
In (b), the maximal lateness is larger, but only one job misses its deadline.

## Slide 27: Scheduling Approaches
Static cyclic scheduling
  All task invocation times are computed offline and stored in a table
  Runtime dispatch is a simple table lookup
Fixed priority scheduling
  Each task is assigned a fixed priority
  Runtime dispatch is priority-based
Dynamic priority scheduling
  Task priorities are assigned dynamically at runtime
  e.g., Earliest Deadline First (EDF), Least-Laxity First (LLF)

## Slide 28: Static Cyclic Scheduling
The same schedule is executed once during each hyper-period (least common multiple of all task periods in a taskset).
  The hyper-period is partitioned into frames of length f.
    If a task’s WCET exceeds f, then programmer needs to cut it to fit within a frame, and save/restore program state manually
  The schedule is computed offline and stored in a table. Runtime task dispatch is a simple table lookup.
Pros:
  Deals with precedence, exclusion, and distance constraints
  Efficient, low-overhead for runtime task dispatch
  Lock-free at runtime
Cons:
  Task table can get very large if task periods are relatively prime
  Maintenance nightmare: complete redesign when new tasks are added, or old tasks are deleted
Not widely used
  Except in certain safety-critical systems such as avionic systems
Notes: Execution timeline is an infinite sequence of hyper periods
Online monitoring and exception handling (babbling idiot prevention)
Advantages:
  Deals with precedence, exclusion, and distance constraints
  Efficient, low-overhead for runtime task dispatch
  Lock-free at runtime
  Online monitoring and exception handling (babbling idiot prevention)
Disadvantages:
  Not efficient for event-driven workload
  Maintenance nightmare
    Complete redesign when new tasks are added, or old tasks are deleted

## Slide 29
Fixed-Priority Scheduling

## Slide 30: Fixed Priority Scheduling
Each task is assigned a fixed priority for all its invocations
Pros:
  Predictability
  Low runtime overhead
  Temporal isolation during overload
Cons:
  Cannot achieve 100% utilization in general, except when task periods are harmonic
Widely used in most commercial RTOSes and CAN bus

## Slide 31: Rate Monotonic & Deadline Monotonic Scheduling
Rate Monotonic Scheduling (RMS)
  Assign higher priority to task with smaller period
  When D = T, RMS is the optimal priority assignment, i.e., if a taskset is not schedulable with RMS priority assignment, then it is not schedulable with any other fixed priority assignment
Deadline Monotonic Scheduling (DMS)
  Assign higher priority to task with smaller relative deadline (indicated by red downward arrow for )
  When D < T, DMS is the optimal priority assignment
Why do we want deadline < period?
  Some events happen infrequently, but need to be handled urgently
0
50
0
100
25
75
2
0
40
80
100
3
1
0
50
0
100
25
75
2
0
40
80
100
3
1
Notes: RTA also applies to DMS

## Slide 32: Two Schedulability Analysis Approaches
Utilization bound test
  Calculate total CPU utilization and compare it to a known bound
  Polynomial time complexity
  Pessimistic: sufficient but not necessary condition for schedulability
Response Time Analysis (RTA)
  Calculate Worst-Case Response Time Ri for each task Taui and compare it to its deadline Di
  Pseudo-polynomial time complexity
    An algorithm runs in pseudo-polynomial time if its running time is polynomial in the numeric value of the input (which is exponential in the length of the input – its number of digits).
  Accurate: necessary and sufficient condition for schedulability
Notes:     refers to a class of algorithms whose running time is polynomial in the numeric value of the input but not necessarily in the input size (the number of bits required to represent the input). This distinction arises because the numeric value of an input can be exponentially larger than its representation in bits.

## Slide 33: Utilization Bound Test
A taskset is schedulable under RM scheduling if its total utilization
  as
  Assumptions: task period equal to deadline (); task with smaller period is assigned higher priority (RM priority assignment); tasks are independent (no resource sharing)
Sufficient but not necessary condition
  Guaranteed to be schedulable if test succeeds
  May still be schedulable even if test fails
  If periods are harmonic (larger periods divisible by smaller periods), then utilization bound is 1
CPU%
100
90
80
70
60
50
40
30
20
10
0
1 2 3 4 5 6 7 8 9 10
69%
# tasks
RM UB Test
# Tasks | Bound
1 | 1.00
2 | 0.828
3 | 0.780
4 | 0.757
5 | 0.743
10 | 0.718
inf | 0.693
Notes: (not deadline-monotonic!) Applies to rate-monotonic priority assignmentA taskset is schedulable under RM scheduling if its total utilization
  as
  Assumptions: task period equal to deadline (); task with smaller period is assigned higher priority (RM priority assignment); tasks are independent (no resource sharing)
(not deadline-monotonic!) Applies to rate-monotonic priority assignmentA taskset is schedulable under RM scheduling if its total utilization 𝑈=∑_(𝑖=1)^𝑁▒𝐶_𝑖/𝑇_𝑖 ≤𝑁(2^(1/𝑁)−1)
  𝑈→0.69 as 𝑁→∞
  Assumptions: task period equal to deadline (𝑃_𝑖=𝐷_𝑖); task with smaller period 𝑃_𝑖 is assigned higher priority (RM priority assignment); tasks are independent (no resource sharing)

## Slide 34: Utilization Bound Test Examples
0
9
18
6
12
0
18
3
3
6
9
15
deadline miss
12
15
6
12
0
18
3
9
15
Taskset non-schedulable
Taskset schedulable (UB test is sufficient but not necessary condition)
Taskset schedulable (periods are harmonic)
4
12
0
8
16
1
2
1
2
1
2
6
12
0
18
3
9
15
4
12
0
8
16

## Slide 35: Response Time Analysis (RTA)
Assumptions:
  No resource sharing (no critical sections)
  Consider the synchronous taskset: all tasks are initially released at time 0 simultaneously, called the critical instant. This is the worst-case: if the taskset is schedulable with this assumption, then it will be schedulable for any other release offset.
  Figure shows task has longer response time when released at time 0, the critical instant, simultaneously with higher priority task
Notes: Synchronous taskset: all tasks are released at time 0 simultaneously.
  This is the worst-case: if taskset is schedulable with this assumption, then it will be schedulable for any other release offset
  Let’s explain this equation with the example taskset

## Slide 36: Response Time Analysis (RTA)
For each task , compute its Worst-Case Response Time (WCRT) and compare to its deadline . is schedulable if
The taskset is schedulable of all tasks are schedulable.
WCRT is computed by solving the following recursive equation:
  where is the set of tasks with higher priority than task .
  is the ceiling operator, e.g.,
Notes: Synchronous taskset: all tasks are released at time 0 simultaneously.
  This is the worst-case: if taskset is schedulable with this assumption, then it will be schedulable for any other release offset
  Let’s explain this equation with the example taskset

## Slide 37: An Example Taskset
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
Utilization =
Utilization bound
Utilization bound test fails since 0.81 > 0.78
But taskset is actually schedulable

## Slide 38: Schedule Timeline
0
10
20
30
40
50
T1
T1
Time
T2
T2
T3
If each task runs on a dedicated CPU on a multiprocessor platform:
If all tasks share a single CPU:
0
10
20
30
40
50
T1
T1
Time
T2
T2
T3
T3
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
Task
Task

## Slide 39: Task T1
T1 is the highest priority task, with no interference from other tasks
, so T1 is schedulable
0
10
20
30
40
50
T1
T1
Time
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
Task

## Slide 40: Task T2
T2 is the medium priority task, with interference
from higher priority Task 1
Solve for recursively, starting with initial value :
  Iteration 1:
  Iteration 2:
Hence , so T2 is schedulable
0
10
20
30
40
50
T1
T1
Time
T2
T2
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
Task

## Slide 41: Task T3
T3 is the lowest priority task, with interference
from higher priority tasks
Solve for recursively, starting with initial value :
  Iteration 1:
  Iteration 3:
  Iteration 4:
Hence , so T3 is schedulable
0
10
20
30
40
50
T1
T1
Time
T2
T2
T3
T3
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
0
Task
Notes: Task
T
D
C
Prio
1
30
30
10
H
2
40
40
10
M
3
52
52
12
L

## Slide 42: RTA for T3: Initial Condition
Initially
We have not taken into account any preemption delays from higher priority tasks 1 and 2 yet
0
10
20
30
40
50
T1
T1
Time
T2
T2
T3
12
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
Task

## Slide 43: RTA for Task 3: Iteration 1
T1 preempts T3 once, and T2 preempts T3 once
  since all 3 tasks are released at time 0 (synchronous release time assumption), and T1 and T2 have higher priority than T3
0
10
20
30
40
50
T1
T1
Time
T2
T2
T3
32
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
Task

## Slide 44: RTA for Task 3: Iteration 2
T1 preempts T3 twice, and T2 preempts T3 once
  Since T3 has not finished execution at time 30, and another job of higher priority task T1 is released at time 30 and preempts T3
0
10
20
30
40
50
T1
T1
Time
T2
T2
T3
42
T3
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
Task
Notes: R3 = 12 + ceil(32/30)*10 + ceil(32/40)*10 = 42

## Slide 45: RTA for Task 3: Iteration 3
T1 preempts T3 twice, and T2 preempts T3 twice
  Since T3 has not finished execution at time 40, and another job of higher priority task T2 is released at time 40 and preempts T3
0
10
20
30
40
50
T1
T1
Time
T2
T2
T3
52
T3
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
Task

## Slide 46: RTA for Task 3: Iteration 4
T1 preempts T3 twice, and T2 preempts T3 twice
  Since T3 has finished execution at time 52, and the next arrivals of T1 and T2 are at time 60 and 80, respectively, so T3 will not experience additional preemptions from T1 and T2
Now the recursive equation has converged, and we have obtained the WCRT of T3 to be
0
10
20
30
40
50
T1
T1
Time
T2
T2
T3
52
T3
Task | T=D | C | Prio
T1 | 30 | 10 | H
T2 | 40 | 10 | M
T3 | 52 | 12 | L
Task

## Slide 47
Earliest Deadline First (EDF) Scheduling

## Slide 48: Earliest Deadline First (EDF)
As each task enters the system, it is assigned a deadline, and its priority is determined by its absolute deadline
  The task with the earlier deadline is assigned the higher priority
Pros:
  Optimal: can achieve 100% CPU utilization
Cons:
  High runtime overhead
  Poor temporal isolation during overload
Notes: Earliest Deadline First (EDF)
  Each job is assigned a deadline upon its arrival
  Task with earlier deadline is assigned higher priority
    Pros: can achieve 100% utilization
    Cons: high runtime overhead, lack of temporal protection for HP tasks

## Slide 49: EDF Scheduling Example
Say you have two tasks, both released at time 0
  T1 has WCET 5 ms, with deadline of 20 ms
  T2 has WCET 10 ms, with deadline of 12 ms
Non-EDF scheduling: T1 before T2, T2 misses its deadline at 12
EDF scheduling: T2 before T1, both tasks meet their deadlines
T1
T2
0
5
15
T2 Deadline
T2
T1
0
5
15
T1 Deadline
20
20
T1 before T2
T2 before T1
Notes: This is a simple example of EDF. Since it’s not widely used in the auto industry, we will not consider it further.

## Slide 50: Schedulable Utilization Bound: RM vs. EDF
Recall the schedulable utilization bound for Fixed-Priority scheduling:
A taskset is schedulable under RM scheduling if its total utilization
  as
The schedulable utilization bound for EDF Scheduling is 1:
  A taskset is schedulable under EDF scheduling if its total utilization
  Assumptions: task period equal to deadline (); tasks are independent (no resource sharing)
CPU%
100
90
80
70
60
50
40
30
20
10
0
69%
RM
EDF
100%
1 2 3 4 5 6 7 8 9 10
# tasks

## Slide 51: RM vs. EDF Example
0
9
18
6
12
0
18
3
3
6
9
15
deadline miss
12
15
Taskset non-schedulable with RM
1
2
0
9
18
6
12
0
18
3
3
6
12
9
15
15
1
2
Taskset schedulable with EDF
Task | T=D | C
 | 6 | 3
 | 9 | 4
Task | T=D | C
 | 6 | 3
 | 9 | 4

## Slide 52: Handling Tasks with D < T
Deadline monotonic (Fixed Priority):
  A task with smaller relative deadline gets higher priority
  Schedulability analysis: No utilization bound test; need to use Response Time Analysis (RTA)
Earliest Deadline First (Dynamic-Priority):
  A task with smaller absolute deadline gets higher priority
  Schedulability analysis: No utilization bound test; need to use Processor Demand Analysis (details omitted)
Notes: Schedulability analysis need to be changed (discussions omitted)

## Slide 53
Resource Synchronization Protocols
(for Fixed-Priority Scheduling)

## Slide 54: Resource Sharing
Some shared resources do not allow simultaneous accesses but require mutual exclusion. A piece of code executed under mutual exclusion constraints is called a critical section.
When two tasks access shared resource, semaphores are used to protect critical sections.
Each shared resource Ri must be protected by a semaphore Si, and each critical section (CS) using resource Ri must begin with wait(Si) and end with signal(Si)
A task waiting for an exclusive resource is said to be blocked on that resource. Otherwise, it proceeds by entering the critical section and holds the resource. When a task leaves a critical section, the associated resource becomes free.
Tasks blocked on the same resource are kept in a queue. When a running task invokes wait(Si) when Si is locked, it enters a waiting state, until another task invokes signal(Si) to unlock Si
globlal memory buffer
write
read
int x;
int y;
wait(s)
x = 3;
y = 5;
signal(s)
wait(s)
a = x+1;
b = y+2;
c = x+y;
signal(s)
Notes: Examples of common resources: data structures, variables, main memory area, file, set of registers, I/O unit, … . Examples of common resources: data structures, variables, main memory area, file, set of registers, I/O unit, … .
Many shared resources do not allow simultaneous accesses but require mutual exclusion (exclusive resources). A piece of code executed under mutual exclusion constraints is called a critical section.
A task waiting for an exclusive resource is said to be blocked on that resource. Otherwise, it proceeds by entering the critical section and holds the resource. When a task leaves a critical section, the associated resource becomes free.
Waiting state caused by resource constraints:

## Slide 55: Blocking Time
Lower-priority tasks can cause delay to higher-priority tasks due to blocking time
If higher priority task tries to lock a semaphore that is locked by lower priority task , blocks until unlocks the semaphore, and experiences a blocking delay .
  Since typical Critical Sections are very short, it seems this blocking time delay . Is bounded by the longest critical section in lower-priority tasks, hence acceptable?
No, blocking delay may be unbounded!
1
2
CS
1
2
CS

Notes: It seems that the maximum blocking time for 1 is equal to the length of the critical section of 2, but …

## Slide 56: Example Taskset
Utilization=5/50+250/500+1000/3000=0.93
WCRT (without blocking delays):
  RA=5, RB=280, RC=2500
Task | T | D | C | Prio
A | 50 | 10 | 5 | H
B | 500 | 500 | 250 | M
C | 3000 | 3000 | 1000 | L

## Slide 57: Priority Inversion
HP: High-Priority; MP: Medium-Priority; LP: Low-Priority
t: LP C locks s
t+∆: HP task A preempts LP task C
t+2: MP task B is invoked, but cannot start running due to HP task A running
t+3: HP task A tries to lock s, blocks since LP task C is holding s; MP task B starts running
t+253: MP task B finishes; LP task C starts running
t+254: LP task C unlocks s; HP last A starts running, but it already missed its deadline long ago!
Task | T | D | C | Prio
A | 50 | 10 | 5 | H
B | 500 | 500 | 250 | M
C | 3000 | 3000 | 1000 | L

## Slide 58: Priority Inversion and Priority Inheritance
Priority inversion happened
  High priority task (A) is blocked by low-priority task (B) for an unbounded interval of time.
    More than the longest critical section of B
In 1997, this bug caused the Mars pathfinder to freeze up occasionally without explanation, and then starts working again
Fixed by uploading a software patch enabling Priority-Inheritance Protocol (PIP)
  When a task locks a semaphore, it inherits the highest priority of all tasks blocked waiting for the semaphore
A task in a CS increases its priority if it blocks other higher priority tasks, by inheriting the highest priority among those tasks it blocks.

## Slide 59: With PIP
t: LP C locks s
t+∆: HP task A preempts LP task C
t+2: MP task B is invoked, but cannot start running due to HP task A running
t+3: HP task A tries to lock s, blocks since LP task C is holding s; C inherits A’s priority and starts running
  MP task B cannot start running, hence cannot cause unbounded blocking to HP task A
t+4: LP task C unlocks s, and returns to its regular Low priority; HP task A locks s and starts running
t+5: HP task A finishes and meets its deadline.
Task | T | D | C | Prio
A | 50 | 10 | 5 | H
B | 500 | 500 | 250 | M
C | 3000 | 3000 | 1000 | L

## Slide 60: PIP Properties
PIP does not prevent deadlocks. Classic deadlock scenario:
  LP task locks s1 at time t
  HP task starts running after t and locks s2, and tries to lock s1, blocked by
  inherits ’s priority and starts running
  tries to lock s2, but holds s2. Deadlocked!

## Slide 61: PIP Properties
Chained blocking:
  Theorem: task can be blocked at most once by each lower priority task
  If n is the number of tasks with priority less than , and m is the number of semaphores on which can be blocked, then
  Theorem: can be blocked at most for the duration of min(n, m) critical sections
Priority Ceiling Protocol is a more advanced protocol, which prevents deadlocks and reduces blocking time (discussions omitted)
B1 B2 B3
priority
1
2
3
4

## Slide 62: Schedulability Analysis
Schedulable utilization bound for RM scheduling with blocking time:
A taskset is schedulable under RM scheduling with blocking time if
priority level i utilization
Response Time Analysis (RTA) for RM scheduling with blocking time:
WCRT is computed by solving the following recursive equation:

## Slide 63
Preemptive vs. Non-Preemptive Scheduling

## Slide 64: Preemptive vs. Non-Preemptive Scheduling
Non-preemptive scheduling pros:
  It reduces runtime overhead
    Less context switches
    No mutex locks needed for critical sections
  It preserves program locality, improving the effectiveness of CPU cache
    As a result, task WCET becomes smaller and execution time distribution becomes more predictable (shown on right)
  Sometimes NP scheduling can improve schedulability
Cons:
  Reduced schedulability
  Scheduling anomalies
Preemptive scheduling pros:
  Better schedulability (higher CPU utilization)
Cons:
  Runtime overhead due to frequent context-switches
  Destroys program locality so task WCET becomes larger
Notes:   Pipeline mechanisms, Prefetch queues
  It reduces stack size, since no more than one task can be active, and tasks can share the same stack space

## Slide 65: Sometimes NP Scheduling Improves Schedulability
An example where NP scheduling improves schedulability (for fixed-priority scheduling)

## Slide 66: Disadvantage of NP Scheduling: Reduced Schedulability
In general, NP scheduling reduces schedulability. The utilization bound under NP scheduling drops to zero due to blocking time
An example with with two tasks T1 and T2, CPU utilization of nearly 0, yet non-schedulable.
  If (WCET of T2) (period of T1), then the taskset is non-schedulable with arbitrarily small system CPU utilization (when goes to 0 and goes to infinity)
  This example is valid whether or has higher priority: even if has higher priority, it may be released very shortly after is released at time 0, and it has to wait for to finish due to NP scheduling
T1
T2
Notes: Non preemption reduces schedulability (analysis must take blocking times into account); Non preemption reduces schedulability (analysis must take blocking times into account);
Schedulable utilization bound drops to zero.
  Here is an example with CPU utilization of nearly 0, yet non-schedulable.

## Slide 67: Disadvantage of NP Scheduling: Scheduling Anomalies
Scheduling anomaly: doubling the processor speed (reducing task execution times by half) makes task miss its deadline
Notes: I have given an overview of the basic concepts of real-time scheduling
Focus on static priority scheduling
Commercial tools from TimeSys and Tripac Software make it easier to do schedulability analysis
  However, it is good to know the internals of these tools

## Slide 68
Multiprocessor Scheduling

## Slide 69: Multiprocessor models
Identical multiprocessors:
  each processor has the same computing capacity
Uniform multiprocessors:
  different processors have different computing capacities
Heterogeneous multiprocessors:
  each (task, processor) pair may have a different computing capacity
MP scheduling
  Many NP-hard problems, with few optimal results, mainly heuristic approaches
  Only sufficient schedulability tests

## Slide 70: Multiprocessor Models
Identical multiprocessors: each processor has the same speed
P1
P2
P3
Task T1
Task T2
background – problem – results

## Slide 71: Multiprocessor Models
Uniform multiprocessors: different processors have different speeds
P1
P2
P3
Task T1
Task T2
x
x/2
x/3
y
y/2
y/3
background – problem – results
speed = 1
speed = 2
speed = 3

## Slide 72: Multiprocessor Models
background – problem – results
Heterogeneous multiprocessors: each (task, processor) pair may have a different relative speed, due to specialized processor architectures
x/2
x/3
x
CPU
DSP chip
Graphics co-processor
Graphics-intensive task:
Number-crunching task:
x/2
x/3
y
1.5 y
y
Task T1
Task T2

## Slide 73: Global vs partitioned scheduling
Global scheduling
  All ready jobs are kept in a common (global) queue; when selected for execution, a job can be dispatched to an arbitrary processor, even after being preempted
Partitioned scheduling
  Each task may only execute on a specific processor
CPU1
CPU2
CPU3
t1
t2
t3
t2
t1
t3
t4
t5
CPU1
CPU2
CPU3
t1
t2
t3
t1
t4
t5
t2
Global scheduling:
Single system-wide queue
Partitioned scheduling:
per-processor queues
Notes:   A task may execute on any processor
  A preempted job may resume on any processor
All ready tasks are kept in a common (global) queue
When selected for execution, a task can be dispatched to an arbitrary processor, even after being preempted
Single system-wide queue or multiple per-processor queues:

## Slide 74: Global Scheduling vs. Partitioned Scheduling
Global Scheduling
Advantages:
  Runtime load-balancing across cores
    More effective utilization of processors and overload management
  Supported by most multiprocessor operating systems
    Windows, Linux, MacOS...
Disadvantages:
  Low schedulable utilization
  Weak theoretical framework
Partitioned Scheduling
Advantages:
  Mature scheduling framework
  Uniprocessor scheduling theory scheduling are applicable on each core; uniprocessor resource access protocols (PIP, PCP…) can be used
  Partitioning of tasks can be done by efficient bin-packing algorithms
Disadvantages:
  No runtime load-balancing; surplus CPU time cannot be shared among processors
Notes:   Unused processor time can easily be reclaimed
  Easier re-scheduling (dynamic loads, selective shutdown, etc.)
  Number of preemptions
  Weak theoretical framework
  Migration cost: can be mitigated by proper HW (e.g., MPCore’s Direct Data Intervention)
  • Poor resource utilization for hard timing constraints
    – No more than 50% resource utilization can be guaranteed
  • Suffers from several scheduling anomalies
    – Sensitive to period adjustments
    Lower average response time

## Slide 75: Partitioned Scheduling
Scheduling problem reduces to:
Bin-packing
problem
Uniprocessor
scheduling
problem
+
NP-hard
Various heuristics algorithms
First Fit (FF)
Best Fit (BF)
Worst Fit (WF)
Next Fit (NF)
Well known
EDF
Utot ≤ 1
t2
t1
t3
t4
t5
RM
(RTA)
...
Notes: FF, NF, BF, FFDU, BFDD, etc.
in the
strong sense
Global (work-conserving) and partitioned approaches are incomparable
Two steps:
  1. Determine a mapping of tasks to processors
  2. Perform run-time scheduling
The Earliest Deadline First (EDF) scheduling algorithm
  - provably optimal (utilization bound = 1.0) on uniprocessors
Partitioned with EDF 
  Assign tasks to the processors, such that no processor’s capacity is exceeded
  Schedule each processor using EDF

## Slide 76: Partitioned Scheduling
Bin-packing algorithms:
  The problem concerns packing objects of varying sizes in boxes (”bins”) with some optimization objective, e.g., minimizing number of used boxes (best-fit), or minimizing the maximum workload for each box (worst-fit)
Application to multiprocessor scheduling:
  Bins are represented by processors and objects by tasks
  The decision whether a processor is ”full” or not is derived from a utilization-based feasibility test.
Since optimal bin-packing is a NP-complete problem, partitioned scheduling is also NP-complete
Example: Rate-Monotonic-First-Fit (RMFF): (Dhall and Liu, 1978)
  Let the processors be indexed as 1, 2, …
  Assign the tasks to processor in the order of increasing periods (that is, RM order)
  For each task , choose the lowest previously-used processor j such that , together with all tasks that have already been assigned to processor j, can be feasibly scheduled according to the utilization-based schedulability test
  Additional processors are added if needed
Notes: Complexity of schedulability analysis for partitioned scheduling: (Leung & Whitehead, 1982)
  The problem of deciding whether a task set is schedulable on m processors with respect to partitioned scheduling is NP-complete
Consequence:
  There cannot be any pseudo-polynomial time algorithm for finding an optimal partition of a set of tasks unless P = NP.
Assumptions:
  Independent, periodic tasks
  Preemptive, uniprocessor scheduling (RM)

## Slide 77: Assumptions for Global Scheduling
Identical multiprocessors
Work-conserving:
  At each instant, the highest-priority jobs that are eligible to execute are selected for execution upon the available processors
  No processor is ever idle when the ready queue is non-empty
Preemption and Migration support
  For global schedulers, a preempted task can resume its execution on a different processor with 0 overhead
  Cost of preemption/migration integrated into task WCET
No job-level parallelism
  the same job cannot be simultaneously executed on more than one processor
Notes: The m highest priority ready jobs are always executing on m processors
Work-conserving scheduler
  No processor is ever idle when the ready queue is non-empty
  Independent tasks
  The independence assumtion can be later removed, considering blocking times and shared resource protocols.
  a processor is never left idle while an active job exists
Task execution is assumed to be ”greedy”:
  If higher-priority tasks occupy all processors, a lower-priority task cannot grab a processor until the execution of a higher priority task is complete.
Task execution is assumed to be ”greedy”:
  If higher-priority tasks occupy all processors, a lower-priority task cannot grab a processor until the execution of a higher priority task is complete.

## Slide 78: Source of Difficulty
The “no job-level parallelism” assumption leads to difficult scheduling problems
“The simple fact that a task can use only one processor even when several processors are free at the same time adds a surprising amount of difficulty to the scheduling of multiple processors” [Liu’69]
CPU1
CPU2
CPU3
Notes: The ”root of all evil” in global scheduling: (Liu, 1969)
  Few of the results obtained for a single processor generalize directly to the multiple processor case; bringing in additional processors adds a new dimension to the scheduling problem. The simple fact that a task can use only one processor even when several processors are free at the same time adds a surprising amount of difficulty to the scheduling of multiple processors.

## Slide 79: Global scheduling example
CPU1
CPU2
CPU3
Global queue
(ordered according to a given policy)
t1
t2
t3
The first m jobs in the queue are scheduled upon the m CPUs
t2
t1
t3
t4
t5
Notes: There is a global queue in which ready tasks ready are placed, according to a certain policy. When there is a free CPU the first task is removed from the queue and is scheduled. When a new task arrives with priority higher than one of the executing tasks, it preempts the executing task with lowest priority. If a task on a different CPU finishes its execution, the preempted task can “migrate” to the free CPU and continue its execution.

## Slide 80: Global scheduling example
t3
CPU1
CPU2
CPU3
t1
t2
When a job finishes its execution, the next job in the queue is scheduled on the available CPU
t2
t1
t3
t4
t5
t2
t1
t3
t4
t5
t4
Global queue
(ordered according to a given policy)

## Slide 81: Global scheduling example
CPU1
CPU2
CPU3
t1
t2
When a new higher priority job arrives, it preempts the job with lowest priority among the executing ones
t2
t1
t3
t4
t5
t4
t3
t2
t1
t3
t4
t5
t3
t3
Global queue
(ordered according to a given policy)

## Slide 82: Global scheduling example
CPU1
CPU2
CPU3
t1
t2
When another job finishes its execution, the preempted job can resume its execution. Net effect: “migrated” from
CPU3 to CPU1
t2
t1
t3
t4
t5
t4
t3
t3
t4
t3
t4
t2
t5
t3
t4
Global queue
(ordered according to a given policy)

## Slide 83: Global vs. Partitioned
Global (work-conserving) and partitioned scheduling algorithms are incomparable:
  There are tasksets that are schedulable with a global scheduler, but not with a partitioned scheduler, and vice versa.

## Slide 84: Global vs Partitioned (FP) Scheduling
A taskset schedulable with global scheduling, but not partitioned scheduling
Global FP scheduling is feasible with priority assignment p1>p2>p3 (or p2>p1>p3)
Partitioned scheduling is not feasible, since assigning any two tasks to the same processor will cause the utilization to exceed 1.
A feasible execution trace
under global scheduling
Task | T=D | C | Prio
T1 | 2 | 1 | H
T2 | 3 | 2 | M
T3 | 3 | 2 | L
Notes: Not feasible for partitioned scheduling, since any two tasks’ combined utilization will exceed 1.
Three tasks T1(1,2); T2(2,3); T3(2,3) with notation: (WCET, period)

## Slide 85: Global vs Partitioned (FP) Scheduling
A taskset schedulable with partitioned scheduling, but not global scheduling
Tasks T1, T3 assigned to Processor 1; T2, T4 assigned to Processor 2
Partitioned FP scheduling with RM priority assignment (p1>p2>p3>p4) is feasible. Both processors have utilization 1.0, and harmonic task periods
A feasible execution trace
under partitioned scheduling
A feasible execution trace
under partitioned scheduling
Global FP scheduling with RM priority assignment p1>p2>p3>p4
Compare to partitioned scheduling: the difference is at time 7, when global FP scheduling must run T3, which has higher priority than T4; this causes Processor 1 to be idle in time intervals [10,12] and [22,24], since only one task T4 can be run
Task | T=D | C | Prio
T1 | 6 | 4 | 4(H)
T2 | 12 | 7 | 3
T3 | 12 | 4 | 2
T4 | 24 | 10 | 1(L)
Idle
Idle
Notes: Not feasible for partitioned scheduling, since any two tasks’ combined utilization will exceed 1.
Partitioned scheduling is feasible
  Four tasks t1=(4,6); t2=(7,12); t3=(4,12); t4=(10,24)

## Slide 86: Difficulties of Global Scheduling
Dhall’s effect
  With RM, DM and EDF, some low-utilization task sets can be unschedulable regardless of how many processors are used.
Scheduling anomalies
  Decreasing task execution time or increasing task period may cause deadline misses
Dependence on relative priority ordering (omitted)
  Changing the relative priority ordering among higher-priority tasks may affect schedulability for a lower-priority task.
Hard-to-find critical instant (omitted)
  A critical instant does not always occur when a task arrives at the same time as all its higher-priority tasks.
Notes: A critical instant does not always occur when a task arrives at the same time as all its higher-priority tasks.

## Slide 87: Dhall’s effect
Global RM/DM/EDF can fail at very low utilization
Example: m processors, n=m+1 tasks. Tasks are light tasks, with small , ; Task is a heavy task, with large , ;
For global RM/DM/EDF, Task has lowest priority, so must run on m processors starting at time 0, causing to miss its deadline
One solution: assign higher priority to tasks with higher utilization
T
Deadline
Miss
m light tasks
1 heavy task
Utot1
Notes: A critical instant does not always occur when a task arrives at the same time as all its higher-priority tasks.

## Slide 88: MP Scheduling Anomalies
Decrease in processor demand (decreasing task execution time or increasing task period) may cause deadline misses!
Anomaly 1
  Decrease in processor demand from higher-priority tasks can increase the interference on a lower-priority task because of change in the time when the tasks execute
Anomaly 2
  Decrease in processor demand of a task negatively affects the task itself because change in the task arrival times cause it to suffer more interference
Notes: EDF does not suffer from execution-time anomalies, but does suffer from period anomalies.

## Slide 89: Anomaly 1

## Slide 90: Anomaly 1

## Slide 91: Anomaly 2

## Slide 92: Anomaly 2
Another example where the critical instant for task c does not occur at time 0 when it arrives at the same time as all its higher-priority tasks.
c
20
b
a
c
23
C’s deadline
missed here