## Slide 1: CSC 112: Computer Operating Systems Lecture 3 Synchronization
Department of Computer Science,
Hofstra University
Acknowledgement: Lecture slides based on UC Berkeley CS 162: Operating Systems and System Programming
And NTNU course on Operating Systems

## Slide 2: Concurrency I
Consider two concurrent threads T0, T1, which access a shared variable x that has been initialized to 0. There is no mutex protection.
Q1: What are the minimum, maximum, and all possible values of x after the two threads have completed execution?
Q2: Suppose we protect statement ‘x = x+2’ in Thread B within a critical section using a mutex lock. What are all the minimum, maximum, and all possible final values of x?
//Thread T0
for (int i=0; i<5; i++) {
x = x + 1;
}
//Thread T0
for (int j=0; j<5; j++) {
x = x + 2;
}
int x = 0;
Notes: for (i=0; i

## Slide 3: Concurrency II
Consider three concurrent threads T1, T2, T3, which access a shared variable D that has been initialized to 100. There is no mutex protection. What are the minimum and maximum possible values of D after the three threads have completed execution?
ANS:
//Initialization
int D=100;
//Thread T1
void main(){
D=D+20;
}
//Thread T2
void main(){
D=D-50;
}
//Thread T3
void main(){
D=D+10;
}

## Slide 4: Recall: Locks: Loads/Stores
This implementation does not ensure mutual exclusion, since both threads may grab the lock:
After Thread 1 reads flag==0 and exits the while loop, it is preempted/interrupted by Thread 2, which also reads flag==0 and exits the while loop. Then both threads set flag=1 and enter the critical section.
Root cause: Lock is not an atomic operation!
flag = 0
Notes: Another problem: performance overhead!

## Slide 5: Mutual Exclusion I
Does it achieve one of more of the correctness properties of a concurrent program:
  Mutual exclusion: Only one thread in critical section at a time
  Progress (deadlock-free): If several simultaneous requests, must allow one to proceed
  Bounded waiting (starvation-free): Must eventually allow each waiting thread to enter
Does it need the TestAndSet() instruction for atomic execution like the previous slide “Locks: Loads/Stores”?
What is its major flaw?
ANS:
//Thread T0
while (true) {
while (S0 == S1);
//Critical section
S0 = S1;
}
//Thread T1
while (true) {
while (S0 != S1);
//Critical section
S1 = !S0;
}
Boolean S0, S1;
S0=false, S1=false;
Notes: Consider the methods used by threads T1 and T2 for accessing their critical sections whenever needed, as given below. (These are the only methods for accessing the critical section, and T1 and T2 each runs a separate higher-level program that uses these methods which is not shown.) The initial values of S1 and S2 are arbitrary.
Which of the following is true?
(a) Mutual exclusion but not progress
(b) Progress but not mutual exclusion
(c) Neither mutual exclusion nor progress
ANS:
acd

## Slide 6: Mutual Exclusion II
Does it achieve one of more of the correctness properties of a concurrent program:
  Mutual exclusion: Only one thread in critical section at a time
  Progress (deadlock-free): If several simultaneous requests, must allow one to proceed
  Bounded waiting (starvation-free): Must eventually allow each waiting thread to enter
ANS:
//Thread T0
while (true) {
flag[0] = true;
while (flag[1]==true);
/* Critical Section */
flag[0] = false;
}
//Thread T1
while (true) {
flag[1] = true;
while (flag[0]==true);
/* Critical Section */
flag[1] = false;
}
Boolean flag[2];
flag[0]=false, flag[1]=false;
Notes: Boolean flag[2] = {false, false};
// Thread T0
while (true) {
flag[0] = true;
while (flag[1] == true);
/* Critical Section */
flag[0] = false;
}
// Thread T1
while (true) {
flag[1] = true;
while (flag[0] == true);
/* Critical Section */
flag[1] = false;
}

## Slide 7: Mutual Exclusion III (Peterson’s Solution)
//Thread T0
while (true) {
flag[0] = true;
turn = 1;
while (flag[1]==true && turn==1);
/* Critical Section */
flag[0] = false;
}
Boolean flag[2];
flag[0]=false, flag[1]=false;
int turn = 0;
//Thread T1
while (true) {
flag[1] = true;
turn = 0;
while (flag[0]==true && turn==0);
/* Critical Section */
flag[1] = false;
}
Does it achieve one of more of the correctness properties of a concurrent program:
  Mutual exclusion: Only one thread in critical section at a time
  Progress (deadlock-free): If several simultaneous requests, must allow one to proceed
  Bounded waiting (starvation-free): Must eventually allow each waiting thread to enter
ANS:
Notes: int i=0, j=1;

## Slide 8: Mutual Exclusion III (Peterson’s Solution Variation)
//Thread T0
while (true) {
flag[0] = true;
turn = 0;
while (flag[1]==true && turn==1);
/* Critical Section */
flag[0] = false;
}
Boolean flag[2];
flag[0]=false, flag[1]=false;
int turn = 0;
//Thread T1
while (true) {
flag[1] = true;
turn = 1;
while (flag[0]==true && turn==0);
/* Critical Section */
flag[1] = false;
}
Does it achieve one of more of the correctness properties of a concurrent program:
  Mutual exclusion: Only one thread in critical section at a time
  Progress (deadlock-free): If several simultaneous requests, must allow one to proceed
  Bounded waiting (starvation-free): Must eventually allow each waiting thread to enter
ANS:
Notes: int i=0, j=1;

## Slide 9: Race Conditions
Consider the two threads each executing t1 and t2. Values of shared variables y and z are initialized to 0
Q. Give all possible final values for x and the corresponding order of execution of instructions in t1 and t2.
1) t1 runs to the end first; then t2 runs to the end: x = 0+0 = 0
2) t2 to line 2; then t1 to the end; then t2 to the end: x = 1+0 = 1
3) t2 to the end; then t1 to the end: x = 1+2 = 3
Are there other possibilities giving additional values?
1 t1(){ |  |  | 1 | t2(){ | 
2 | int x; |  | 2 |  | y = 1;
3 | x = y + z; |  | 3 |  | z = 2;
4 } |  |  | 4 | } | 
int y=0, z=0;
9

## Slide 10: Race Conditions
Addition operation x=y+z consist of multiple machine instructions in assembly language:
  fetch operand y into register r1
  fetch operand z into register r2
  add r1 + r2, store result in r3
  store r3 in memory location of x
If a task switch to t2 occurs between machine instructions A and B; then t2 runs to completion before switching back to t1, then:
y is read as 0 (t2 didn’t set y yet)
z is read as 2 (t2 sets z before execution instruction B of add. in t1)
the sum is then x = 0 + 2 = 2
1 t1(){ |  |  | 1 | t2(){ | 
2 | int x; |  | 2 |  | y = 1;
3 | x = y + z; |  | 3 |  | z = 2;
4 } |  |  | 4 | } | 
int y=0, z=0;
10

## Slide 11: Race Conditions
Q. Give a solution using semaphores.
Solution: we protect the addition x = y + z within a critical section, using a binary semaphore (mutex). This code guarantees that x can never have the value 1 or 2, possible values are x = 0, 3
(Line “int x” can be outside or inside the critical section with no difference. We use a slightly different notation of s.wait()/s.signal() to denote sem_wait(&s) and sem_post(&s).
1 t1() { |  | 1 t2() {
2 | int x; | 2 s.wait();
3 | s.wait(); | 3 y = 1;
4 | x = y + z; | 4 z = 2;
5 | s.signal(); | 5 s.signal();
6 } |  | 6 }
11
int y=0, z=0;
semaphore s = 1;

## Slide 12: Semaphores I
Q. Use semaphores and insert wait/signal calls into the two threads so that only “wordle” is printed.
1 int t1() { |  | t2: | 1 int t2() { | 
2 | printf("w"); |  | 2 | printf("o");
3 | printf("d"); |  | 3 | printf("r");
4 } |  |  | 4 | printf("l");
 |  |  | 5 6 } | printf("e");
t1:
t1 has to run first to print "w", so s1 should be initialized to 1.
t2 has to wait until the "w" has been printed by t1, then it is woken up by t1 calling s2.signal(), so s2 should be initialized to 0.
1 int t1(){
s1.wait();
printf("w");
s2.signal();
s1.wait();
printf("d");
s2.signal();
2
3
4
5
6
7
8 }
1 int t2(){
s2.wait();
printf("o");
printf("r");
s1.signal();
s2.wait();
printf("l");
printf("e");
2
3
4
5
6
7
8
9 }
12
semaphore s1=1, s2=0
Notes:   It is signalled by t1, so the initial value of s2 has to be 0.

## Slide 13: Semaphores II
The following three functions of a program f1(), f2(), f3() run in separate threads each and print some prime numbers. All three threads are ready to run at the same time. Use synchronization using the semaphores S1, S2 and S3 and wait/signal operations on the semaphores to ensure that the program outputs the prime numbers in increasing order (2, 3, 5, 7, 11, 13).
Semaphore S1=0;
Semaphore S2=0;
Semaphore S3=0; f1() {
printf("3");
printf("5");
}
f2() {
printf("2");
printf("13");
}
f3() {
printf(“7");
printf("11");
}
Notes: Insert appropriate wait or signal operations in the code lines indicated with // SYNC and give the correct initial values for the semaphores. Give the completed functions and the initial values for the semaphores.
Hint: Note that it might not be required to add a wait or signal operations in all of the places indicated.

## Slide 14: Semaphores II Solution
Solution 1 (left): With initial values of all semaphores = 0, only f2 can run, prints 2, signals S1 and then waits for S2. S1.signal() starts f1, which was waiting for S1 and can now print 3 and 5 and then signal S3. S3.signal() now starts f3, which prints 7 and 11 and signals S2. This returns execution to f2, which can then finally print 13.
Solution 2(right): s2 has initial value 1, so f2 calls S2.wait() and runs first. The rest of the same as Solution 1. You can see that initializing s2=0 has the same effect as initializing s2=1 and let f2 call S2.wait() first. So Solution 1 is better with one less call to wait().
semaphore S1=0;
semaphore S2=1;
semaphore S3=0;
f1() {
S1.wait();
printf("3");
printf("5");
S3.signal();
}
f2() {
S2.wait();
printf("2");
S1.signal();
S2.wait();
printf("13");
}
f3() {
S3.wait();
printf("7");
printf("11");
S2.signal();
}
semaphore S1=0;
semaphore S2=0;
semaphore S3=0;
f1() {
S1.wait();
printf("3");
printf("5");
S3.signal();
}
f2() {
printf("2");
S1.signal();
S2.wait();
printf("13");
}
f3() {
S3.wait();
printf("7");
printf("11");
S2.signal();
}
Notes: Insert appropriate wait or signal operations in the code lines indicated with // SYNC and give the correct initial values for the semaphores. Give the completed functions and the initial values for the semaphores.
Hint: Note that it might not be required to add a wait or signal operations in all of the places indicated.

## Slide 15: Semaphores III
Q. Which strings can be output when running the 3 threads in parallel?
Either t1 or t2 could start first, so the first letter can be A or B
Then both t1 and t2 signal s_c, only after both have signalled s_c, t3 can start and print C
t3 signals s_a and s_b, which start in arbitrary order again
Accordingly, the output is a regular expression ((AB|BA)C)+
  Print A or B in arbitrary order, then print C, then the process repeats
int t1() {
while(1) {
printf("A");
s_c.signal();
s_a.wait();
6 }
7 }
int t2() {
while(1) {
printf("B");
s_c.signal();
s_b.wait();
6 }
7 }
int t3() {
while(1) {
s_c.wait();
s_c.wait();
printf("C");
s_a.signal();
s_b.signal();
8 }
9 }
semaphore s_a=0, s_b=0, s_c=0;
15
Notes: Here, we have used a regular expression to indicate the structure of a text pattern. Regular expressions (short: regexps) are a common tool in Unix

## Slide 16: Deadlocks I
Deadlock scenario 1:
t2 runs first until line 2 (so lock2=0, lock1=1); switch to t1
t1 starts and runs until line 3 (so lock1=0, lock2=0); back to t2
t2 waits for lock2 in line 4; switch to t1, waits for lock1 in line 5
This results in a circular waiting condition, where each thread grabs one lock and requests the other.
1 int t1() {
2 z = z + 2;
lock1.wait();
x = x + 2;
lock2.wait();
lock1.signal();
y = y + 2;
lock2.signal();
9 }
1 int t2() {
lock2.wait();
2
3
y = y + 1; lock1.wait(); x = x + 1;
lock1.signal(); lock2.signal(); z = z + 1;
4
5
6
7
8
9 }
16
//Initialization
int x=0, y=0, z=0; semaphore lock1=1, lock2=1;
z = z + 2; lock1.wait(); x = x + 2;
lock2.wait(); lock1.signal(); y = y + 2; lock2.signal();
2
3
4
5
6
7
8
9 }
//Initialization
int x=0, y=0, z=0; semaphore lock1=1, lock2=1;
1 int t1() { 1 int t2() {
lock2.wait();
y = y + 1; lock1.wait(); x = x + 1;
lock1.signal(); lock2.signal(); z = z + 1;
2
3
4
5
6
7
8
9 }
Deadlock scenario 2:
t1 runs first until line 4 (so lock1=0, lock2=1); switch to t2
t2 starts and runs until line 3 (so lock1=0, lock2=0); back to t1
t1 waits for lock2 in line 5; switch to t2, waits for lock1 in line 4
(Other interleavings are possible, e.g., t1 grabs lock1, t2 grabs lock2 requests lock 1, t1 requests lock 2)
To prevent deadlocks, every thread should acquire locks in the same order, e.g. both acquire lock1 before lock2, or both acquire lock2 before lock1
Notes: Are there other execution orders leading to a deadlock?
You can remove all other statements and only leave the lock wait() instructions and get into this deadlock.)

## Slide 17: Deadlocks II
Q. What are the possible values of x, y and z in the deadlock state?
t1 runs until Line 5 lock2.wait() and t2 runs until Line 4 lock1.wait(), so x = 2, y = 1, z = 2
Q. What are the possible values of x, y and z if the program finishes successfully without a deadlock?
t1 runs first to the end, then t2 (or vice versa): x=3, y=3, z=3
In t1, lock1.signal() sets lock1=1, lock2.signal() sets lock2=1, this exiting the critical sections protected by lock1 and lock2.
Since Line 2 of t1 “z=z+2”, and Line 8 of t2 “z=z+1” are not protected within a critical section, a thread switch may occur in the middle of each line, e.g.,
  t2 Line 8 reads z=0; before z is written back; switch to t1 Line 2, run t1 to the end; switch to t2 Line 8, write back z=0+1=1.
  Or, t1 Line 2 reads z=0; before z is written back; switch to t2 Line 2, run t2 to the end; switch to t1 Line 2, write back z=0+2=2.
1 int t1() { |  |  | 1 | int t2() { | 
2 | z = z + 2; |  | 2 |  | lock2.wait();
3 | lock1.wait(); |  | 3 |  | y = y + 1;
4 | x = x + 2; |  | 4 |  | lock1.wait();
5 | lock2.wait(); |  | 5 |  | x = x + 1;
6 | lock1.signal(); |  | 6 |  | lock1.signal();
7 | y = y + 2; |  | 7 |  | lock2.signal();
8 | lock2.signal(); |  | 8 |  | z = z + 1;
9 } |  |  | 9 | } | 
int x=0, y=0, z=0; semaphore lock1=1, lock2=1;
17
Notes: Semaphores -> locks + condition variables
  Binary semaphores -> locks
  Semaphore for ordering
Semaphore for P/C